|  | United Nations | ECE/TRANS/WP.29/2012/6 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 20 December 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

156th session

Geneva, 13–16 March 2012

Item 4.8.2 of the provisional agenda

# Regulation No. 117 ( Tyre – Rolling resistance, 
rolling noise and wet grip)

Proposal for Supplement 1 to the 02 series of amendments to Regulation No. 117 (Tyres - Rolling resistance, rolling noise and wet grip)

Submitted by the Working Party on Noise *

The text reproduced below was adopted by the Working Party on Noise (GRB) at its fifty-fourth session to propose an alternative to improve the accuracy of the deceleration method. It is based on ECE/TRANS/WP.29/GRB/2011/11 as reproduced by Annex III to the report (ECE/TRANS/WP.29/GRB/52, para. 12). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and the Administrative Committee (AC.1) for consideration.

Annex 6

Paragraph 3.5., amend to read:

"3.5.	Duration and speed.

When the deceleration method is selected, the following requirements apply:

(a)	The deceleration j shall be determined in exact dω/dt or approximate Δω/Δt form, where ω is angular velocity, t – time;

(b)	For duration Δt, the time increments shall not exceed 0.5 s;

(c)	Any variation of the test drum speed shall not exceed 1 km/h within one time increment."

Paragraph 4.6.2., amend to read:

"4.6.2.	Deceleration method

The deceleration method follows the procedure below:

(a)	Remove the tyre from the test surface;

(b)	Record the deceleration of the test drum ((Do/ (t and that of the unloaded tyre ((T0/ (t3 or record the deceleration of the test drum jD0 and that of the unloaded tyre jT0 in exact or approximate form in accordance with paragraph 3.5."

Paragraph 5.1.5., amend to read:

"5.1.5.	Deceleration method

Calculate the parasitic losses Fpl, in newton.

| Where: |
| --- |
| ID |  | is the test drum inertia in rotation, in kilogram meter squared, |
| R |  | is the test drum surface radius, in meter, |
| (D0 |  | is the test drum angular speed, without tyre, in radians per second, |
| (t0 |  | is the time increment chosen for the measurement of the parasitic losses without tyre, in second, |
| IT |  | is the spindle, tyre and wheel inertia in rotation, in kilogram meter squared, |
| R |  | is the tyre rolling radius, in metre, |
| (T0 |  | is the tyre angular speed, unloaded tyre, in radian per second. |

or

| Where: |  |  |
| --- | --- | --- |
| ID |  | is the test drum inertia in rotation, in kilogram meter squared, |
| R |  | is the test drum surface radius, in meter, |
| jD0 |  | is the deceleration of the test drum, without tyre, in radians per second squared, |
| IT |  | is the spindle, tyre and wheel inertia in rotation, in kilogram meter squared, |
| Rr |  | is the tyre rolling radius, in metre, |
| jT0 |  | is the deceleration of unloaded tyre, in radians per second squared." |

Paragraph 5.2.5., amend to read:

"5.2.5.	Deceleration method

The rolling resistance Fr, in newton, is calculated using the equation:

| Where: |  |  |
| --- | --- | --- |
| ID |  | is the test drum inertia in rotation, in kilogram metre squared, |
| R |  | is the test drum surface radius, in meter, |
| Fpl |  | represents the parasitic losses as calculated in paragraph 5.1.5., |
| (tv |  | is the time increment chosen for measurement, in second, |
| Δ(v |  | is the test drum angular speed increment, without tyre, in radian per second, |
| IT |  | is the spindle, tyre and wheel inertia in rotation, in kilogram metre squared, |
| Rr |  | is the tyre rolling radius, in metre, |
| Fr |  | is the rolling resistance, in newton. |

or

| Where: |  |  |
| --- | --- | --- |
| ID |  | is the test drum inertia in rotation, in kilogram metre squared, |
| R |  | is the test drum surface radius, in meter, |
| Fpl |  | represents the parasitic losses as calculated in paragraph 5.1.5., |
| jV |  | is the deceleration of the test drum, in radians per second squared, |
| IT |  | is the spindle, tyre and wheel inertia in rotation, in kilogram metre squared, |
| Rr |  | is the tyre rolling radius, in metre, |
| Fr |  | is the rolling resistance, in newton." |

Annex 6, Appendix 1

Paragraph 4, amend to read:

"4.	Control accuracy

…

(d)	time: +/- 0.5 ms

…"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.