## Slide 1
Summary of Activities
up to Now
March 16, 2012
20th ITS Informal Group Meeting
K. Hiramatsu and M. Sekine
NTSEL: National Traffic Safety and Environmental Laboratory
<number>
Document No. ITS-20-04
(20th ITS, 16 March 2012, agenda item 3)

## Slide 2
Past Activities :
TOR : November 2004
  To develop common understanding of driver assistance systems
Report of Two Years Activities : March 2007
  Appropriateness of "Driver in the Loop" under normal driving condition
  Effectiveness of damage mitigation under pre-crash condition where collision is no longer avoidable
Proposal of Warning Guidelines to WP29 : March 2010
<number>

## Slide 3
  How does ADAS assist driver ? :
<number>
Level 0
Level 1
Level 2
Level 3
recognition
judgment
operation
recognition
judgment
operation
recognition
judgment
operation
recognition
judgment
operation
Assistance by Advanced Technologies
Behavioral Model of a Driver
Conventional driving
Information
Warning
Control

## Slide 4
<number>
<number>
Report of two years activities :
Information :
  To keep monitoring the situation of self-commitment basis guidelines, ESoP, AAM and JAMA, in each region for a time being
Warning :
  To develop high-priority warning guidelines in cooperation with IHRA-ITS WG
Control :
  To have baseline ideas for effective use of control systems in ADAS

## Slide 5
Warning Guidelines :
Purpose : to provide basic recommendations for the design of high-priority warnings on ADAS
  Better understanding from drivers
  Reduced confusion
  More accurate and consistent expectations
High-priority warning : to be delivered at critical situation where the driver is required to take immediate action or decision to avoid crash event
Adoption : at 154th session of WP29, June, 2011
<number>

## Slide 6
<number>
Warning guidelines :
– ECE/TRANS/WP.29/2011/90 –
High-priority warning should be noticeable in the driving environment.
High-priority warning should be distinguishable from other messages in the vehicle.
High-priority warning should provide spatial cues to the hazard location.
High-priority warning should inform the driver of proximity of the hazard.
High-priority warning should elicit timely response or decisions.
Multiple warnings should be prioritized.
False/nuisance warnings rate should be low.
System status and degraded performance of high-priority warnings should be displayed.
Notes: Notice
Recognize: what is happening?
From where does it come?
How much is it close to my vehicle?
Elicit warning timely
If others, warnings should be prioritized
False/nuisance should be minimized
Degradation of performance should be displayed

## Slide 7
Conventional
Driving
Driver only
Assistance
Driving
Driver + System
Substitute
Driving
System only
Level of Driver Assistance
<number>
Manual
Automation
Driver’s role : partial operator to supervisor

## Slide 8
  Systems should be designed in which driver is always held responsible for his/her driving. For this purpose followings are effective.
    Installation of auditory or visual announcement devices providing information on the system functioning
  Control systems activated under normal driving condition should be designed based on “Driving in the loop”, where driver should be involved in driving in a way or other. For this purpose followings are effective.
    Announcement is made when the driving initiative is transferred from system to driver.
    Driver is kept involved in driving operation. For example, starting initiative should not be given to system.
    System allows switching on or off by driver
    System allows overriding by driver
  As for Control systems to reduce collision speed activated under pre-crash condition where collision is no longer avoidable, there is no time for necessity of overriding and driver is not very likely to depend on system.
Report on Control Systems in WP29/ITS Informal Group(2007):
<number>

## Slide 9
Background：
  Rapid technology evolution in ADAS makes the driver handling easier and more comfortable.
  Roles of driver assistance systems varies dependent upon system configurations.
  Such advanced systems should not be hindered by the reason of different rules among the regions.
Aim：
  Baseline ideas on driver-system interaction are needed for proper development of advanced systems .
  The first draft was submitted at the last meeting of ITS Informal Group, and revised several times.
<number>
Control Principles
- Background and Aim -

## Slide 10
Activities：
  Submission of the first draft from IHRA-ITS WG in November, 2010
  Presentation at 19th ITS Informal Group Meeting in March, 2011
  Comments from OICA, JAMA and others
  Revision and circulation to relevant quarters in February, 2012
Next step(provisional)：
  Introduction of revised control principles : ITS Informal Group Meeting in March, 2012
  Presentation to WP29 in 2012
  Examination among related GRs in 2012-2013
<number>
Control Principles
- Activities up to Now -

## Slide 11
Thank you for your attention
<number>