## Slide 1
Holistic approach
for
rolling noise mitigation
GRB 56th
Sep 3 – 5, 2012
Informal document GRB-56-14
(56th GRB, 3-5 September 2012,
agenda item 9)
Transmitted by the expert from the ETRTO

## Slide 2
Content
Introduction
Basic functions of the tyre
Pavement and tyre interaction
Contributions to noise reduction
Road noise mitigation requires global approach
Views/recommendations further work

## Slide 3
Road Pavement Potential
Tyre influence compared to road and speed
Road and speed can be controlled locally where annoyance is shown through
noise mapping (EU Dir 2002/49 in EUROPE)
Different roads with the same tyres measured in 7.5 m
8-10 dB(A)
Vehicle speed from 80 to 50 km/h
5-9 dB(A)
Tyre of same size and category
2-3 dB(A)

## Slide 4
Safety
- Braking (dry & wet)
- Aquaplaning
Economy
- Mileage Performance
- Fuel Consumption
Comfort
- Mechanical comfort
- Acoustical comfort
Handling
- Tyre characteristics
- High Speed
Tyre Basics – Contribution to vehicle properties
Environment
- C02 emissions
- Rolling Noise nuisance

Notes: <number>

## Slide 5
To what extent can tyre manufacturers, road manufacturers, and road owners act independently, or should they join their efforts to make progress on:
What are the interactions between tyre and road to produce
the road / tyre / vehicle performances?
Emissions: ROLLING RESISTANCE
Safety: WET GRIP
Pollution: NOISE

## Slide 6
Noise mechanisms for tyre/road noise
rotation
horn effect
horn effect
macro roughness
beat of
tread blocks
airpumping
Stick-slip
mega roughness
surface vibrations
road texture impact
groove resonance
snap out of tread blocks
Notes: <number>

## Slide 7
Tyre excitation
Asphalt accord. ISO 10844
SMA 0/8
SMA 0/11
Source: Meßdaten: Pullwitt, BASt, BMBF-Projekt Leiser Verkehr, 2003
Pressure in the foot print on different road surfaces
Depending on the roughness and the waviness of the road surface the tread pattern of the tyre or the road surface texture is predominating. An effective decrease of rolling noise without measures on road making is not possible.
Notes: <number>
Unsaubere Arbeit,
schlechtes Geräuschergebnis.
Bei Tage nicht zu sehen.

## Slide 8
Close proximity measurements: CPX
The use of Standard Reference Test tyres allows to classify road pavement for rolling noise emissions on a normative basis.
Trailer Types CPX
Müller BBM GmbH
DAGA 2010

## Slide 9
13 dB
Between the noisiest tyre on the noisiest road surface (Tyre 16 on SMA 0/16) and the quietest tyre on the quietest road surface (Tyre 12 on Rollpave PERS), there is a noise difference of approximately 17 dB at both 50 and 80 km/h. Even between tyre 16 on the SMA 0/16 and tyre 12 on a more commonly used surface as the double layer PAC (section 16), there is a difference of 14-15 dB.
Variation of the tyre/road noise on different surfaces
AVERAGE LAcpx (dB) at 80 km:h for 22 Tyres
Truls Berge, Noise measurements of passenger car tyres at the Kloosterzande test track, 2011

## Slide 10
Road noise mitigation requires - global approach
Tyre/road noise in real life is generated on a wide range of different road surfaces.
The approach for efficient societal benefit for rolling sound emissions has to be considered on a global basis where the main actors are the pavement, the tyre & the vehicle.
Traffic flow management & driver behaviour need to be included in this global approach.

## Slide 11
View on further works to be performed
AIPCR WORLD CONGRESS –MEXICO 2011- S/C 2A-WG ROAD NOISE MITIGATION
Need for regulations, harmonized procedures or policies for low noise pavements and other noise reducing measures; in particular, harmonised procedures for classification, check of conformity of production of road surfaces.
Many solutions for noise reduction have been developed. Further noise reducing measures are needed for:
  improving the mix design of the pavement
  promoting the next generation for low noise surfaces
  promoting low noise dense surfaces for urban areas
  optimization of low noise concrete pavements, both technical and subjective (acceptability by the population)
  sharing knowledge and experience

## Slide 12
Thank you