## Slide 1: Japanese proposal on R51 limit values
JASIC
<number>
Informal document GRB-56-05
(56th GRB, 3-5 September 2012,
agenda item 3(b))

## Slide 2
<number>
Basic concept of Japanese proposal on limit values with sub-categories
At GRB 55, based on the Monitoring database (856 vehicles) and the Japanese database (184 vehicles), Japan proposed limit values for R51-03 with sub-categories as Inf. Doc. GRB-55-01. In consideration of Inf. Doc. GRB-54-03, proposed by the expert from Germany, Japan has reviewed the original proposal and changed subcategories, limit values and tolerances slightly, which are described in WP.29/GRB/2012/7 and Inf. Doc. GRB-56-01.
Basic concepts of the revised proposal are as follows;
Stage 1 limit values are chosen from around 10% cut-off levels of the frequency distributions of Monitoring+ Japanese database. Owing to the introduction of the new test method with Stage 1 limit values and ASEP, the reduction of the road traffic noise is expected.

## Slide 3
<number>
Stage 2 limit values are chosen from about 30% or more cut-off levels of the frequency distributions of Monitoring+ Japanese database in order to reduce the road traffic noise further.
The application date of Stage 1 should be 2 years after the entry into force of R51-03, while the application dates of Stage 2 should be basically 4 years after Stage 1 for Non-heavy duty vehicles (M1, M2(GVW≤3.5t) and N1) except Small Low Power trucks, and 6 years after Stage 1 for heavy duty vehicles (M2(3.5t<GVW), M3, N2 and N3). As the development cycle of Small Low Power trucks is similar to Heavy duty vehicles, the application date of Stage 2 of Small Low Power trucks is 6 years after Stage 1.

## Slide 4
“3 stage” approach is very ambitious but has clear message for enforcing the vehicle noise level. Because of the uncertainty of noise reduction technology advance and other regulations that might influence on noise reduction measures (ex. CO2 and pollutant emission regulation) , Japan proposes the temporary limit values and entry-into-force dates of Stage 3, which shall be reviewed and fixed until the entry-into-force date of Stage 2. The limit values are reviewed to be about 70% or more cut-off level, which might be more practical.
<number>

## Slide 5
<number>
 |  | Stage 1 | Stage 2 |  | Stage 33 | 
 |  | 2 years after entry into force of ECE R51.03 | 4 years after stage 1 | 6 years after stage 1 | [4] years after stage 2 | [6] years after stage 2
M1 | PMR ≤ 120 kW/t | 72 | 70 | - | [68] | -
 | 120 < PMR ≤ 160 kW/t | 73 | - | 71 | [70] | -
 | PMR > 160 kW/t | 75 | 73 | - | [72] | -
M2 | GVW ≤ 2.5 ton | 72 | 70 | - | [69] | -
 | 2.5 ton < GVW ≤ 3.5 ton | 74 | 72 | - | [71] | -
 | 3.5 ton < GVW | 75 | - | 73 | - | [71]
M3 | P ≤ 135 kW | 76 | - | 74 | - | [73]
 | 135 < P ≤ 250 kW | 79 | - | 78 | - | [76]
 | P > 250 kW | 80 | - | 78 | - | [76]
N1 | GVW ≤ 2.5 ton and PMR(GVW)1 ≤ 35kW/t | 74 | - | 72 | - | [70]
 | GVW ≤ 2.5 ton and 35kW/t < PMR(GVW)1 | 72 | 70 | - | [68] | -
 | 2.5 ton < GVW ≤ 3.5 ton | 74 | 72 | - | [71] | -
N2 | P ≤ 135 kW | 77 | - | 76 | - | [73]
 | P > 135 kW | 78 | - | 77 | - | [75]
N3 | P ≤ 250 kW | 80 | - | 78 | - | [76]
 | P > 250 kW | 82 | - | 802 | - | [78]
1 “PMR(GVW)” means PMR calculated by using the maximum authorized vehicle mass. 2 Entry-into-force date of N3 with an engine power exceeding 250 kW for stage 2 is 8 years after stage 1. 3 Limit values and entry-into-force dates of “Stage 3” shall be reviewed and fixed until the entry-into-force date of “Stage 2”. |  |  |  |  |  | 
Proposal on new limit values
Unit: dB(A)

## Slide 6
Changes from GRB-55-01 (original Japanese proposal)
1) Subcategories
Thresholds of small M3 and N2 is changed from 125 kW to 135 kW. Germany proposed 180kW for small M3 and 150 kW for N2 but the change of 135 kW seems to have little influence according to Monitoring database.
A subcategory for small M2 (GVW≤ 2.5t) is added based on German proposal. The limit values are also based on German proposal.
2) Limit Values
For stage1
  N2 : The limit value for N2 not exceeding 135 kW is reinforced to 77 dB(A) while the limit value for N2 exceeding 135 kW is reinforced to 78 dB(A) in reference to German proposal.
  N3: The limit value for N3 exceeding 250 kW is changed to 82 dB(A), in consideration of the difficulty of the noise reduction in this subcategory. (1/4 of data exceed 81 dB(A) in Monitoring and Japanese database)
<number>

## Slide 7
<number>
2) Limit Values (Cont.)
For Stage 2
  M1: The limit value for M1 with between 120 and 160 kW/t PMR is remained but the transition period is changed to 6 years after Stage 1. Two year extension is required for the correspondence to the change of the maximum acceleration (3.0 m/s2 instead of 2.0 m/s2)
  N3: The limit value for N3 exceeding 250 kW is changed to 80 dB(A) with 8-year transition period, in consideration of the difficulty of the noise reduction in this subcategory. (3/4 of data exceed 79 dB(A) in Monitoring and Japanese database)
For stage 3, in consideration of GRB-54-03, the limit values are reviewed and set as more practical levels

## Slide 8
Table of Limit values proposed by GRB-55-01 (Japan), GRB-54-03 (Germany)
and WP.29/GRB/2012/07 & GRB-56-01 (Japan)
※ +2 years for the entry-into-force
<number>

## Slide 9
3) Tolerance
Tolerance for off-road vehicles are changed to the German proposal. The determination of wading depth is quoted from WP29/GRB/2005/5.
Tolerance for M3 with PI engine is added owing to the threshold change to 135kW from 125kW. The rated engine speed of PI engine (ex. 4400 rpm) is higher than CI engine (ex.3400 rpm) and the noise level of PI engine is higher than CI engine consequently. The actual use engine speed of PI M3 is not so high as 0.85 to 0.89 S. Therefore the tolerance of M3 with PI engine is set only for the stage 1 with the condition that the test condition for M3 with PI engines should be reviewed until the entry into force of Stage 2.
<number>

## Slide 10
Analysis of the proposed limit values
Using Monitoring and Japanese database, the proposed limit values and subcategories are analyzed as the following slides.
In Japan, M2 buses are N1 derivatives or M3 derivatives (downsizing) and Japanese database doesn’t include M2 data. Therefore, the analysis of M2 is not conducted.
<number>

## Slide 11
<number>
Lurban Distribution of M1 category
72dB
(Stage 1)
70dB
(Stage 2)
68dB
(Stage 3)
75dB (Stage 1)
73dB (Stage 2)
72dB (Stage 3)
73dB
(Stage 1)
71dB (Stage 2)
70dB (Stage 3)
Analysis of M1

## Slide 12
Lurban Distribution of N1 category
74dB (Stage 1)
72dB (Stage 1)
74dB (Stage 1)
72dB (Stage 2)
70dB (Stage 2)
72dB (Stage 2)
2.5t < GVW
GVW ≤ 2.5t
Sound level for Small Low Power N1 is different from Light N1
<number>
70dB (Stage 3)
68dB (Stage 3)
70dB (Stage 3)
Analysis of N1

## Slide 13
In order to reduce noise level of Small Low Power trucks by 2-3 dB,
an engine and a transmission have to be covered.
Noise measures of Small Low Power trucks
E/G・T/M cover
(under body)
For keeping a space between an engine and covers, the gap between the ground and the under cover will be smaller than the present gap.
E/G・T/M cover
(under body)
▼It is difficult to reduce the gap because of the usage condition especially for agricultural fields.
⇒No space for noise cover
<number>

## Slide 14
<number>
From GRB-55-5Rev1 (informal document from China)

## Slide 15
77dB (Stage 1)
76dB (Stage 2)
Lurban Distribution of N2 category
<number>
75dB (Stage 3)
78dB (Stage 1)
77dB (Stage 2)
73dB (Stage 3)
125 to 135 kW N2 should be included in the smaller group
Analysis of N2

## Slide 16
80dB (Stage 1)
82dB (Stage 1)
78dB (Stage 2)
80dB (Stage 2)
Lurban Distribution of N3 category
<number>
76dB (Stage 3)
78dB (Stage 3)
Analysis of N3

## Slide 17
Lurban Distribution of M3 category
76dB (Stage 1)
74dB (Stage 2)
Positive Ignition (PI) M3s (whose rated speeds are over 4,000 rpm)
<number>
80dB
(Stage 1)
78dB
(Stage 2)
76dB
(Stage 3)
79dB
(Stage 1)
78dB
(Stage 2)
76dB
(Stage 3)
73dB (Stage 3)
125 to 135 kW N2 should be included in the smaller group
Analysis of M3

## Slide 18: Difference between PI and CI engines in M3
Difference between PI and CI engines are due to the difference of engine rotating speeds.
 | PI | CI
Engine Type | TB45E | ZD30DDTi
Cylinder layout | Linear 6 | Linear 4
Cylinder Capacity | 4.478 L | 2.953 L
Rated Power kW（PS）/rpm | 127(173) /4400 | 110（150） /3400
Transmission | 5MT | 5MT
Driving type | 2WD | 2WD
GVW | 5315 kg | 5405k g
Passenger | 29名 | 29名
Max engine speed in R51 test | 3880rpm | 3000rpm
Noise level（ｄBA） | 78.0 | 73.4
CI engine
rated speed
PI engine
rated speed
CI engine M3
PI engine M3
<number>
Engine Speed [rpm]
Noise level [dB]

## Slide 19
(Reference) Database
<number>
 |  | Japanese + Monitoring |  | 
 |  |  | Japanese | Monitoring
M1 | PMR≤120kW/t | 575 | 52 | 523
 | 120<PMR≤160kW/t | 60 | 5 | 55
 | 160kW/t<PMR | 23 | 0 | 23
 | M1G | 28 | 4 | 24
M2 | GVW≤3.5t | - | - | -
 | 3.5t<GVW | - | - | -
M3 | P≤125kW | 2 | 1 | 1
 | 125<P≤250kW | 53 | 15 | 38
 | 250kW<P | 18 | 2 | 16
N1 | GVW≤2.5t & PMR≤35kW/t | 14 | 14 | -
 | GVW≤2.5t & 35kW/t<PMR | 25 | 7 | 18
 | 2.5t<GVW | 51 | 10 | 41
N2 | P≤125kW | 41 | 14 | 27
 | 125kW<P | 38 | 24 | 14
N3 | P≤250kW | 35 | 12 | 23
 | 250kW<P | 77 | 24 | 53
Total |  | 1040 | 184 | 856

## Slide 20
<number>
Conclusion
Japan proposes limit values and subcategories for R51-03 based on EU and Japanese database.
“3 Stage” approach is practical as well as ambitious. Flexibility of “Stage 3” limit values leads the whole environmental benefit, including noise, CO2 and pollutant emissions.
This proposal could be the basis of the common position for stakeholders.