|  | United Nations | ECE/TRANS/WP.29/GRE/2013/14 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 25 January 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-ninth session

Geneva, 8–11 April 2013

Item 5(j) of the provisional agenda

Collective amendments - Regulations Nos. 6, 7 and 48

Proposal for [Supplement 12 to the 04 series of amendments, Supplement 5 to the 05 series of amendments,] Supplement 3 to the 06 series of amendments to Regulations No. 48 (Installation of lighting and light-signalling devices)

Submitted by the experts from France and Germany*

The text reproduced below was prepared by the experts from France and Germany to implement direction indicator lamps with spatial variation of the intensity into UN Regulation No. 48. The modifications to the existing text of the Regulation are marked in bold for new or strikethrough for deleted characters.

I.		Proposal

Insert a new paragraph 2.10.1., to read:

"2.10.1.	Horizontal orientation of a direction indicator means the ratio of the length of path of the movement in horizontal direction to that in vertical direction on the apparent surface should not exceed the value of [10:6]."

Insert a new paragraph 5.9.3., to read:

"5.9.3. 	The photometric characteristics of direction indicator lamps of the categories 1, 1a, 1b, 2a or 2b may change the luminous intensity during a flash inside the maximum apparent surface and if it is noted in the communication form of the direction indicator lamp (Regulation No. 6).

In this case:

(a)	the variation propagates in a horizontal orientation outwards only, until all light sources of the lamp are switched on;

(b)	the variation shall not exceed [200] ms;

(c)	once lit light source shall remain lit until all light sources of the lamp shall be switched off simultaneously at the end of the flash.

The variation [of direction indicator lamps of the categories 2a or 2b] is prohibited if the [hazard warning or] emergency stop signal is activated."

Paragraph 6.5.8., amend to read:

"6.5.8.		Tell-tale Operating ….

If it is entirely … to paragraph 6.2.2. 6.4.2. of Regulation No. 6 or another suitable way13…."

II.	Justification

1.	The proposal to propagate the flashing of the direction indicator light in the direction of turning can improve safety and avoid misinterpretation.

2.	The on time of a flash of the turning signal durates has a max of  500 ms and starts with the rise time followed by a period of max. intensity of the flash. The duration of the variation is equivalent to the rise time and limited to [200] ms. Anyway it shall not be longer than the heating of tungsten filament.

3.	The proposal is clearly linked to UN Regulation No. 6 which is necessary with regard to the handling of the Regulation and the application to after marked products.

4.	The requirements should allow only solution with a focus on safety and avoid distractive design.

5.	A misleading reference in paragraph 6.5.8. regarding UN Regulation No. 6 was corrected.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, program activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate