|  | United Nations | ECE/TRANS/WP.29/GRE/2013/38 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 25 January 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-ninth session

Geneva, 8-11 April 2013

Item 5(j) of the provisional agenda

Collective amendments - Regulations Nos. 6, 7 and 48

Proposal for supplement 23 to the 02 series of amendments to Regulation No. 7 (front and rear position (side) lamps stop-lamps and end-outline marker lamp)

Submitted by the expert from Poland*

The text reproduced below was prepared by the expert from Poland (see informal document GRE-68-29). The modifications to the existing text of the UN Regulation are marked in bold for new or strikethrough for deleted characters.

- Proposal

Add new paragraph 5.8., to read:

"5.8.	To obtain type approval according this Regulation is required possibility to install lamp in question at least on one type of vehicle according requirements of Regulation No 48."

- Justification

1.	Regulation No 7 does not contain requirements regarding the change of luminance of the lamps. It is possible to obtain a type approval for a lamp which cannot be mounted on a vehicle according Regulation No. 48. But such lamps could be used as aftermarket parts and could be installed on used vehicles. This proposal is intended as a protection against such situations.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.