| Submitted by the expert from France | Informal Document GRE-67-08 (67th GRE, 26-29 March 2012, agenda item 4(a)) |
| --- | --- |

Proposal for Supplement 10 of the 04 Series of amendments – Regulation No. 48 (Installation of Lighting and Light-signalling Devices)

Paragraph 6.6.8, amend to read as follows:

    - Tell-tale

Circuit-closed tell-tale mandatory. Flashing warning light and/or , which can operate in conjunction with the tell-tale(s) specified in paragraph 6.5.8., that otherwise operate independently, flashing simultaneously as hazard warning tell-tale.

JUSTIFICATION

The proposal is intended to align ECE 48 (Installation of Lighting and Light-signalling devices) with ECE 121 (Location and Identification of hand controls, tell-tales and indicators) and to eliminate inconsistencies between these two Regulations.

Currently, we have in ECE 121:

# Table 1

# Symbols, their illumination and colours.

[....]

| No. | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | Item | Symbol 2 | Function | Illumination | Colour |

| 5. | Direction indicator | 1, 3 | Control | No |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Tell-tale | Yes | Green |

| 6. | Hazard warning signal |  | Control | Yes |  |
| --- | --- | --- | --- | --- | --- |
|  |  | 1 | Tell-tale 4 | Yes | Red |

1		Framed areas of the symbol may be solid. (no impact with this proposal)

3		The pair of arrows is a single symbol.  When the controls or tell-tales for left and right turn operate independently, however, the two arrows may be considered separate symbols and be spaced accordingly.

4 	Not required when arrows of turn signal tell-tales that otherwise operate independently flash simultaneously as hazard warning tell-tale.

This proposal does not change the technical substance of the requirements.