## Slide 1: Comments on GRE/2012/27(Lighting & Signalling WG)
Headlamp Initial Aiming
October 2012
Informal document GRE-68-20
(68th GRE, 15-18 October 2012,
agenda item 4(b))
Notes: <number>

## Slide 2
GRE/2012/27 proposes changes to ECE R48 to improve the minimum range of visibility, and to replace the artificial 2000lm limit for automatic levelling with more appropriate glare control.
Notes: <number>

## Slide 3
Proposed changes:
  To redefine the initial aim and static load-levelling requirements of dip beam cut-off in terms of theoretical range on the road rather than the current % downward inclination.
  To reduce aiming tolerance, and delete the additional aiming tolerance in CoP, aligning it with the approval requirement.
  To add a requirement to measure glare values in loaded conditions as part of both Type Approval and CoP, if the resultant aim falls outside permitted tolerance.
  To delete the reference to 2000lm as a threshold for automatic levelling.
  To add a visible warning to the driver, defining what is the minimum visibility distance, if theoretical range is less than 50m.
Notes: <number>

## Slide 4
Proposed Initial nominal aim to correspond to 75m theoretical range
Specified % inclination is ( Headlamp height / 75 ) as a %, rounded to nearest 0.1%.
Notes: <number>

## Slide 5
Currently: initial aim is specified by the manufacturer, within permitted limits dependent on lamp height. Height bands overlap for tolerance.
Proposed Initial nominal aim to correspond to 75m theoretical range
min height | max height | %down
500 | 1000 | 1.0% to 1.5%
800 | 1200 | 1.5% to 2.0%
Notes: <number>

## Slide 6
Under proposal,
  No overlap between height bands
  Most headlamps would be aimed higher than at present
  Risks increased glare.
Proposed Initial nominal aim to correspond to 75m theoretical range
  <sports car
  < normal family car
  < van/SUV
Notes: <number>

## Slide 7
Theoretical Range vs. real visibility
  Is Theoretical Range a good measure of real visibility range?:
  CIE TC4-45 generated a way to measure visibility range: it is significantly more complicated than simply the cut-off intersection, but correlates well with human perception.
  The following examples are taken from the CIE TC4-45 report
    Two similar R98 headlamps, with similar mounting heights (715mm, 717mm)
    Both are aimed at 1.0% down. This is the same value of aim that would apply under the proposal for these headlamp heights.
    Ranges are calculated according to TC4-45 method.
Notes: <number>

## Slide 8
Glare intensities plotted on screen located at 50m from Car
Illuminance values plotted on screen at 25m (0,0 is the Headlamp Optical Axis)
Illuminance values plotted on road surface
75m
60m
forward Visibility
Low gradient through the cutoff = less glare sensitivity to initial aiming tolerances
Notes: <number>

## Slide 9
Glare intensities plotted on screen located at 50m from Car
Illuminance values plotted on screen at 25m (0,0 is the Headlamp Optical Axis)
Illuminance values plotted on road surface
75m
85m
forward Visibility
High gradient through the cutoff = more glare sensitivity to initial aiming tolerances
Notes: <number>

## Slide 10
Theoretical Range vs. real visibility
  Both lamps have a theoretical range of 75m
    Sample 11 has TC4-45 visibility range of 60m
    Sample 5 has TC4-45 visibility range of 85m
  Conclusion: theoretical range is a poor measure of real-world visibility
Notes: <number>

## Slide 11
Currently total load levelling tolerance is 2.0% approval, 2.6% CoP
Manufacturer may define initial aim to optimise levelling results
Tolerance with load levelling to be 50m to 100m theoretical range (6.2.6.1.2) for both approval and CoP
Notes: <number>

## Slide 12
Proposal is shown expressed as %.
  Initial aim is defined by regulation
  Highest permitted aim with levelling unchanged at -0.5%
  Corresponds to a reduction in load levelling tolerance for most cars of 60-75%
Tolerance with load levelling to be 50m to 100m theoretical range (6.2.6.1.2) for both approval and CoP
Notes: <number>

## Slide 13
Tolerance with load levelling
To consistently meet CoP requirements, initial aim and levelling system need to be repeatable with a standard deviation of better than 0.1%. Repeatability of suspension system alone is not this good.
Example for 650mm high passenger car headlamp
Notes: <number>

## Slide 14
6.2.6.1.3 requires that if, under loading conditions of Annex 5, aim falls above the 100m range, glare must be measured
  This is assessing the glare with the headlamp aimed as it would be under Annex 5 load conditions. Measurement to take place during headlamp type approval.
    But at time of headlamp Type Approval, R48 inspection has not taken place, so the aim of the headlamp under Annex 5 conditions is not known.
Notes: <number>

## Slide 15
Deletion of 2000lm requirement
  Current regulation para 6.2.9 prohibits the use of para 6.2.2.2 manual levelling option with LED or >2000lm light sources
  Proposal deletes this prohibition
    Provided that 50-100m theoretical range can be achieved by manual levelling, manual levelling would be permissible for any headlamp.
  GTB working group is currently reviewing visibility and glare: it would be better to await their outcome.
Notes: <number>

## Slide 16
Warning message
  If theoretical range under Annex 5 loading conditions falls below 50m but above 25m, a warning notice is to be placed in the car, declaring the minimum theoretical range as a minimum ”visibility distance”
      Visibility distance does not correlate directly with theoretical range (see above).
Notes: <number>

## Slide 17
GRE/2012/21 proposed changes to ECE R48 (1 of 3):
  To redefine the initial aim and static load-levelling requirements of dip beam headlamps in terms of theoretical range on the road rather than the current % downward inclination.
  Conclusion:
    Redefining the aim point will raise the aim for most passenger cars This may not give the desired visibility range
    To prevent this causing increased glare, aiming and levelling tolerances must be tightened
      Industry needs aiming and levelling capability data to identify if this tolerance tightening is practicable.
Notes: <number>

## Slide 18
Thank You
Notes: <number>