## Slide 1
Poland: comments on OICA comments on GRE/2012/27
Headlamp Initial Aiming and leveling tolerances influence for road illumination distance
68 GRE, 17 October 2012
Informal document GRE-68-31
(68th GRE, 16-18 October 2012,
agenda item 4(d))
Notes: <number>

## Slide 2
GRE/2012/27 proposes changes to ECE R48 to improve the minimum range of visibility, and to replace the artificial 2000lm limit for automatic levelling with more appropriate glare control.
Road illumination distance understand as cut-off crossing with road surface – clear and simple definition in line with present Reg. 112, 98, 123 and aiming practice
Notes: <number>

## Slide 3
Proposed changes:
  To redefine the initial aim and static load-levelling requirements of dip beam cut-off in terms of theoretical range on the road rather than the current % downward inclination.
  How is „practical” range guaranteed by present ECE Regulations or by manufactures?
  Do drivers know it ?
  To reduce aiming tolerance, and delete the additional aiming tolerance in CoP, aligning it with the approval requirement.
  To add a requirement to measure glare values in loaded conditions as part of both Type Approval and CoP, if the resultant aim falls outside permitted tolerance.
  Glare is restricted and controlled by headlamp Regulations (112, 98, 123).
  Till now it is no any reference on vehicle to this defined glare values. According to present requirements of Reg. 48 “on vehicle” glare can differ from regulated in 112, 98 and 123 in uncontrolled manner. It should be clarified how much more glare is accepted and how to ensure it.
  Artificial 2000 lm borderline does not work.
Notes: <number>

## Slide 4
Proposed changes:
  To delete the reference to 2000lm as a threshold for automatic levelling.
  Presently are the same restrictions for manual and automatic levelling ( 2%-2.5%) but practice for automatic levelling is diverse.
  To add a visible warning to the driver, defining what is the minimum visibility distance, if theoretical range is less than 50m.
  „Road illumination distance”
Notes: <number>

## Slide 5
Proposed Initial nominal aim to correspond to 75m theoretical range
Specified % inclination is ( Headlamp height / 75 ) as a %, rounded to nearest 0.1%.
Notes: <number>

## Slide 6
Currently: initial aim is specified by the manufacturer, within permitted limits dependent on lamp height. Height bands overlap for tolerance.
Proposed Initial nominal aim to correspond to 75m theoretical range
min height | max height | %down
500 | 1000 | 1.0% to 1.5%
800 | 1200 | 1.5% to 2.0%
Notes: <number>

## Slide 7
Under proposal, What for are needed overlaps?
  No overlap between height bands
  Most headlamps would be aimed higher than at present
  It will depend on manufacturers decision
  and choice of range of amended Reg.48
  (30 to100m or 50 to 100m)
  It will be safety oriented advantage and goal of amendment because of longer average road illumination distance.
  Risks increased glare.
  Not true. Decreased glare
  comparing present state.
Proposed Initial nominal aim to correspond to 75m theoretical range
Notes: <number>

## Slide 8
Proposed Initial nominal aim to correspond to 75m theoretical range
  <sports car
  < normal family car
  < van/SUV
  Is it any reference in Reg. 48 to sports car, normal family car, van/SUV?
  Should be introduced?
  Why?
Notes: <number>

## Slide 9
Theoretical Range vs. real visibility
  Is Theoretical Range a good measure of real visibility range?:
  CIE TC4-45 generated a way to measure visibility range: it is significantly more complicated than simply the cut-off intersection, but correlates well with human perception.
  The following examples are taken from the CIE TC4-45 report
    Two similar R98 headlamps, with similar mounting heights (715mm, 717mm)
    Both are aimed at 1.0% down. This is the same value of aim that would apply under the proposal for these headlamp heights.
    Ranges are calculated according to TC4-45 method.
Notes: <number>

## Slide 10
Glare intensities plotted on screen located at 50m from Car
Illuminance values plotted on screen at 25m (0,0 is the Headlamp Optical Axis)
Illuminance values plotted on road surface
75m
60m
forward Visibility
Low gradient through the cutoff = less glare sensitivity to initial aiming tolerances
Notes: <number>

## Slide 11
Glare intensities plotted on screen located at 50m from Car
Illuminance values plotted on screen at 25m (0,0 is the Headlamp Optical Axis)
Illuminance values plotted on road surface
75m
85m
forward Visibility
High gradient through the cutoff = more glare sensitivity to initial aiming tolerances
Notes: <number>

## Slide 12
Theoretical Range vs. real visibility
  Both lamps have a theoretical range of 75m
    Sample 11 has TC4-45 visibility range of 60m
    Sample 5 has TC4-45 visibility range of 85m
  Conclusion: theoretical range is a poor measure of real-world visibility
Notes: <number>

## Slide 13
Theoretical Range vs. real visibility
  Conclusion: theoretical range is a poor measure of real-world visibility
  To objectively assess aiming/leveling results of GRE/2012/27 appropriate are calculations for lowest allowed leveling according present requirements 2.5% down aiming. How big will be differences between both headlamps and where will be 3lx position on left side?
  Have in mind inverted square law. 1% aiming is inappropriate for this situation.
  By 2.5% aiming results should be very closed to 28 m
  In GRE/2012/27 is proposed : ”It is also possible on the same way to declare a longer than minimum required road illumination distance according applicant knowledge”
  Could be modified „It is also possible on the same way to declare a longer or shorter than minimum required road illumination distance according applicant knowledge”
Notes: <number>

## Slide 14
Currently total load levelling tolerance is 2.0% approval, 2.6% CoP
Manufacturer may define initial aim to optimise levelling results
Tolerance with load levelling to be 50m to 100m theoretical range (6.2.6.1.2) for both approval and CoP
Notes: <number>

## Slide 15
Proposal is shown expressed as %.
  Initial aim is defined by regulation
  Highest permitted aim with levelling unchanged at -0.5%
  Corresponds to a reduction in load levelling tolerance for most cars of 60-75%
Tolerance with load levelling to be 50m to 100m theoretical range (6.2.6.1.2) for both approval and CoP
It is alternative in GRE/2012/27:
„The crossing distance could be lower but not less than [25 m or 30m] under the condition that there will be information for driver
It should be carefully verified. But... What is the problem?
Manufacturers convenience (because not technical possibility)
or ...
SAFETY OF MILIONS DRIVERS AND PEDESTRIANS
Notes: <number>

## Slide 16
Tolerance with load levelling
To consistently meet CoP requirements, initial aim and levelling system need to be repeatable with a standard deviation of better than 0.1%. Repeatability of suspension system alone is not this good.
Example for 650mm high passenger car headlamp
Notes: <number>

## Slide 17
Tolerance with load levelling
To consistently meet CoP requirements, initial aim and levelling system need to be repeatable with a standard deviation of better than 0.1%. Repeatability of suspension system alone is not this good.
Example for 650mm high passenger car headlamp
Repeatability (tested in Motor Transport Institute including performance of suspension) for automatic leveling for many cars was much better than 0.1%
For same (van/SUV/delivery
trucks) tolerances are bigger
For some cars (sport cars)
are lower
Notes: <number>

## Slide 18
6.2.6.1.3 requires that if, under loading conditions of Annex 5, aim falls above the 100m range, glare must be measured
  This is assessing the glare with the headlamp aimed as it would be under Annex 5 load conditions. Measurement to take place during headlamp type approval.
    But at time of headlamp Type Approval, R48 inspection has not taken place, so the aim of the headlamp under Annex 5 conditions is not known.
At time of headlamp Type Approval, could be very easy measured and additionally reported:
- what are the highest possible aiming/ mounting height values
Notes: <number>

## Slide 19
Deletion of 2000lm requirement
Current regulation para 6.2.9 prohibits the use of para 6.2.2.2 manual levelling option with LED or >2000lm light sources
  Proposal deletes this prohibition
    Provided that 50-100m theoretical range can be achieved by manual levelling, manual levelling would be permissible for any headlamp.
  GTB working group is currently reviewing visibility and glare: it would be better to await their outcome.
  GTB working group reviewed GLARE ONLY (Klettwitz tests) in respect to obligatory automatic leveling.
  Results are as was easy to theoretically predict: significant influence of pitch angle. No significant influence of light source flux.
  No visibility range research were done till now.
  It is easy to predict that cut-off position at 20m before vehicle (or less for CoP reasons) cannot guarantee visibility for speed of 100 km/h
Notes: <number>

## Slide 20
Warning message
  If theoretical range under Annex 5 loading conditions falls below 50m but above 25m, a warning notice is to be placed in the car, declaring the minimum theoretical range as a minimum ”visibility distance”
      Visibility distance does not correlate directly with theoretical range (see above).
  For short distances correlates very well
  Please verify before reporting
Notes: <number>

## Slide 21
GRE/2012/21 proposed changes to ECE R48 (1 of 3):
  To redefine the initial aim and static load-levelling requirements of dip beam headlamps in terms of theoretical range on the road rather than the current % downward inclination.
  Conclusion:
    Redefining the aim point will raise the aim for most passenger cars This may not give the desired visibility range
    To prevent this causing increased glare, aiming and levelling tolerances must be tightened
      Industry needs aiming and levelling capability data to identify if this tolerance tightening is practicable.
Notes: <number>

## Slide 22
  Conclusion:
    Redefining the aim point will raise the aim for most passenger cars This may not give the desired visibility range
    Not proved. Illegitimate statement.
    To prevent this causing increased glare, aiming and leveling tolerances must be tightened
      Industry needs aiming and levelling capability data to identify if this tolerance tightening is practicable.
      It is not a problem to identify.
      It is possible esy measure values for vehicles offered on market.
      It is simple and it was done.
Notes: <number>

## Slide 23
THANK YOU FOR YOUR ATTENTION
Notes: <number>