## Slide 1: AEGPL amendments proposals to Regulations n. 83 and 115 Bi-fuel vehicles – New definition and provisions
GFV - Brussels, 15th December 2011

## Slide 2
Objectives
The proposed amendments are aimed at redefining the class of bi-fuel vehicles to permit the simultaneous use of gas and petrol, even if limited in amount or duration.
These modifications are needed primarily for the approval of some bi-fuel vehicle equipped with petrol direct injection systems and retrofit systems intended to be fitted on vehicles equipped with petrol direct injection systems: in order to safeguard the petrol injectors, a certain amount of petrol may need to be injected also in gas mode, especially when particular temperature conditions are reached.
To this end, are introduced:
  modifications to bi-fuel vehicles definitions;
  new requirements to set a minimum limit to gas energy ratio (used as inverse index of petrol use);
  a method to calculate the gas energy ratio;

## Slide 3
Bi-fuel vehicles
Definition and new requirements
Definition
Main elements:
  two separate fuel storage systems
  designed to run on only one fuel at a time.
  the simultaneous use of both fuels is limited in amount or duration (new)
New requirements
Combined application of the following restrictions:
  60 seconds max limit applied to petrol warm-up period;
  Gas energy ratio higher than 80% as calculated over the entire driving cycle;
Note: the choice of a min gas limit instead of a max petrol limit is motivated by the fact that petrol consumption is very low and, furthermore, this would be difficult to be measured with simple instruments.

## Slide 4: Emissions
No need to adapt measurement methods and correction factors for calculation of NOx and CO emissions as they are “essentially” fuel-independent (error on corrected concentration due to different DF’s is negligible and conservative)
THC emission calculation are “more” fuel-dependent due to the different density of the pollutants, but the assumption that only LPG is burned during the cycle (as it stands now – warm-up on petrol) is a conservative condition.

## Slide 5: Emissions THC calculation
EXAMPLE
Data
Ambient conditions:
ambient temperature: 23 °C = 297.2 K,
barometric pressure: PB = 101.33 kPa,
relative humidity: Ra = 60 per cent,
saturation vapour pressure: Pd = 2.81 kPa of H2O at 23 °C.
Volume measured and reduced to standard conditions (para. 1.)
V = 51.961 m3
Analyser readings:
Diluted exhaust sample (Ce) Dilution-air sample (Cd)
HC (1) 92 ppm 3.0 ppm
CO 470 ppm 0 ppm
NOx 70 ppm 0 ppm
CO2 1.6 per cent by volume 0.03 per cent by volume
(1) in ppm carbon equivalent

## Slide 6: Emissions THC calculation
Given that:
DF = for petrol
DF = for LPG
DF = for NG for CNG
DF’s differs in percentage terms by the following:
ΔDF% (LPG – Petrol) = -11.2%
ΔDF% (CNG – Petrol) = -29.1%
Calculating for all fuels the corrected concentration of HC in the sampling bag:
Ci = Ce - Cd
Ci = 89.371 for petrol
Ci = 89.418 for LPG
Ci = 89.558 for CNG
so, in percentage terms, the differences, in relation to petrol, are:
ΔCi % (LPG-petrol) = +0.053%
ΔCi % (CNG-petrol) = +0.209%
Percentage error is positive but negligible

## Slide 7: Emissions THC calculation
Given that:
MHC = Ci *Vmix*QHC
Differences in DF’s do not weigh significantly in final calculation.
QHC’s are, instead, influential:
QHC = 0.631 for petrol
QHC = 0.649 for LPG
QHC = 0.714 for NG
In conclusion, considering the cycle fully driven on gas, the mass emissions per km will be higher with respect to the limit case (20%petrol, 80%gas):
ΔMHC%(LPG-limit)= + 0,57%
ΔMHC%(CNG-limit)= + 2,42%

## Slide 8: Energy gas ratio - Calculation method
Measurement of gas mass consumed during the cycle:
fuel weighing system measuring the weight of the LPG storage container during the test:
  accuracy of ± 2 per cent of the difference between the readings at the beginning and at the end of the test or better
  careful installation of the device according to the instrument manufacturers’ recommendations and to good engineering practice to avoid measurement errors;
other measurement methods are permitted if an equivalent accuracy can be demonstrated;
Note: with particular reference to mass flow metering, the reliability of such type of instrument – on gas - seems not proven yet in transient conditions and, furthermore, its positioning and installation, in a bench test, might raise some problems, likely affecting reproducibility of the measurement method
Notes: <number>

## Slide 9: Energy gas ratio - Calculation method
Formula demonstration
Ggas = Egas/Etot (1) where: Egas= mgas* Hgas (2)
  Etot is the total energy required for type 1 test (MJ)
  Egas is the amount of energy supplied by gas fuel (MJ)
  mgas is the mass of gas burned during the type 1 test (kg) which supplies Egas
  Hgas is the specific heating value of gas (MJ/kg).
The total energy used during the type I test can be derived from fuel consumption data, assuming that only gas is burned during the test:
Etot= mtot* Hgas (3)
  mtot is the total mass of gas derived from fuel consumption data (kg)
  Hgas is the specific heating value of gas (MJ/kg).

## Slide 10: Energy gas ratio - Calculation method
The total mass (expressed in kg) can be derived from the mean fuel consumption of R101 (expressed in l/100km) by the following equation:
mtot= FC*d*dist/100 (4)
  FC is the fuel consumption calculated according to Annex 6 of Regulation 101 (l/100km)
  d is the density of gas (LPG: 0.538 kg/l, CNG: 0,654 kg/m3, see par. 5.2.4. of regulation 101)
  dist is the total distance travelled during the type 1 test (km)
Substituting eq. 4 into 3, and then eqs. 3 and 2 into 1 the result becomes:
Ggas = mgas*100/(FC*dist*d) (5)

## Slide 11: Energy gas ratio - Calculation method
FC as calculated on LPG only is a conservative assumption: