## Slide 1: WLTC VALIDATION 1
14/10/2011- M. CAPITAINE

## Slide 2: SUMMARY
VEHICULE TEST
DYNAMOMETER
MESUREMENTS
TEST SUMMARY
DRIVABILITY
COMPARAISON JAPAN/STEVEN
DRIVABILITY => ~CO2
THERMO MANAGEMENT

## Slide 3: VEHICULE TEST
VEHICULE | A | B | C
FUEL | GASOLINE | DIESEL | DIESEL
ENGINE DISPLACEMENT | 1149 cm3 | 2300 cm3 | 1600 cm3
POWER | 74kW at 5500rpm | 92kW at 3500rpm | 80kW at 4000rpm
TEST INERTIA | 1250 kg | 2040 kg | 1470 kg
TRANSMISSION | MT (5) | MT (6) | AT
EMISSION STANDARD | Euro5 | Euro5 | Euro5
MANAGEMENT SPECIFICITY | AIR SURALIMENTATION | - | STOP&START

## Slide 4: DYNAMOMETER
DYNAMOMETER FOR LIGHT-DUTY VEHICULES STANDARD TESTS
DYNAMOMETER SYSTEM | HORIBA - Single roller 48"
ABSORPTION NOMINAL POWER | 103 kW [96 - 200 km/h]
OPERATING TEMPERATURE | +20°C to +30°C ± 2°C
HUMIDITY CONTROL | 5g to 13g water / kg dry air ± 5%
ELECTRIC INERTIA RANGE | 450 to 3500kg
BLOWER CONTROL | Proportional to vehicle speed
BAGS DILUTED GAS SAMPLING | HORIBA 9300T - 9 & 12m3/min
BAGS DILUTED GAS ANALYSIS | HORIBA MEXA 9400

## Slide 5: MESUREMENTS
MEASUREMENTS | METHODS |  | 
 | VEHICULE A | VEHICULE B | VEHICULE C
ROLLER SPEED | Dynamometer sensor |  | 
TIRE SPEED | CAN-Bus | CAN-Bus | Frequencemeter
GEAR SHIFT POINTS | CAN-Bus | CAN-Bus | -
ACCELERATION PEDAL ANGLE (%) | CAN-Bus | CAN-Bus | Voltage measurement
ENGINE COOLANT TEMPERATURE | CAN-Bus | CAN-Bus | -
ENGINE SPEED (VOLUNTARY) | CAN-Bus | CAN-Bus | -
POLLUTANTS EMISSIONS (VOLUNTARY) | Bag Sampling (4phases) HCt / CH4 / CO / NOX / NO / CO2 (=> Fuel consumption) |  | 

## Slide 6: TESTS SUMMARY
Comment : Same driver for all tests
VEHICULE | CYCLE | GEAR SHIFT | VEHICULE CONDITIONS | TEST NUMBERS (DRIVE MESUREMENT)
A | WLTC | GEAR SHIFT 1 (JAPAN) | COLD | 3
 |  |  | HOT | 6
 |  | GEAR SHIFT 2 (STEVEN) | COLD | 3
 |  |  | HOT | 4
 | NEDC |  | COLD | 2
B | WLTC | GEAR SHIFT 1 (JAPAN) | COLD | 2
 |  |  | HOT | 3
 |  | GEAR SHIFT 2 (STEVEN) | COLD | 2
 |  |  | HOT | 2
 | NEDC |  | COLD | 2
C | WLTC | GEAR SHIFT 3 (AUTOMATIC) | COLD | 2
 |  |  | HOT | 2
 | NEDC |  | COLD | 1

## Slide 7: DRIVABILITY
LOW / VEHICULE A / GEAR SHIFT JAPAN / COLD TEST SUMMARY
ROLLER SPEED

## Slide 8: DRIVABILITY
MIDDLE / VEHICULE A / GEAR SHIFT JAPAN / COLD TEST SUMMARY
ROLLER SPEED

## Slide 9: DRIVABILITY
HIGH / VEHICULE B / GEAR SHIFT JAPAN / COLD TEST SUMMARY
ROLLER SPEED

## Slide 10: DRIVABILITY
EXT-HIGH / VEHICULE B / GEAR SHIFT JAPAN / COLD TEST SUMMARY
ROLLER SPEED

## Slide 11: DRIVABILITY
OBSERVATIONS SYNTHESIS & PROPOSALS
LOW
  Observation : Engine speed too low during some low speed phases
  Cause : Gear shift engaged too long
  Result : Risk of engine cut-off
  Proposal : Disengage gear shift earlier
MIDDLE
  Observation : Engine speed too high during some accelerations having engaged
  Cause : Gear shift 1
  Result : Engine point unrepresentative of reality
  Proposal : Gear shift 2

## Slide 12: DRIVABILITY
OBSERVATIONS SYNTHESIS & PROPOSALS
HIGH (& ALL PHASES)
  Observation : Speed management with accel pedal during some of the small decelerations
    (engine break or small acceleration, but not with the break pedal => Otherwise with the speed was out of the tolerances)
  Result : Risk of deterioration of the repetability (??)
EXTRA-HIGH (& HIGH PHASE MAIN ACCELERATION, DEPENDING ON ENGINE POWER)
  Observation : Target speed is hard to follow during the main acceleration
  Cause : Engine in full acceleration (depending on engine power)
  Result :
    Vehicule cannot follow the cycle
    Deteriorates the repetability
    Proposal : Limit the acceleration (not speed)

## Slide 13: COMPAR JAPAN / STEVEN
No fundamental difference of drivability between the two gear shift procedures, but changes engine speed :

## Slide 14: DRIVABILITY => ~CO2
Significant dispersion in the Extra-High cycle
Cause : Engine in full acceleration

## Slide 15: DRIVABILITY => ~CO2
Significant dispersion in the Extra-High cycle
Possible cause : Engine in full acceleration

## Slide 16: THERMO MANAGEMENT
ENGINE HOT AT HALF OF THE MID CYCLE

## Slide 17: THERMO MANAGEMENT
HOT FROM THE HALF OF THE LOW CYCLE