## Slide 1
<number>
<number>
Progress Report of World-wide Light-duty Test Cycle
Prepared by Japan
DHC group
under GRPE/WLTP informal group
17th January 2012
Palais des Nations, Geneva

## Slide 2
<number>
1. Progress summary after the 8th DHC meeting
2011 |  |  |  |  |  |  | 2012
June | Jul. | Aug. | Sep. | Oct. | Nov. | Dec. | Jan.
Validation1
10th DHC
@Brussels
8th DHC
62nd GRPE
@Geneva
9th DHC
@Stockholm
(1)
(2)
Web
26th July
(1) Propose WLTC ver.1 (DHC-09-02, DHC-09-05)
(2) Provide WLTC ver.2 for validation1
(mainly Ex-HIGH phase was modified based on EU request)
(3) Report on validation1 test results
Decide 3 months delay for further review on WLTC ver.2
(4) Review supplemental methodology and WLTC ver.3
Decide to develop the cycle for “Low powered vehicle”
with additional data acquisition
(5) Provide WLTC ver.4 for validation1b
Web
12th Dec.
Web
10th Jan.
(3)
(4)
(5)
Further review
Ex-HIGH modification
Slight modification

## Slide 3: 2. Summary of Validation 1 Test
Participate parties : JRC, India, Austria, ACEA, Korea, and Japan.
  Difficulty at the low speed part (less than 10km/h). require half clutch operation
  Difficulty to trace the cycle for low powered vehicles.
  Concern to reproducibility at micro transient portions.
  Difficulty to trace the cycle due to max. speed limit of vehicle specification.
  Some of vehicles is not completely warmed up at the end of Low phase from cold starting. Middle phase might be necessary for hot start testing, if applicable.
  Observed tire slippage at the high acceleration and deceleration.
The reports are available on UN-ECE web site. (DHC10) : http://www.unece.org/trans/main/wp29/wp29wgs/wp29grpe/wltp_dhc10.html

## Slide 4
3. Needs to modify WLTC ver.2
Reasons | Actions
Reflection of validation1 | Some of comments were reflected to WLTC ver.4
Additional requirement from EU (representativeness of “dynamic performance”) | Adopted the supplemental methodology maintaining the original parameter.
Additional requirement from India (difficulty to trace the cycle for low powered vehicles) | Decided to develop the cycle for low powered vehicles. Under the discussion on the definition of “low powered vehicles”.

## Slide 5: 4. Characteristics of WLTC ver.4
WLTC version 4 was developed to reflect validation1 test results and to apply supplemental methodology.
Cum. Frequency
of V * a_positive
Cum. Frequency
of Vehicle speed
WLTC ver. 4
Apply supplemental methodology
Reflection of validation1
Set minimum speed @ 10km/h
Eliminate the micro transient portions
Set maximum acceleration @ 95 percent tile

## Slide 6: 5. Gear shift point
Two(2) methods are under the development
  Japan: Vehicle speed basis
    based on in-use data analysis
      Vehicle speed and Acceleration basis
    classified vehicle category and gearbox
      Passenger car / Light duty commercial vehicle
      (5 / 6 speed gearbox for reference)
    Agreed that this shift point can be used for validation1b test about WLTC ver.4
  EU: Engine speed basis
  (will be proposed before validation2)

## Slide 7
6. Next Actions
 | 2012 |  |  |  |  |  |  |  |  | 
 | Oct. | Nov. | Dec. | Jan. | Feb. | Mar. | Apr. | May. | Jun. | Jul.
Meetings |  |  |  |  |  |  |  |  |  | 
Develop the harmonized cycle |  |  |  |  |  |  |  |  |  | 
Validation |  |  |  |  |  |  |  |  |  | 
Confirmation |  |  |  |  |  |  |  |  |  | 
Low powered vehicle |  |  |  |  |  |  |  |  |  | 
WLTC v4
Additional data acquisition
10th DHC
@Brussels
13th DHC
64th GRPE
@Geneva
11th DHC
63rd GRPE
@Geneva
12th DHC @ Web
Web meeting, if necessary
Modification
Validation1b
Validation2
Confirmation
Modify, if necessary
Modify, if necessary
Validation1&2
Evaluate gear shift proposal
Develop low powered vehicle cycle
Discuss the definition of “low powered vehicles”