## Slide 1: Gear shift analysis ~ Further Review on original JPN gear shift points ~
Prepared by Japan
13 January 2012

## Slide 2: Summary
Although it was observed that there is slight difference between the shift points according to vehicle types, Japan propose two kind of shift points for Passenger car and LDCV for Validation-1 test (same as original proposal).
For reference, Japan provide specific shift points for vehicle types. If these specific points improve the drivability during Validation test, we will discuss the classification of gear shift points.

## Slide 3: Multiple regression analysis of in-use driving data
Investigated influence between shift up point and each factor
It was observed that “Vehicle speed” and “Acceleration” have big impact on the gear shift points. Furthermore, it was observed that vehicle specifications influence gear usage.
Explanatory variable | Standard partial regression coefficient β | correlation coefficient γ
Vehicle speed @shift up-1 | 0.852 | 0.826
Acceleration @shift up-1 | -0.214 | -0.222
Vehicle category (PC: 0, LDCV: 1) | 0.163 | 0.010
Engine displacement | -0.045 | 0.013
Fuel type (0: Petrol, 1: Diesel, 3: LPG) | -0.036 | 0.052
Power to mass ratio | 0.030 | -0.018
No. of gears | 0.011 | 0.017
Dependent variable: Gear position after shift up
small
impact

## Slide 4: Classification
Passenger car
Light duty commercial vehicle
4/5 gearbox
6 gearbox
Low geared vehicle
Van type (Passenger car basis)
4/5 gearbox
6 gearbox
4/5 gearbox
In-use data were analyzed according to vehicle type
Truck type
5 gearbox
4/5/6 gearbox
4/5/6 gearbox

## Slide 5: Criteria of classification for Light duty commercial vehicle
Low geared vehicle: DTC < 0.09 (Gio, Ace, Every)
Truck type: Wn < 0.55 (LT, Bongo, Canter, Caravan)
Van type: Wn > 0.55 (Porter, Transit, Partner, Trafic, Sprinter)
(DTC)
(Wn)

## Slide 6: Gearshift equation
The gearshift equations were developed by multiple regression.
Because the dataset of 6 speed gearbox of LDCV are from limited number of vehicles, the result of multiple regression are reflected specific gear usage. (-> not reliable)

## Slide 7: The boundary condition
The boundary condition was set based on an average of the estimated gear position in each operation.
Boundary condition

## Slide 8: Additional condition
Put in 1st gear with the clutch disengaged 5 seconds before each take-off event.
Keep same gear position at least 4 second
Avoid shift up at the top of hill (when shift to deceleration phase)
Apply the downshift event under the deceleration phase. except high deceleration phase because full braking operation was expected.
(only LDCV) Avoid to use 1st gear except take-off phase
In order to make the shift change event natural and stable, the following additional condition were applied.
Shall be driven in the range of idling engine speed and 90% of maximum rated engine speed.
  When engine speed exceed 90% of maximum rated speed, it is necessary to shift up gear
  When engine speed below the idling speed, it is necessary to disengage clutch and shift down gear
The following criteria is necessary from viewpoint of operation.

## Slide 9: Shift operation
Clutch operation
Speed (km/h)
Time (s)
②
①
Clutch disengaged
Clutch engaged
within 2seconds
Shift indication
Shift indication by Japan shows the start points to shift gears (clutch off point). Shift operation shall be completed within 2 seconds

## Slide 10: Gear shift point for PC
earlier than 5 speed
earlier than 5 speed

## Slide 11: Gear shift point for PC
earlier than 5 speed
later than 5 speed
It was observed that there is few difference between the shift points according to # of gearbox.

## Slide 12: Gear shift point for LDCV

## Slide 13: Gear shift point for LDCV
It was observed that there is slight difference between the shift points according to vehicle type. However these unique shift points be merged into one unified shift points.

## Slide 14: Vehicle information

## Slide 15: Vehicle information

## Slide 16: Vehicle information
Total: 153 vehicles

## Slide 17: Definition of the gear shift point
Shift up-1: Clutch disengaged point for up-shifting
Shift up-2: Clutch engage point after putting in higher gear
Shift down-1: Clutch disengaged point for down-shifting or neutral
Extract driving condition at the shift up-1, shift up-2 and shift down-1
Shift up-1
Shift up-2

## Slide 18: 5.3. Drive Train Coefficient（DTC）
DTC : Drive Train Coefficient
2πr / (im * if) ： running distance
per engine speed (m)
r ： tire radius (m)
im ： gear ratio
if ： final reduction gear ratio
V ： vehicle speed （m/s）
Ne ： engine speed （1/s）
y = DTC * G(x)
G(x)