## Slide 1: Test results of Validation test 1b and Cycle modifications
<number>
the 12th DHC group
under GRPE/WLTP informal group
29 March 2012
Joint Research Centre, Ispra
Prepared by Japan

## Slide 2: Table of contents
<number>
Result of Validation 1b by Japan
Result of Validation 1b by India and JRC
Summary of Indicated portions
Cycle modification for Validation 2
Proposed WLTC ver.5 for Validation 2
List of issues
Characteristics of proposed WLTC ver.5
Detail of modifications

## Slide 3: 1.1. Overview of Validation test 1b in Japan
<number>
Vehicle No. | A | B | C | D | E | F
Vehicle category | PC | PC | LDCV | LDCV | LDCV | PC
Fuel type | Petrol | Petrol | Petrol | Petrol | Petrol | Petrol
Engine capacity (cc) | 658 | 1339 | 658 | 1495 | 1998 | 1000
Max. rated power (kW) | 43 / 7200 | 73 / 6000 | 36 / 5800 | 71 / 6000 | 98 / 5600 | 50/6000
Curb vehicle mass (kg) | 710 | 1000 | 960 | 1120 | 1760 | 910
Test mass (kg) | 820 | 1110 | 1070 | 1330 | 1870 | 1046 (1020*)
Gross vehicle mass (kg) | 930 | 1275 | 1430 | 2030 | 3340 | 1250
Power to mass ratio (KW/t) (Curb mass basis) | 60.6 | 73.0 | 37.5 | 58.2 | 55.7 | 54.9
After treatment | TWC | TWC | TWC | TWC | TWC | TWC
Emission standard | 2005 | 2005 | 2005 | 2005 | 2005 | EURO V
Transmission | 5MT | 5MT | 5MT | 5MT | 5MT | 4AT
Test mass: A~E: Current JPN regulation test mass (Curb mass + 110 kg)
: F: Proposed gtr test mass (almost same as JP-mass)
Gear shift: fixed gear shift (by Japan)
Vehicle F: Current JPN reg. mass: 1020 kg, Proposed gtr test mass: 1046 kg

## Slide 4: 1.2. Test result of Passenger car
<number>
ARROW (↓): Require precise acceleration pedal/clutch operation
CIRCLE (○): Hard to follow the trace (require close to W.O.T. operation)

## Slide 5: 1.2. Test result of Passenger car
<number>
ARROW (↓): Require precise acceleration pedal/clutch operation
CIRCLE (○): Hard to follow the trace (require close to W.O.T. operation)

## Slide 6: 1.2. Test result of Passenger car
<number>
ARROW (↓): Require precise acceleration pedal/clutch operation
CIRCLE (○): Hard to follow the trace (require close to W.O.T. operation)

## Slide 7: 1.3. Test result of Light duty commercial vehicle
<number>
ARROW (↓): Require precise acceleration pedal/clutch operation
CIRCLE (○): Hard to follow the trace (require close to W.O.T. operation)

## Slide 8: 1.3. Test result of Light duty commercial vehicle
<number>
ARROW (↓): Require precise acceleration pedal/clutch operation
CIRCLE (○): Hard to follow the trace (require close to W.O.T. operation)

## Slide 9: 1.3. Test result of Light duty commercial vehicle
<number>
ARROW (↓): Require precise acceleration pedal/clutch operation
CIRCLE (○): Hard to follow the trace (require close to W.O.T. operation)

## Slide 10: 2. Result of Validation 1b by India and JRC
<number>
India
  Dynamic concerns (difficult to follow the cycle)
    48-67, 140-160, 250-265, 275-295, 660-670, 760-770, 815-825, 1060-1065, 1080-1123, 1140-1180, 1375-1385, 1420-1450, 1530-1585, 1640-1675
  PMR concerns (Vehicles of 35 to 65 kW/t have difficulty)
    780-804, 1165-1210, 1180-1250, 1530-1740
  Difficult to follow the lower speeds of 10km/h
JRC
  Observed difficulty to drive the low speed parts (~10 km/h) with the 1st gear
  With typical European vehicles, there seems to be few problem to follow the trace (accelerations and top speed portions of WLTC ver.4).

## Slide 11: 3. Summary of validation 1b
<number>
From the viewpoints of drivability, traceability and reproducibility, the following 31 portions are pointed out by India, JRC and Japan.
2
3
4
5
6
7
8
9
1011
13
17
19
20
23
22
21
26
28
1415
25
1
12
18
24
26
29
30
16
27
31: number of decimal places

## Slide 12: 3. Summary of validation 1b
<number>
No. | Time | Comments | by
1 | 24 - 28 | Need to be smoothness | Japan
2 | 48 – 67 | Difficult to drive the low speed parts | JRC/India/Japan
3 | 140 – 160 | Difficult to drive the low speed parts | JRC/India/Japan
4 | 185 - 210 | Difficult to drive the low speed parts | JRC/India/Japan
5 | 250 - 270 | Need to be smoothness | India/Japan
6 | 275 - 295 | Need to be smoothness | India/Japan
7 | 545 – 560 | Need to be smoothness | Japan
8 | 600 - 615 | Require close to W.O.T. operation | Japan
9 | 660 - 670 | Difficult to drive the low speed parts | JRC/India/Japan
10 | 709 | Difficult to drive the low speed parts | JRC/India/Japan
11 | 715 – 718 | Difficult to drive the low speed parts | JRC/India/Japan
12 | 720 – 730 | Require close to W.O.T. operation | Japan
13 | 760 - 770 | Difficult to drive the low speed parts | JRC/India/Japan
14 | 770 – 785 | Require close to W.O.T. operation | Japan
15 | 780 -804 | Difficult to drive (PMR concern) | India
16 | 800 – 810 | Require close to W.O.T. operation | Japan

## Slide 13: 3. Summary of validation 1b
<number>
No. | Time | Comments | by
17 | 815 – 830 | Need to be smoothness | India/Japan
18 | 860 – 870 | Require close to W.O.T. operation | Japan
19 | 910 – 925 | Require close to W.O.T. operation | Japan
20 | 950 – 980 | Require close to W.O.T. operation | Japan
21 | 1060 – 1065 | Difficult to drive the low speed parts | JRC/India/Japan
22 | 1070 – 1125 | Difficult to follow the target speed Require close to W.O.T. operation | India/Japan
23 | 1140 - 1155 | Difficult to drive the low speed parts | JRC/India/Japan
24 | 1155 - 1250 | Difficult to follow the target speed Require close to W.O.T. operation | India/Japan
25 | 1310 – 1325 | Require close to W.O.T. operation | Japan
26 | 1375 - 1385 | Require close to W.O.T. operation | India/Japan
27 | 1420 - 1450 | Difficult to follow the target speed | India
28 | 1530 - 1585 | Require close to W.O.T. operation | India/Japan
29 | 1640 - 1675 | Require close to W.O.T. operation | India/Japan
30 | 1530 - 1740 | Difficult to drive (PMR concern) | India
31 | All | to be one decimal point ( to XX.X km/h) | Japan

## Slide 14: 4. Proposed cycle modification for Validation 2
<number>
As a first step to move forward to validation 2, Japan propose to modify the following items (15 portions).
  the minimum speed set to 12km/h
  Smoothing to improve repeatability
  Set vehicle speed one decimal point
Other 16 remaining portions regarding dynamic concerns which was indicated by India and Japan should be considered during Validation 2.

## Slide 15: 5. Proposed WLTC ver.5 for Validation 2
<number>
12 km/h
12 km/h
12 km/h
12 km/h
12 km/h
12 km/h
Smoothing
Smoothing
Smoothing
Smoothing
Smoothing
Concern
Concern
Concern
Concern
Concern
Concern
1
2
3
4
5
6
7
8
9
10 11
12
13
14
15
16
17
18
31: Time chart was changed from two decimal point to one decimal point

## Slide 16: 5. Proposed WLTC ver.5 for Validation 2
<number>
12 km/h
12 km/h
Concern
Concern
Concern
Concern
Concern
Concern
Concern
Concern
Concern
19
20
21
22
23
24
25
26
28
29
30
Concern
27
31: Time chart was changed from two decimal point to one decimal point

## Slide 17: 6.1. List of issues
<number>
No. | Time | Comments | by | Action
1 | 24 - 28 | Need to be smoothness | Japan | Smoothing
2 | 48 – 67 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h
3 | 140 – 160 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h
4 | 185 - 210 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h
5 | 250 - 270 | Need to be smoothness | India/Japan | Smoothing
6 | 275 - 295 | Need to be smoothness | India/Japan | Smoothing
7 | 545 – 560 | Need to be smoothness | Japan | Smoothing
8 | 600 - 615 | Require close to W.O.T. operation | Japan | Evaluated during validation2
9 | 660 - 670 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h & Smoothing
10 | 709 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h
11 | 715 – 718 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h
12 | 720 – 730 | Require close to W.O.T. operation | Japan | Evaluated during validation2
13 | 760 - 770 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h
14 | 770 – 785 | Require close to W.O.T. operation | Japan | Evaluated during validation2
15 | 780 -804 | Difficult to drive (PMR concern) | India | Evaluated during validation2
16 | 800 – 810 | Require close to W.O.T. operation | Japan | Evaluated during validation2

## Slide 18: 6.2. List of issues
<number>
No. | Time | Comments | by | Action
17 | 815 – 830 | Need to be smoothness | India/Japan | Smoothing
18 | 860 – 870 | Require close to W.O.T. operation | Japan | Evaluated during validation2
19 | 910 – 925 | Require close to W.O.T. operation | Japan | Evaluated during validation2
20 | 950 – 980 | Require close to W.O.T. operation | Japan | Evaluated during validation2
21 | 1060 – 1065 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h
22 | 1070 – 1125 | Difficult to follow the target speed Require close to W.O.T. operation | India/Japan | Evaluated during validation2
23 | 1140 - 1155 | Difficult to drive the low speed parts | JRC/India/Japan | Minimum speed to 12 km/h
24 | 1155 - 1250 | Difficult to follow the target speed Require close to W.O.T. operation | India/Japan | Evaluated during validation2
25 | 1310 – 1325 | Require close to W.O.T. operation | Japan | Evaluated during validation2
26 | 1375 - 1385 | Difficult to follow the target speed Require close to W.O.T. operation | India/Japan | Evaluated during validation2
27 | 1420 - 1450 | Difficult to follow the target speed | India | Evaluated during validation2
28 | 1530 - 1585 | Difficult to follow the target speed | India/Japan | Evaluated during validation2
29 | 1640 - 1675 | Difficult to follow the target speed | India/Japan | Evaluated during validation2
30 | 1530 - 1740 | Difficult to drive (PMR concern) | India | Evaluated during validation2
31 | All | to be one decimal point ( to XX.X km/h) | Japan | one decimal point

## Slide 19: 7.1. Characteristics of proposed WLTC ver.5
<number>
Chi squared value of proposed WLTC v5 is identical to that of WLTC v4

## Slide 20: 7.1. Speed frequency distributions
<number>
Proposed

## Slide 21: 7.3. v * a_pos frequency
<number>
LOW
MIDDLE
HIGH
Extra-HIGH
95%tile of WWW database is 10 m2/s3
Max. of WLTC v5 is 11.2 m2/s3
95%tile of WWW database is 14 m2/s3
Max. of WLTC v5 is 16.7 m2/s3
95%tile of WWW database is 16 m2/s3
Max. of WLTC v5 is 19.7 m2/s3
95%tile of WWW database is 18 m2/s3
Max. of WLTC v5 is 20.9 m2/s3
The maximum v*a of WLTC ver.5 exceed 95%tile of WWW database

## Slide 22: 8. Detail of modification
<number>
1
2
3
4
Not modified, but need further evaluation

## Slide 23: 8. Detail of modification
<number>
5
6
7
8
9
Not modified, but need further evaluation

## Slide 24: 8. Detail of modification
<number>
10
12
13
14
15
18
17
11
16
Not modified, but need further evaluation

## Slide 25: 8. Detail of modification
<number>
19
20
21
22
22
Not modified, but need further evaluation

## Slide 26: 8. Detail of modification
<number>
24
24
25
27
23
26
Not modified, but need further evaluation

## Slide 27: 8. Detail of modification
<number>
28
30
29
Not modified, but need further evaluation

## Slide 28
<number>
Source: JSAE 2008