## Slide 1
Current status of WLTP-DHC
Prepared by Japan
the 13th DHC group
under GRPE/WLTP informal group
5th June 2012
Palais des Nations, Geneva

## Slide 2: Table of contents
<number>
Progress since last GRPE meeting
Summary of Validation1b
Profile of WLTC ver.5
Gear Shift Prescription
Open Issues Lists
Next actions
Next meeting
Notes: <number>

## Slide 3: 1. Progress since last GRPE meeting
’11/9 10 11 12 ’12/1 2 3 4 5 6
WLTC
Version4
WLTC
Version5
Validation 1 Test
(WLTC Version 2)
Validation 1b Test
Add new parameter (v*a positive)
for cycle modification
LPVC*
Version2
Cycle
Gear shift
Concern on “Dynamic” profile
Concern for Low Powered Vehicle (LPV)
Additional data
acquisition for LPV
Vehicle speed basis
Validation 1b Test
During 12th DHC meeting @ JRC,
it was agreed to move on to Validation2
with following conditions.
WLTC version5
LPVC version2
Steven 3 gear shift (engine speed basis)
Steven 3
Exchange the strategy of each method,
then modified based on validation result
backup
Validation 2 Test
Engine speed basis
<number>

## Slide 4: 2.1. Summary of Validation 1b
From the viewpoints of drivability, traceability and reproducibility, the following 31 portions are pointed out by India, JRC and Japan.
2
3
4
5
6
7
8
9
1011
13
17
19
20
23
22
21
28
1415
25
1
12
18
24
26
29
30
16
27
31: number of decimal places
<number>

## Slide 5: 3.2. Profile of WLTC ver.5
12 km/h
12 km/h
12 km/h
12 km/h
12 km/h
12 km/h
Smoothing
Smoothing
Smoothing
Smoothing
Smoothing
Concern
Concern
Concern
Concern
Concern
Concern
1
2
3
4
5
6
7
8
9
10 11
12
13
14
15
16
17
18
Modification points from version4. Red  Applied, Blue  Concern
<number>

## Slide 6: 3.2. Profile of WLTC ver.5
12 km/h
12 km/h
Concern
Concern
Concern
Concern
Concern
Concern
Concern
Concern
Concern
17
19
20
21
22
23
24
25
26
28
29
30
27
Concern
Modification points from version4. Red  Applied, Blue  Concern
<number>

## Slide 7: 3.3. Profile of WLTC ver.5
Chi squared value of proposed WLTC v5 is identical to that of WLTC v4
<number>

## Slide 8: 3.4. Profile of WLTC ver.5
Proposed
<number>

## Slide 9: 3.5. Profile of WLTC ver.5
LOW
MIDDLE
HIGH
Extra-HIGH
95%tile of WWW database is 10 m2/s3
Max. of WLTC v5 is 11.2 m2/s3
95%tile of WWW database is 14 m2/s3
Max. of WLTC v5 is 16.7 m2/s3
95%tile of WWW database is 16 m2/s3
Max. of WLTC v5 is 19.7 m2/s3
95%tile of WWW database is 18 m2/s3
Max. of WLTC v5 is 20.9 m2/s3
The maximum v*a of WLTC ver.5 exceed 95%tile of WWW database
<number>

## Slide 10: 4. Gear Shift Prescription (Steven3)
Input Parameter
Rated engine power
Rated engine speed
Idling speed
engine speed for short trips
decisive for downshifts,
number of gears
Gear ratios
Test mass of the vehicle
others
Calculations
Determination of usable gears
Lowest gear determination
Initial highest gear determination
Calculation of available power
Determination of driving resistance power
Determination of acceleration power
Determination of highest gear
Gear use starts
Corrections/modifications
gear insertion 1 second before standhill
  Prohibit the gear skip
  The minimum hold time is 3 s.
  set the gear lever to neutral / clutch to engaged
  no gearshift, if acc is followed by dec condition
  others
Application
Set gear shift information
to drivers aid
<number>

## Slide 11: 5.1. Open Issues -1
<number>
 | Issues | Discussion points | Status
1 | Deadline for submission of driving data | India and China requested deadline be extended to May | Decided to start development of new cycle after 8th DHC meeting. Later data submission is still open for analysis.
2 | Regional Weighting when developing the WLTC | traffic volume same weighting compromised weighting | It was agreed to adopt the traffic volume ratio during the 8th DHC meeting
3 | Threshold Speed for L/M/H | according to DHC-06-03 CP’s requirement | Threshold speeds of 60, 80 and 110km/h were agreed for the cycle phases during 7th DHC meeting
4 | High Phase Cycle Construction (US&EU versus other regions) | only ONE unified cycle possess TWO types of High phase cycle | It was agreed to possess two (2) types of HIGH phase cycle during 7th meeting.
5 | Mode Construction | a) cold start test only b) cold start & hot soak start | Base mode construction was provided for Validation 2. Based on validation2 results, final decision will be discussed.
CLOSED
<number>
CLOSED
CLOSED
CLOSED
Notes: <number>

## Slide 12: 5.2. Open Issues -2
<number>
 | Issues | Discussion points | Status
6 | Weighting Factor for L/M/H/Ex-H Phase | harmonized weighting factors permit regional weighting factors | Refer document DHC-13-05 for further discussion
7 | Gear Shift Points | fixed points based on vehicle specification others | Vehicle specific shift points (b) was provided for Validation 2.
8 | How to treat the vehicles which are not able to follow the prescribed cycle | continue to drive with wide-open-throttle exempt the Ex-H (or M&H) phase (s) others | Refer documentDHC-13-03, DHC-13-04 for further discussion
9 | Check the driving profile based on the vehicle characteristic |  | Analyze the in-use data based on vehicle characteristic (i.e. power to mass ratio)
<number>
CLOSED
Notes: <number>

## Slide 13
 | 2012 2013 |  |  |  |  |  |  |  |  | 
 | June | Jul. | Aug. | Sep. | Oct. | Nov. | Dec. | Jan. | Feb. | Mar.
Meetings |  |  |  |  |  |  |  |  |  | 
Validation 2 test |  |  |  |  |  |  |  |  |  | 
Confirmation test |  |  |  |  |  |  |  |  |  | 
Related DTP activities |  |  |  |  |  |  |  |  |  | 
<number>
6.Next Actions
13th DHC
64th GRPE
14th DHC
16th DHC
65th GRPE
Report of Validation 2
Agreement of OIL
15th DHC
Interim Report of Validation 2
Conducting test
Data analysis
Start confirmation test
GTR draft
Report to GR
To be confirmed
No concern should be observed
DTP-ICE
10th DTP
11th DTP
To be discussed
Cycle profile, Weighting Factors, Gear shift prescription, LPVC
<number>

## Slide 14: 7. Next Meetings
Next 14th DHC meeting will be set during next DTP meeting in September at JRC.
Main agenda items will be
Validation2 test results from contracting parties
WLTC modification
Weighting factors of L/M/H/ExH Phases
LPVC
Gear Shift Points of WLTC
(15th DHC meeting will be set around November 2012)
<number>
Notes: <number>