## Slide 1
<number>
Mr H A Nakhawa, ARAI, Pune, India
13th DHC Informal Group Meeting
64th GRPE Session, June 2012
Geneva
Validation 1 results of Indian Vehicles on LPVC Version 1.4
and
Issues pertaining to WLTC Version 5
WLTP-DHC-13-03

## Slide 2: Validation 1 Test on Low Powered Vehicles and Issues pertaining to WLTC Version 5
Contents:
Validation 1 results of Indian Vehicles on LPVC Version 1.4
Issues pertaining to WLTC Version 5 based on India Validation 1b results
<number>

## Slide 3
<number>
Contents:
Introduction
Vehicle Models Tested
Test Matrix
Test Results
Observations and Recommendations on LPVC
Validation 1 results of Indian Vehicles on LPVC Version 1.4

## Slide 4: Introduction
Test Cycle - Low Power Vehicle Cycle (LPVC) version 1.4
Steven 3 Gear shift methodology for Gear Shift Calculation
Total 8 low powered vehicles PMR < 34 kW/t tested
All vehicles are Manual Transmission
Speed Tolerance +/- 2 km/h
<number>
 | Power Range kW | PMR Range kW/t (on Kerb weight)
Diesel | 6.5 to 46.3 | 10.1 to 27.7
CNG | 15.5 | 14.09

## Slide 5: Vehicle Models Tested
Sr. No. | Make | Model | Vehicle Category | Fuel Type | Kerb Weight kg | Test Mass kg * | Engine CC | Max. Power kW | PMR kW/t | Max. vehicle speed in km/h | Phases Followed based on vehicle classification
1 | Mahindra | Gio | M1 | Diesel | 670 | 842 | 441.5 | 6.8 | 10.1 | 55 | L+L+L
2 | Piaggio | Ape Mini | N1 | Diesel | 597 | 838 | 441 | 6.5 | 10.88 | 59 | L+L+L
3 | Tata Motors | Magic Iris | M1 | Diesel | 685 | 833 | 611 | 8 | 11.67 | 55 | L+L+L
4 | Tata Motors | Magic CNG | N1 | CNG | 1100 | 1275 | 701 | 15.5 | 14.09 | 77 | L+M+L
5 | Piaggio | Ape Truck Plus | N1 | Diesel | 800 | 1218 | 871 | 12.5 | 15.63 | 74 | L+M+L
6 | Mahindra | Maxximo | N1 | Diesel | 950 | 1313 | 909 | 18 | 18.95 | 70 | L+M+L
7 | Mahindra | Bolero Camper SC | N1 | Diesel | 1725 | 2149 | 2523 | 46.3 | 26.84 | 100 | L+M+H
8 | Mahindra | Bolero SLX | M1 | Diesel | 1670 | 1854 | 2523 | 46.3 | 27.7 | 100 | L+M+H
<number>
*Note:
Test mass = Kerb mass + 100 + Optional mass.
Optional mass = 15% of the (GVW - Kerb mass – 100) for Passenger vehicles and,
35% of the (GVW - Kerb mass – 100) for Commercial vehicles

## Slide 6: Test Matrix
<number>
Sr. No. | Make | Model | Fuel Type | No of Tests Steven 3 Gear Shift |  | Total Tests per vehicle
 |  |  |  | Cold | Hot | 
1 | Mahindra | Gio | Diesel | 2 | - | 2
2 |  | Maxximo | Diesel | 2 | - | 2
3 |  | Bolero SLX | Diesel | 2 | - | 2
4 |  | Bolero Camper | Diesel | 2 | - | 2
5 | Tata Motors | Iris | Diesel | 2 | - | 2
6 |  | Ace Magic | CNG | 3 | - | 3
7 | Piaggio Vehicles | Ape Truk Plus | Diesel | 1 | 2 | 3
 |  | Ape Mini | Diesel | 1 | 2 | 3
8 |  |  |  |  |  | 
Total Tests |  |  |  | 15 | 4 | 19

## Slide 7
<number>
Actual cycle traced by the test vehicle as per LPVC Version 1.4
Inset shows the details of the Test Vehicle including the Power, Kerb Mass, PMR in kW/t. (Power/Kerb Mass), Engine cc, Test Mass
Tested as per GTR test mass
Test mass = Kerb mass + 100 + Optional mass.
Optional mass = 15% of the (GVW - Kerb mass – 100) for PC and,
35% of the (GVW - Kerb mass – 100) for LDCV
Test Results

## Slide 8: Test Results
<number>

## Slide 9
<number>
Test Results

## Slide 10: Test Results
<number>

## Slide 11: Test Results
<number>

## Slide 12: Test Results
<number>

## Slide 13: Test Results
<number>

## Slide 14: Test Results
<number>

## Slide 15: Test Results
<number>

## Slide 16: Test Results
<number>

## Slide 17
Gear Shift
The low powered vehicles have a very deep first gear which is necessary to achieve the required gradeability. There is a big difference between the 1st to 2nd gear. This is reflected in N/V ratio also.
The Low powered vehicles show a deviation at the beginning of the cycle ~ 10-20 sec, where there is a shift at ~ 12 km/h and just thereafter. This phenomenon is observed on three test vehicles & it repeats at every 1st to 2nd gear transition.
We suggest to lower the gear shift point to ~ 10 km/h. Alternatively, the vehicles may be started in second gear without using the first gear.
In current regulation, fixed gear shift points are specified. A steady speed step of ~ 2 seconds is provided to account for the time required for gear change. However, with the Steven gear shift procedure, the gear shift points would be different depending on vehicle characteristics. Provision of steady speed step of ~ 2 s is necessary in WLTC driving cycle. Some thought needs to be given to address this issue.
Observations and Recommendations

## Slide 18
Cycle smoothening
In case of many vehicles, the cycle deviation & the tendency for the same is observed at the beginning of the cycle between 10 – 20 sec which involves a gear change at ~ 12 km/h speed.
This deviation is on account of transient nature of the cycle & gear change from 1st to 2nd . We recommend to smoothen this part of the cycle.
Vehicles up to PMR 22 kW/t have single / two cylinder engines – engine response to speed change is sluggish.
Too many fluctuations in the driving cycles lead to violations. Hence, smoothening to extent possible is desirable.
<number>
Observations and Recommendations

## Slide 19
<number>
13th DHC Informal Group Meeting
64th GRPE Session, June 2012
Geneva
Issues Post Validation 1b pertaining to WLTC Version 5

## Slide 20: Overview
The Present WLTC V5.0
Compact & Sub Compact Car Segment
Concerns Highlighted by India during 12th DHC (ISPRA)
Concerns and Issues
The Way Forward
<number>
Notes: <number>

## Slide 21: The Present: WLTC V5.0
<number>
 | Low | Middle | High | Ex-High | Total L/M/H | Total L/M/H/Ex H
Time in s | 589 | 433 | 455 | 323 | 1477 | 1800
Distance, km | 3 | 5 | 7 | 7.7 | 15 | 22.7
Max Speed, km/h | 56.5 | 76.6 | 97.4 | 131.3 | 97.4 | 131.3
Notes: <number>

## Slide 22: Indian Compact & Sub Compact Car Segment
Compact & Sub Compact Car segment is relevant to global economy, specially for developing and under-developed countries.
Such vehicles help the world in fuel & energy conservation, lower CO2 emissions, etc.
Produced in high volumes in Asia and exported throughout the world
Potential customers are first time buyers
Preferred by smaller families with second car usage.
<number>
Notes: <number>

## Slide 23: Main Concerns & Issues: H & Ex-H Phases
<number>
During 12th DHC India had presented Validation data. Most of Indian Compact Cars cannot follow the target speed with large deviations in driving High and Ex-High Phases as shown. (WLTP-DHC-12-02).
WLTC V5.0 finalized at ISPRA meeting has not addressed concerns of steep accelerations of High and Ex-High Phase.(WLTP-DHC-12-08) and these points are still open for investigation/finalisation.
Notes: <number>

## Slide 24: Results of Validation 1b
Vehicle | Engine CC | PMR, kW/Ton | V Max, kph | L | M | H | Ex | Class as per Steven
A | 796 | 49.0 | 135 | O / O | O / EP | X / EP | X / EP | Class3
E | 814 | 53.1 | 137 | O / O | O / EP | X / EP | X / EP | Class3
W | 998 | 55.6 | 145 | O / O | O / O | X / EP | X / EP | Class3
S | 1197 | 64.6 | 160 | O / O | O / O | O / EP | X / EP | Class3
B | 1198 | 70.7 | 169 | O / O | O / O | O / O | O / EP | Class3
AC | 796 | 36.4 | 135 | O / O | O / EP | X / EP | X / EP | Class3
W | 1197 | 45.2 | 140 | O / O | O / EP | X / EP | X / EP | Class3
SC | 1586 | 50.2 | 160 | O / O | O / O | X / EP | X / EP | Class3
<number>
Most of Indian Compact Cars fall in Class 3 Category. Validation 1b Test Results, show that these vehicles cannot drive High and Ex-High Phases of the Current Version of WLTC.
Class 3 cycle demands such cars to be driven in WOT (the Engine Protection Area) which is rarely used in actual driving situations.
India has already cited these concerns related to drivability during 12th DHC Meet at ISPRA
Legend :
O / O : OK for Drive Cycle Traceability and WOT (Engine Protection Mode) not activated
O / EP: OK for Drive Cycle Traceability and WOT (Engine Protection Mode) activated
X / EP: Not OK for Drive Cycle Traceability and WOT (Engine Protection Mode) Activated
Notes: <number>

## Slide 25: Cycle Class 3 Speed Threshold Change Proposal
Vehicle Speed< 135kph
Cannot run on EX H Phase
– OK with L, M and H with slight moderation on M, H Phases
Vehicle Speed > “A” km/h
Can Run on EX H Phase – No Issues
135<Vehicle Speed > “A” km/h
May NOT or difficult to Run on EXH Phase
Vehicles having max speed slightly > 135 km/h with lower PMR (power ~ 60 kW) will not be able to:
  Trace the EX H Phase, and /or
  May trace but with engine in WOT (engine protection region)
Notes: <number>

## Slide 26: Cycle Class 3 Speed Threshold Change Proposal
<number>
It is proposed to have the EX H Phase applicable for vehicles with Max speed around 155~160 km/h. Even with 160 km/h, some vehicles will have issues, however they are in the borderline areas.This change along with the slight moderation for M and H Phases should make the cycle conducive for application in major areas of the world
Notes: <number>

## Slide 27
The Way Forward
Compact and sub compact vehicles with PMR >34 kW/t and power < 60 kW have issues in negotiating the class 3 WLTC cycle consisting of L+M+H+ExH. Such vehicles are generally Gasoline/CNG/LPG vehicles having low torque to mass ratio and maximum speed around 130-155 km/h. The ExH phase of driving cycle is difficult to be traversed.
This has been presented at 12th DHC meeting at Ispra by India in Validation 1b test results
We propose that vehicles with max. speed upto 155 – 160 km/h be subjected to Class 3 L+M+H phases only. This would allow 15 - 18% margin on declared maximum speed to take care of driveability problems.
This change along with the slight moderation for M and H Phases should make the cycle conducive for application in major areas of the world
<number>
Issues pertaining to WLTC Version 5 based on India Validation 1b results

## Slide 28: Thank You
<number>