## Slide 1: Modification of WLTC Ver.5
Prepared by Japan
13th DHC group
under GRPE/WLTP informal group
5 June 2012
the Palais des Nations (Geneva/Switzerland)
WLTP-DHC-13-04

## Slide 2: Overview of our proposal
The WLTC should be sufficiently representative for all participating regions.
Through the validation test for WLTC-ver.5, some major vehicles came under the engine protection region, in which ordinary driving rarely steps.
The WLTC should be the cycle in which major vehicles in the current market can be operated perfectly without coming under the engine protection region.
Japan proposes the modification of the WLTC-ver.5 to eliminate points where some major vehicles come under the engine protection region without decreasing the amount of CO2.
<number>

## Slide 3: Engine Protection Region
１．Necessity of Engine Protection region
In general, engine temperature depends on the balance between combustion heat and emitted heat from surface of cylinder and cylinder head, valve sheet etc.
In the condition of high engine speed/high load, the engine cannot emit its heat enough, therefore engine temperature rises rapidly, resulting in melting exhaust valve, pistons or catalyst. Moreover, under such condition, catalysts could also be overheated and damaged.
To prevent such problems, “engine protection” is needed.
To protect engines and catalysts from such damages, Air/Fuel ratio should be enriched under the certain conditions to reduce the temperatures of engine valves and cylinders’ interface by latent heat of vaporization of incomplete combustion fuels. It also leads to reduce oxidation reaction in catalyst due to the lack of oxygen, resulting in reducing exhaust and catalyst temperatures. In such cases, however, three-way catalyst won’t work and emissions will worsen. (As a result, CO emissions drastically increase).
<number>
Notes: <number>

## Slide 4: Engine Protection Region
<number>
２．Rareness of the driving under the engine protection region
According to our study, engine protection region for specific major vehicles was observed in rare case even when intentionally driving on many steep slopes in Tokyo.
On the other hand, these vehicles came under the engine protection region at many points of WLTC ver.5.
In this sense, the cycle is far from representative cycle of usual conditions for specific major vehicles.

## Slide 5
<number>
Total
4,210,219
(100%)
Passenger Vehicles
3,524,788
(83.7%)
1,138,752
(27.0%)
382,393
(9.1%)
Commercial Vehicles
674,780
(16.0%)
Assessment of the impacts in market
About 40% of total vehicles in Japan are estimated to be tested with the “engine protection region” in WLTC-ver.5.
Total domestic sales of new vehicles in Japan (FY2011)
Number of vehicles owned in Japan (FY2011)
Total
75,512,887
(100%)
Passenger Vehicles
58,670,314
(77.7%)
18,486,738
(24.5%)
8,963,641
(11.9%)
Commercial Vehicles
14,970,422
(19.8%)

## Slide 6
Vehicle No. | A1 | A2 | A3 | A4 | B | C
Vehicle category | PC | PC | PC | PC | PC | PC
Fuel type | Petrol | Petrol | Petrol | Petrol | Petrol | Petrol
Engine capacity (cc) | 658 | 658 | 658 | 658 | 658 | 658
Max. rated power (kW) | 40 / 6500 | 40 / 6500 | 40 / 6500 | 40 / 6500 | 38 / 6800 | 38 / 6800
Curb vehicle mass (kg) | 670 (assumed) | 780 | 890 | 1000 | 790 | 970
Test mass (kg) | 800 | 910 | 1020 | 1130 | 900 | 1106
Gross vehicle mass (kg) | 890 | 1000 | 1110 | 1220 | 1090 | 1270
Power to mass ratio (KW/t) (Curb mass basis) | 59.7 | 51.3 | 44.9 | 40.0 | 48.1 | 39.2
After treatment | TWC | TWC | TWC | TWC | TWC | TWC
Emission standard | 2005 | 2005 | 2005 | 2005 | 2005 | 2005
Transmission | CVT | CVT | CVT | CVT | CVT | CVT
Test vehicles (PC)
<number>

## Slide 7
Vehicle No. | D1 | D2 | D3 | D4 | D5 | E
Vehicle category | LDCV | LDCV | LDCV | LDCV | LCVD | LDCV
Fuel type | Petrol | Petrol | Petrol | Petrol | Petrol | Petrol
Engine capacity (cc) | 658 | 658 | 658 | 658 | 658 | 658
Max. rated power (kW) | 36/ 5800 | 36/ 5800 | 36/ 5800 | 36/ 5800 | 36/ 5800 | 39 / 7000
Curb vehicle mass (kg) | 560 (assumed) | 670 | 780 | 870 | 990 | 970
Test mass (kg) | 800 | 910 | 1020 | 1130 | 1250 | 1232
Gross vehicle mass (kg) | 1060 | 1170 | 1280 | 1420 | 1540 | 1520
Power to mass ratio (KW/t) (Curb mass basis) | 64.3 | 53.7 | 46.2 | 41.4 | 36.4 | 40.2
After treatment | TWC | TWC | TWC | TWC | TWC | TWC
Emission standard | 2005 | 2005 | 2005 | 2005 | 2005 | 2005
Transmission | 3AT | 3AT | 3AT | 3AT | 3AT | 4AT
Test vehicles (LDCV)
<number>

## Slide 8: Test Results PC
<number>

## Slide 9: Test Results PC
<number>

## Slide 10: Test Results LDCV
<number>

## Slide 11: Test Results LDCV
<number>

## Slide 12: Test Results LDCV
<number>

## Slide 13: Japanese Proposal
9 points for modification
WLTC-ver.5
modified (ver.5.1)
<number>

## Slide 14: Characteristics of Ver.5 & Ver.5.1
 | Driving distance (km) | Driving time (s) | Average speed (km/h) | Maximum speed (km/h) | Maximum acceleration (km/h/s) | Average positive acceleration (*1) (m/s2) | Average positive acceleration*speed (*1) (m2/s3) | RPA (m/s2) | Relative workload (*2)
Middle Phase |  |  |  |  |  |  |  |  | 
Ver.5 | 4.756 | 433 | 39.54 | 76.60 | 5.65 | 0.4640 | 4.755 | 0.1950 | 1.000
Ver.5.1 | 4.717 | 433 | 39.22 | 76.60 | 4.60 | 0.4300 | 4.359 | 0.1894 | 0.986
High Phase |  |  |  |  |  |  |  |  | 
Ver.5 | 7.158 | 455 | 56.63 | 97.40 | 5.7 | 0.5053 | 6.092 | 0.1328 | 1.000
Ver.5.1 | 7.124 | 455 | 56.24 | 97.40 | 5.7 | 0.4018 | 4.634 | 0.1177 | 0.988
*2:Relative workload per unit mileage. A negative value is calculated as zero.
(example of trial calculation in 1.5L passenger car)
*1:It calculates for acceleration>0.05m/s2.
<number>