## Slide 1: Concept for introducing the Weighting Factors for L/M/H/ExH phase
Prepared by Japan
13th DHC group
under GRPE/WLTP informal group
5 June 2012
the Palais des Nations (Geneva/Switzerland)
WLTP-DHC-13-05

## Slide 2: Introducing Weighting Factors
<number>
The proportions of each phase are different among countries/regions.
In order to adjust the proportions into the actual traffic conditions in each countries/regions, the ratios of each phases (“Weighting Factors”) should be introduced.
WLTC-ver.5
(Validation 2 is currently being conducted.)
“Weighting Factors” was listed as one of the “Open Issues” at the 62nd GRPE meeting in June 2011. But, this issue has not been discussed well yet.

## Slide 3: What is the Weighting Factors?
The test procedure(including cycle) is one and only in the world.
Fuel
consumption:○○L/100km
NOx:○○g/km
Fuel
consumption:○○L/100km
NOx:○○g/km
Fuel
consumption:○○L/100km
NOx:○○g/km
Fuel
consumption:○○L/100km
NOx:○○g/km
×α%
×β%
×γ%
×δ%
Test results measured according to the WLTP
Weighting Factors =Weighted by some coefficients in each phase
Fuel consumption:○○L/100km
NOx:○○g/km
<number>

## Slide 4: Why Weighting Factors are needed?
Calculation of chi-square value in speed/acceleration distribution to compare WLTC-ver.5 with each country data.
Japan
EU
The gap between WLTC and Japan (as well as India and Korea) is wider than that of EU and US.
How can we describe the local characteristics with WLTC?
India
ｒ: Region



<number>
Korea
US



## Slide 5: Calculation method of the Weighting Factors
STEP 1: Convergence calculation of time proportions which give the least chi-square value in speed/acceleration distribution.
TPL
TPM
TPH
TPExH
the least
χ2 value
Weighted WLTC
JP unified distribution
<number>

## Slide 6: Calculation method of the Weighting Factors
STEP 2: Conversion of time proportion to distance proportion (= Weighting Factors)
【Calculation for Japanese WF】
(Ref.) Calculation for WF in other region
Weighting Factors[%] | L | M | H | ExH | 
EU | 13.4 | 28.9 | 30.3 | 27.4 | 
India | 34.9 | 47.4 | 17.7 | 0.0 | 
Korea | 22.4 | 37.7 | 39.6 | 0.3 | 
US | 4.2 | 31.5 | 41.0 | 23.3 | 
 |  | L | M | H | ExH | Total
1 | Time Proportion | 0.392 | 0.511 | 0.096 | 0.001 | 1
2 | Mean Speed of WLTC | 18.9 | 39.5 | 56.6 | 92.0 | -
3 | Distance Coverage(=1×2) | 7.41 | 20.21 | 5.44 | 0.09 | 33.15
 | Distance proportion (= Weighting Factors)[%] | 22.4 | 61.0 | 16.4 | 0.3 | (100)
Ref. | Distance proportion of WLTC [%] | 13.3 | 20.5 | 30.8 | 35.5 | (100)



<number>



## Slide 7
Fuel consumption (L/100km)
 |  | L | M | H | ExH | Total
1. WLTC |  | 6.090 | 4.983 | 4.760 | 5.970 | 5.417
2. WF[%] |  | 22.4 | 61.0 | 16.4 | 0.3 | (100)
1×2 |  | 1.36 | 3.04 | 0.78 | 0.02 | 5.200
Carbon monoxide (g/km)
(L/100km)
(g/km)
 |  | L | M | H | ExH | Total
1. WLTC |  | 0.098 | 0.028 | 0.084 | 0.628 | 0.268
2. WF[%] |  | 22.4 | 61.0 | 16.4 | 0.3 | (100)
1×2 |  | 0.022 | 0.017 | 0.014 | 0.002 | 0.055
(Ref) Calculation of fuel consumption and emission
<number>