## Slide 1: Combined approach for vehicle test weight, stepless inertia and vehicle selection
18 January 2012
DTP meeting Geneva
Revised proposal by
The Netherlands (Andre Rijnders ), T&E (Iddo Riemersma) and ICCT (Peter Mock)
WLTP-DTC-08-04

## Slide 2: General consideration
WLTP objective: representative fuel consumption / CO2 value
This requires:
A representative vehicle in a representative test
Representative test mass definition and vehicle selection
Conditions:
Applicable and verifiable at type approval
Limited test burden
Level playing field and sound against wrong incentives
Similar approach for all vehicle models, categories and types

## Slide 3: Vehicle test mass definition
Problem:
How to define representative vehicle test mass?
Approach:
Take the unladen mass of the vehicle
Add representative mass for vehicle options
Identify constant and variable mass contributions
Relate variable mass contribution to the remaining load capacity of the vehicle.

## Slide 4: Vehicle test mass definition
Option equip.
Remaining loading capacity
LM
M1 vehicles
Unladen mass
Vehicle test mass
100 kg
Driver Luggage
Extra luggage or passengers
Vehicle test mass is the unladen vehicle mass (UM) plus mass of vehicle options (OM) + 100 kg + 15% of remaining difference with LM
Test mass = UM + OMREP + 100 + 0.15 (LM – RM)
15%
LM-RM
RM
Constant mass contribution: 100 kg
Variable mass contribution: 15% of (LM – RM)

## Slide 5: Vehicle test mass for N1 vehicles
Option equip.
Body work mass
Remaining loading capacity
LM
N1 vehicles
Unladen mass
Vehicle test mass
100 kg
Discussion necessary for multi stage vehicles
Driver Luggage
Passengers
Average
Payload
Vehicle test mass is the unladen vehicle mass (UM) plus mass of vehicle options (OM) + 100 kg + 35% of remaining difference with LM
Test mass = UM + OMREP + 100 + 0.35 (LM – RM)
35%
LM-RM
RM
Same approach chosen as for M1 vehicles
Same constant mass of 100 kg
Variable added mass based on AEA report, results in 35% of (LM – RM)

## Slide 6: Representative mass for vehicle options
Problem: How to define representative mass for vehicle options?
Approach:
Define best case and worst case test mass (vehicle with no options and vehicle with full options)
Interpolation based on actual vehicle weight (assuming linear relation between mass and CO2)
Note: Emission compliance only demonstrated at worst case vehicle

## Slide 7: Representative vehicle selection
Problem: How to select a representative vehicle for road load determination?
Approach:
Road load is dependent of vehicle options
Determine road load at worst case vehicle, and optionally at best case vehicle (at choice of manufacturer)
Interpolation based on actual vehicle weight (assuming linear relation between mass and CO2)

## Slide 8: Combined approach
<number>
CO2
kg
UM = unladen mass (empty vehicle)
+ 15% of LM-RMH
OMH = unladen mass + mass of all available optional equipment
LM = laden mass, gross vehicle weight
TMH = test mass
UM
+ 100 kg
+ 15% of LM-RMH
TML
modeled
vehicles
TMH used for:
non-CO2-emissions (worst-case)
CO2 emissions (upper value for regression line)
coastdown
TML used for:
CO2 emissions (lower value for regression)
coastdown (optional, OEM choice)
extrapolation allowed up to [50 kg]
(in case that additional options added later)
RMH (heaviest vehicle reference mass)
+ 100 kg
Stepless inertia: Best and worst case vehicle tested at their defined test masses Interpolation for vehicles in between

## Slide 9: Conclusions
Advantages:
More representative vehicle test mass (actual mass of optional equipment, actual loading capacity considered)
Same definition applicable for all vehicle models, types and categories (M1 and N1)
Test mass also considers vehicle construction features and design
Improved representativity of road load values
More accurate and vehicle specific CO2 values
Disadvantages:
Administration of masses for individual vehicles needed
CO2 performance depends on customer’s choice

## Slide 10
End of presentation

## Slide 11: Defining representative vehicle mass
Total vehicle mass is considered to be composed of:
Unladen mass
Optional equipment (factory installed)
Optional equipment (after sales, owner installed)
Driver mass
Passengers mass
Luggage / Payload
These mass contributions can be:
Constant (vehicle independant)
Variable (dependant of vehicle construction and design)
Approach to define representative vehicle mass:
Estimate each individual contribution (constant and variable)

## Slide 12: Defining representative vehicle test mass
 | Constant | Variable (payload dependent)
Unladen mass | Actual mass | 
Optional equipment (factory installed) | Actual mass | 
Owner installed equipment (after sales) | 5 kg | 0 kg
Driver | 75 kg | 0 kg
Passengers | 0 kg | 0 to 60 kg
Luggage / Payload | 20 kg | 0 to 40 kg
Total | 100 kg | 0 to 100 kg
Variable mass translates on average in 15% of (LM-RM) for M1 vehicles