## Slide 1
Position paper on Mode Construction during Validation 2
Prepared by OICA
DHC/DTP group
under GRPE/WLTP informal group
Geneva 17.01.2012
Draft
WLTP-DTC-08-06

## Slide 2
5. Mode Construction Proposal during Validation2
This document represents the position of OICA working groups on WLTP mode construction for presentation at DHC11 at the GRPE Meeting January 2012 in Geneva.
The proposal covers the mode construction for conventional vehicle with options to be tested in Validation 2.
Mode construction for electrified vehicles provides procedures for determination of electrical range, for charge depleting (CD) and charge sustaining (CS) test procedures
Draft

## Slide 3
[ Coventional Vehicles, Baseline test - Cold start -]
LOW
589s
MIDDLE
433s
6 – 36 h Soak
preconditioning
HIGH
455s
Ex-HIGH
323s
preconditioning
Charge
Starter Batteries
LOW
589s
MIDDLE
433s
HIGH
455s
Ex-HIGH
323s
Sample#1
RCB#1
Sample#2
RCB#2
Sample#3
RCB#3
Sample#4
RCB#4
HIGH
455s
Ex-HIGH
323s
Sample#1
RCB#1
Sample#2
RCB#2
Note1) in case 4 bags sampling is not available,
HIGH and Ex-HIGH phases can be executed separately.
LOW
589s
MIDDLE
433s
No sampling
No RCB
After completion of
L&M analysis
Note2) Cycle phase to be driven
Vehicle maximum speed | Less than 60km/h | Less than 80km/h | Less than 110km/h | others
Cycle phase(s) | LOW | LOW and MIDDLE | LOW, MIDDLE and HIGH | ALL
5. Mode Construction Proposal during Validation2
1 PM-Filter for all 4 phases, some labs to measure 2 Filters (L+M, HxH), SoC for each phase separately
1 PM-Filter for all 4 phases, some labs to measure 2 Filters (L+M, HxH), SoC for each phase separately
Draft

## Slide 4
[ Baseline test - Hot start -] Optional
LOW
589s
MIDDLE
433s
No intermediate soak is required
preconditioning
Charge
Starter Batteries
LOW
589s
MIDDLE
433s
Sample#1
RCB#1
Sample#2
RCB#2
Note1) some of laboratories will be required to run the intermediate soak study ( i.e. 0, 5, 10 and more )
Note2) Cycle phase to be driven
Note3) In case hot start test is conducted after cold start test, starter battery charge shall be omitted. Soak for equipment preparation before preconditioning phases.
Vehicle maximum speed | Less than 60km/h | others
Cycle phase(s) | LOW | LOW and MIDDLE
5. Mode Construction Proposal during Validation2
1 PM- Filter for last 2 phases, SoC for each phase separately
Draft

## Slide 5
[ Ki determination ]
LOW
589s
HIGH
455s
MIDDLE
433s
Ex-HIGH
323s
Loading cycle
Baseline test
- Cold start -
Baseline test
- Cold start -
Continue to run until regeneration was completed
5. Mode Construction Proposal during Validation2
Note1) Cycle phase to be driven
Vehicle maximum speed | Less than 60km/h | Less than 80km/h | Less than 110km/h | others
Cycle phase(s) | LOW | LOW and MIDDLE | LOW, MIDDLE and HIGH | ALL
Draft

## Slide 6
5. Mode Construction Proposal during Validation2
[ Mode Construction for electrified Vehicles – CD,CS, Electrical range ]
Draft
A series of Low cycles shall be validated, additionaly
A series of Low+ Middle cycles shall be validated

## Slide 7
5. Mode Construction Proposal during Validation2
[ Mode Construction for electrified Vehicles – Thinkable options in case that a hot start test is required. For that case, the procedure should be also validated for the RCB correction factor determination during VP2]
]
Draft