## Slide 1
slide <number>
Progress Report
DTP Subgroup
Lab Process Internal Combustion Engines
(LabProcICE)
Geneva, 18.1.2012
WLTP-DTC-08-07
Notes: <number>

## Slide 2
slide <number>
State of the working progress
Issues on DTP level
Input for validation 2
4) Work in progress items / proposals / open issues
5) Next steps
Overview

## Slide 3
slide <number>
several dates Draft working team meetings
26.10.2011 Telephone Conference
22. – 23.11.2011 Brussels workshop
1.1) Meetings since DTP 7 September 2011

## Slide 4
slide <number>
Open issues list
has been updated (LabProcICE-111)
GTR draft
has been updated, incl. Subgroup AP (LabProcICE-112)
Definitions
- overview definition term list (LabProcICE-049rev1)
detailed definition list (LabProcICE-050)
 Review postponed, coordination by Draft Coordinator expected
1.2) OIL, gtr draft, definitions

## Slide 5
slide <number>
State of the working progress
Issues on DTP level
Input for validation 2
4) Work in progress items / proposals / open issues
5) Next steps
Overview

## Slide 6
slide <number>
Test Room and Soak Area Temperature
DTP7 decision for validation phase 2:
soak and test temperature: 25 °C
note: final decision still open (EC proposal 22 °C)
recommandation: some labs should conduct tests at lower temperatures
target tolerance of the actual value: +/- 2 °C
 evaluation of technical feasibility

## Slide 7
slide <number>
Principle: Using a setpoint and monitoring of actual value in 3 phases (see LabProcICE-107rev1)

## Slide 8
slide <number>
Method for subtraction of pollutant mass in intake air
(LabProcICE-020)
Aim: measure low pollutant mass with higher accuracy by considering the pollutant level that is contained in the combustion and intake air of the vehicle
Concerns by US EPA / Japan
 Issue is put on hold until results of validation and correlation show the clear need and effect of the proposed method

## Slide 9
slide <number>
Vehicle test mass & Inertia classes
DTP7:
combined solution, see WLTP-DTP-07-12 by NL, T&E and icct
improved definition of vehicle test mass (more representative by taking into account optional equipment, luggage/payload)
substitution of current inertia system by step-less inertia approach (more representative CO2 result for individual vehicle)
Approach needs to be discussed in connection with
family concepts (gtr and/or regional)

## Slide 10
slide <number>
Validation 2:  mandatory testing with TMH (mass of the vehicle (with all optional equipment)
TMH and TML (without optional equipment) only recommended at some labs VTF: practicability during Validation 2 questioned
N1 payload discussion [loading factor 35%]
 see LabProcICE-094 (justification for vehicle test mass)
DTP8: updated combined proposal for vehicle test mass, inertia classes and vehicle selection
 DTP-08-02, DTP-08-04 by T&E, NL, icct

## Slide 11
slide <number>
Vehicle selection RLD
- optional body parts influencing the aerodynamics - design trims, wheel rims
(a) Sales volume based approach (LabProcICE)
 fitting criteria: exceeds 50% of the sales volume
 improved representativity
(b) Worst case criteria (counterproposal Japan)
Alternative solution:
testing worst case and in addition best case (if requested by manufacturer)
 in line with test mass approach + covers Japanese proposal

## Slide 12
slide <number>
Multimode gear boxes
Emissions testing proposal:  Test agreed worst case  Compliance with emissions standards in all modes  Exemptions for modes used in very limited conditions
CO2 / FE testing proposal:
(a) Single default mode  test default mode
(b) No default mode or multi default modes  test best and worst case, average results of both modes Note: Japan has withdrawn counterproposal to test & average all modes
Additional provisions:
Manufacturer shall give evidence to authority about the emission and fuel economy in the different modes  validation 2: test all modes in case of no default mode
- Tested options be provided in test report, e.g. for In-Service-testing

## Slide 13
slide <number>
Open issues:
- Definitions need to be rediscussed/specified
 mode, default mode, multi-mode etc
 ACEA / JAMA will prepare overview of concepts of (default) modes
- adaptive or „self-learning“ systems
____________________________________________________
GSI
To be tested in validation 2 (if available)  LabProcICE will provide test procedure
Open issues:
Test GSI and/or fixed gear shift points in gtr? GSI as multimode?
 certification issue? GSI currently only mandatory in EU.

## Slide 14
slide <number>
State of the working progress
Issues on DTP level
Input for validation 2
4) Work in progress items / proposals / open issues
5) Next steps
Overview

## Slide 15
slide <number>
Updated parameter list: LabProcICE-100rev1
 Major amendments since DTP 7:
temperature requirements (setpoint, continously monitoring)
Tolerance of speed trace (+-2 km/h)
Test mass and inertia approach
Multimode and GSI requirements
Road Load Determination - excluded from validation phase 2 - general need for validation?  JAMA yes. Feedback of ACEA RLD experts expected
- gtr changes to ISO are relevant for regional correlation exercises
LabProcICE parameter setting for validation 2

## Slide 16
slide <number>
Excel data sheet for reporting of results (by Heinz Steven)
 revision: LabProcICE-101rev1
Assessment Criteria (LabProcICE-102rev1):
1. Objectives (what do we want)
2. Assessment Parameter (what to look for)
3. Assessment Criteria (how to judge)
Mode Construction
review of DHC proposals by DTP experts (LabProcICE/EV)
 last draft proposal
Further Working Documents for Validation 2:

## Slide 17
slide <number>
State of the working progress
Issues on DTP level
Input for validation 2
4) Work in progress items / proposals / open issues
5) Next steps
Overview

## Slide 18
slide <number>
  RLD - Tyre Selection Criteria
  selection based on 6 rolling resistances classes according to EU Tyre Labelling Regulation 1222/2009.
  RR measured acc. to ECE-R117.
  Tyres in the worst rolling resistance classes shall be chosen for road load determination. If tyres from more than three rolling resistance classes are specified for the vehicle, tyres from the second worst rolling resistance class shall be chosen.
  DTP 7:
   Re-definition of classes necessary?
  LabProcICE proposal:
   No need for refinement  Proposal confirmed

## Slide 19
slide <number>
RLD – Coast down mode
Reasoning: Parasitic drags during vehicle coast down (e.g. regenerative braking) would distort the road load data
 no realistic/representative evaluation of driving resistance
LabProcICE & EV proposal for definition and application of coast
down mode  LabProcICE-106 (note: details to be reviewed)
Definition:
“Vehicle coast down mode means a special mode of operation for example where drivetrain components are mechanically decoupled from the wheels and/or electrically controlled which enables an accurate and repeatable road load determination and an accurate dyno setting when using the coastdown method.”

## Slide 20
slide <number>
- Mode shall only be engaged for coast down (on the road or chassis
dynamometer).
- The vehicle coast down mode shall not act as a defeat device.
Application requirements – 3 step-approach:
tolerances specified for coasting down of conventional vehicles should apply equally to electrified vehicles
2. equivalence of the coast down determination on the road and on the dyno to be shown
3. mode shall be used if a vehicle can not meet the tolerance range set for dyno load setting or can not show the equivalence

## Slide 21
slide <number>
LabProc - Monitoring of Battery SoC
Position of DTP:
The energy content of all batteries has to be considered for determination of CO2 and energy consumption in the test cycle.
Agreed by DTP6:
- apply conditioning test cycle with fully charged battery
- battery shall not be charged again before the emission testing
Proposal: (based on LabProcICE-056rev2 /-081):
- Monitoring of energy difference during test
- Comparison with energy of consumed fuel during test
- Correction of CO2 value if energy difference exceeds certain threshold

## Slide 22
slide <number>
Validation phase 2
 check of feasibility
Open questions:
- Closed compartment during cycle causes high temperature load on measurement clamps
- Correction of CO2 value is unsure due to CO2 measurement tolerances.

## Slide 23
slide <number>
ME – 40 CFR Part 1066 - Succeeding legislation for current US regulation (40 CFR part 86) - Issues of the HDV legislation (40 CFR part 1065) shall be adopted for LDV legislation - Final rulemaking planned for late 2012
Main issues – harmonization, time consuming, invest: - New hardware needed for PM-measurement (filterholder …)
- New checks required (hardware/software)  Several analyser checks have to be done at a concentration „expected at the standard“  Additional interference checks for N2O, CO2 analysers  NOx quench check  Additional leak checks in the CVS system

## Slide 24: Further steps: LabProcICE experts will continuously cross-check development of Part 1066 and gtr Open questions: - How to deal with major differences in future? - To what extent is disharmonization with US legislation acceptable?

## Slide 25
Other issues
DTP-07-13 by Poland (comments on the measurement methods of hydrocarbons emissions according to Regulation 83.06)  check by LabProcICE ME experts  also relevant for GFV Informal Group
Other open issues see OIL LabProcICE-111  feedback/proposals on any of the listed items or on the gtr draft LabProcICE-112 are welcomed!

## Slide 26
slide <number>
State of the working progress
Issues on DTP level
Input for validation 2
4) Work in progress items / proposals / open issues
5) Next steps
Overview

## Slide 27
slide <number>
Small teams (LabProc, ME, RLD) will continue work on draft gtr / OIL / definitions
Additional Tel/web conferences, e. g. ME experts (check of Part 1066)
Evaluation of new test procedure during Validation Phase 2
Next face-to-face workshop: planned in March 2012, Brussels

## Slide 28
slide <number>
Thanks for your attention.
LabProcICE contact:
Béatrice Lopez de Rodas - beatrice.lopez(at)utac.com
Konrad Kolesa - konrad.kolesa(at)audi.de
Stephan Redmann – stephan.redmann(at)bmvbs.bund.de