## Slide 1: WLTP-E-Lab Sub Group Progress report WLTP-DTP-E-LabProc-053
Leader: Per Ohlund / Kazuki Kobayashi
WLTP-DTC-08-12

## Slide 2: Open issues
11 open Issues are
To be discussed 2 (UF, Battery charging time) =>To be discussed during V2
Depends on new cycle 1 ( AE city for Low speed EV) => To be discussed during V2
Depends on Validation results 5 (ex,EV range, CD /CS test,)=>TBD after V2
Follow ICE group 3 (R/L, multi gear box,)
The Issues to be validated are listed on parameter setting list.
The procedure for validation phase 2 are shown next.

## Slide 3: Consideration items on E-Lab. Gr.
Day 1
Day 2 (EV: Day 1)
Day 3 (EV: Day 2)
Battery condition [Ah}
Precondition
Drain & Fill
Soak 6hr
Pre-con cycle
Soak 12~36 hr
Canister loading
Confirm tire pressure
Prepare RCB measurement
Discharge
WLTC×1
Charge sustaining (CS) mode test (cold)
Full charge
max. 12 hr
⊿E
within 1hr
Plug OFF
WLTC×n
Charge depleting (CD) mode test
WLTC×1
(Drain & Fill)
Soak 12~36 hr
⊿E
AER
EAER
RCDR
Full charge
Charging voltage
100 / 200V (PL12)
End of charge
criteria (PL1)
Order of CD/CS
(PL4)
Interruption
condition (PL5)
RCB break off
criteria (PL2/9)
Termination condition
for EV range (PL6/7)
Charge sustaining (CS) mode test (hot)
Prepare RCB measurement
CO2/FC calculation
(PL8/10)
Performance of
Watt-hour meter,
Am-meter (PL3)
Multi mode
gear box
(PL11)
◆Test flow (independent test for L/M/H/ExH)
Confirm
tire pressure
*) EAER: Equivalent All Electric Range
*) RCDR: Charge Depleting Range
*) NEC: Net Energy Change = RCB * nominal voltage of RESS
*) RCB: RESS Charge Balance (=SOC)
*) RESS: Rechargeable energy storage system
*) AER: All Electric Range

## Slide 4: PL1. End of charge criteria
Back ground：
  ACEA proposal: Starting within 1 hour from “plug-off”
  Japanese proposal: ”from charge completed”
How to：
  Monitoring RCB fluctuation after charge complete
  CD test：2（max/minimum charging）×4 phase（L/M/H/ExH）×3 times
  Impact of battery type ？ (Ni-MH /Lithium，，)
Measurement parameter：
  RCB（Voltage/electric current & CAN）
Test equipment ：
  RCB measurement system
Charge complete
Plug off
CD test start
1hr
fluctuation
CS test
CD test
WANTED! Participant!
Laboratory ,manufacture

## Slide 5: PL2/9. RCB break off criteria
Back ground：
  RCB Break off Criteria (CD→CS)
How to：
  Comparing 2 calculation result by each procedure
  CDtest：4phase（L/M/H/ExH）×3times
Measurement parameter：
  RCB，Fuel Consumption， total Energy demand at wheels to perform the cycle based on the theoretical profile of the WLTC
Test equipment：
  RCB measurement system
CS mode
CD mode
To be analyzed : a relative NEC:
1) (RCB x Nominal Voltage of the battery) / (RCB x Nominal Voltage of the battery + Energy of the Fuel)
2) (RCB x Nominal Voltage of the battery) / (total Energy demand at wheels to perform the cycle based on the theoretical profile of the WLTC)
or an absolute NEC : RCB x Nominal Voltage of the battery
*) RCB: RESS Charge Balance (=SOC)
*) RESS: Rechargeable energy storage system
*) NEC: Net Energy Change = RCB * nominal voltage of RESS
WANTED! Participant!
Laboratory ,manufacture

## Slide 6: PL4. Order of CD/CS test
Back ground：
  Confirm impact the order of CD/CS test
  Soak -CS test –Charge or CD test –shifting CS mode-Charge
  For example the temperature impact around Battery
How to：
  CD&CS test：4phase（L/M/H/ExH）×3times
Measurement parameter：
  RCB（Voltage/Electric current & CAN& temperature Battery or any other electrical parts）
Test equipment：
  RCB measurement system

## Slide 7: PL6/7. Termination condition for EV range (EV)
Back ground：
Japan：the deviation occurs not more than once within 4 second
US：more than 2 second
Europe：Target more than 50km/h：Below 50km/h，
Target Less than 50km/h：more than 5s 6times during 1 hour
How to：
  Running until completely stop and calculate EV range by each procedure
  Compare each result
  EV range test：4Phase（L/M/H/ExH）
Measurement parameter：
  RCB（Voltage/electric current & CAN）,Distance
Test equipment：
  RCB measurement system

## Slide 8: PL6/7. Termination condition for EV range (OVC HEV)
Back Ground：
  To compare PHEV and Range Extender
  How to：
  Confirmation test procedure for range extender
  Compare with PHEV
  CD& CS test：4phase（L/M/H/ExH）×3times
Measurement parameter：
  RCB（Voltage/Electric current & CAN）
Test equipment：
  RCB measurement system
WANTED! Participant!
Laboratory ,manufacture
Especially Range extender manufacture

## Slide 9: PL12. Charging voltage 100 / 200V
Back ground：
  Charging voltage has impact for charging efficiency.
  There are several Voltage in all of the world.
  US:110-120V,Japan:100/200V.EU:220-240V(127V)
How to ：
  Measure Charging time，Fluctuation during Plug ON，impact for CS/CD test result,Electric Range.
  PHEV:CD test：each Voltage×4phase（L/M/H/ExH）×3times
  EV: Electric range :Each Voltage × 4phase（L/M/H/ExH） ×3times
Measurement parameter：
  RCB（Voltage & CAN）
Test equipment ：
  RCB measurement system
Japan conducted pre-validation 2
How do we treat the difference of Voltage of each region?

## Slide 10
WLTP DTP
Lab Process-EV sub group
(Pre-Validation2)
NTSEL Japan
16th January
<number>

## Slide 11
Vehicle weight
Motor
Drive
battery
Control system
Driving method
Type
Max. output
Max. torque
Max. speed
Type
Rated voltage
Rated capacity
[kg]
[kW/min-1]
[Nm/min-1]
[min-1]
[V]
[kWh]
1,100
Permanent magnet
synchronous motor
47 / 3,000 ～ 6,000
180 / 0 ～ 2,000
8,500
Lithium-ion cells
330
16
Inverter control
Rear-wheel drive
2009 years model
Vehicle spec.
Vehicle condition (12/2011)
Odometer : 5269 km
Non-blended regenerative brake system
<number>

## Slide 12
System configuration
<number>

## Slide 13
Operation room
Vehicle test room
Chassis dynamometer
<Dynamo meter （Fr or Rr or 4WD）>
Alternating current system
・Absorption power : 220kW
・Motoring power : 200kW
Electrical inertia method
・2WD total : 570 – 2750 kg
・4WD total : 800 – 3500 kg
<MEIDACS – DY6200P>
<number>

## Slide 14
CAN monitor
Prove
Measurement machine
Rear
Front
・Vehicle speed
・Battery voltage
・Motor current
・Accessory current
・Air-conditioner / Heater current
・Outdoor / Room temperature
Connector
Data logger
PC
telecommunication
equipment
<number>

## Slide 15
Measurement item
・WLTP (WLTC v3 HS1127)
・JC08
Driving mode
・Range
・ Energy consumption rate
・ Acceleration / Break pedal
opening rate
Measured items
Time [sec]
Velocity [km/h]
150
1800
0
600
1200
0
50
100
Velocity [km/h]
150
0
50
100
JC08
WLTP
Test cycle
・Full Charging time
5.5 hours @ 200V
12.4hours @100V
・Driving time
3.0 hour @ WLTP
6.5 hour @ JC08
Plug off
Driving
Day1
Day2
Battery SOC
revel [%]
Fully charged
Charging
Plug off
Fully charged
Driving
Charging
<number>

## Slide 16
Test result (WLTP vs. JC08)
 | WLTP (23.112km) | JC08 (8.172km)
Range [km] | 101 | 129
Energy consumption rate [Wh/km] (Supplied energy from an outlet for charging) | 147 (14.8kWh@AC200V) | 115 (14.9kWh@AC200V)
<number>
Motor
Battery
Measurement point of
energy consumption

## Slide 17
Test result (energy consumption of L,M,H,ex-H in WLTP)
Parts in WLTP (Range A km) | Low (3.06) | Mid (4.74) | Hi (7.06) | Ex-High (8.25)
Energy consumption : Y [kWh] | 0.29 | 0.50 | 0.76 | 1.11
Assumed range : X [km] | 137 | 123 | 120 | 97
Motor
Battery
Measurement point of
energy consumption
“Assumed range” is a range that was calculated on the assumption that
the test vehicle was frequently driven in each part of the WLTP.
Definition ⇒ X = (13/Y) × A
13kWh: Fully charged energy in the battery
<number>

## Slide 18
Test result (AC200V vs. AC100V in a charge)
Charging voltage | AC200V | AC100V
Range [km] | 101 | 106
supplied energy from an outlet for charging [kWh] | 14.8 | 16.9
Electric energy consumption rate (WLTC v3 HS1127) [Wh/km] | 147 | 159
<number>

## Slide 19
Proposed actions for gtr development
 | 2011 11 12 | 2012 1 3 6 9 12 | 2013 1 3 6 9 12
E-Lab action |  |  | 
Validation 2 Confirmation Round Robin |  |  | 
test sequence
WLTC completed
Validation 2
Round Robin
Draft gtr2
Modify gtr
reflection
[ Background ]
1. Draft gtr 1 is the portion exclude Validation phase 2.
2. Some of open issues need to be evaluated during the validation program.
3. Draft gtr 2 is reflected the result of Validation 2 .
Parameter set
Short V1
Draft gtr1
Procedure for V2
Confirmation
F2F

## Slide 20: Appendix：Open issues
Green color means “agreed or deleted”
Red color means “to be discussed “.
Blue color means” to be confirmed in Validation phase 2”.
Under line means “changed from last DTP in Geneva”.
These under lined issues will be reported today.

## Slide 21
Proposal
Step 3 Charge Sustaining Mode
Unknown SOC
 | operation switch | initial discharge | pre-conditioning | Soak time | Charge sustaining test | Charging OIL No.8 Charging method
EV | n/a | n/a | n/a | n/a | n/a | ConsumptiontestOILNo.2 Charging time: OIL No.9 Condition: OIL No.7 end of charge :OIL No.10,10bis
OVC HEV | without | OIL No.14 discharge condition MR | follow ICE | follow ICE | OIL No.26,27 RCB correction Ex; correct emission? | 
 | With |  |  |  |  | 
 | With |  |  |  |  | 
NOVC HEV | Without | n/a | follow ICE | follow ICE |  | n/a
 | with |  |  |  |  | 
 | with |  |  |  |  | 
Cold start of ICE
Charging Condition Battery [Ah]
Performance of Watt-hour meter, Am-meter
OIL No.15,16,17
Validation test

## Slide 22
Proposal
Appendix: RCB Compensation
 | Operation switch | Range test | Pollutants (including AP/PN/PM) |  | CO2/Fuel Consumption | 
 |  |  | CD test | CS test | CD test | CS test
EV | Without | n/a | n/a | n/a | n/a | n/a
OVC HEV | With (incl. pure EV) |  | n/a | OIL26/26bis/27 | n/a | Applicable OIL No.27 To be discussed based on Validation result
 | With (no pure EV) |  |  |  |  | 
 | Without |  |  |  |  | 
NOVC HEV | With (incl. pure EV) |  | n/a | OIL26/26bis/27 | n/a | Applicable OIL No.27 To be discussed based on Validation result
 | With (no pure EV) |  |  |  |  | 
 | Without |  |  |  |  | 
Discharge(+)
Charge(-)
CO2/Fuel consumption/(Emission)
0
∆RCB (Ah)
∆RCB (Ah)
Cycle
Start
End
EU) ECE101 Annex8
Start
±x%of fuel energy?
OIL No.27 RCB correction criteria
RCB Correction for CO2 &FC
OIL No.25bis
How to measure?
Opt.1) Voltage [V]
Opt.2) Current [Ah]
Opt.3) CAN
To be measured by current regulation

## Slide 23
Proposal
Step 3 Charge Sustaining Mode (bis)
OIL.10bis
Charge complete
Plug off
Test start (OIL10)
1hr
End of charge criteria
Validation test

## Slide 24
Proposal
Step4 Charge Depleting Mode
 | operation switch | charging after CS test | Charge depleting test/EV range test OILNo.11Interruption Condition | Charging
EV | n/a | n/a | Test termination Condition OIL No.12 Stop Condition OILNo.13 | Same as Step3
OVC HEV | without | refer to step3 | RCB break off criteria: OIL No.25& 25bis Deceleration condition; OIL No.13bis EAER determination OIL No.21 To be discussed based on validation result. | Same as Step3
 | with |  |  | 
 | with |  |  | 
NOVC HEV | without | n/a | n/a | n/a
 | with |  |  | 
 | with |  |  | 
Test 1
Test 2
CO
2
RCDA calculated with k factor
Driving cycle [/]
All Electric Range
Equivalent All Electric Range
Charge Depleting Range RCDA
Fully Charged
Recharging 12h max
Charging Condition [Ah]
Alternative
(in case of
CD test has
to be
retested) :
ICE
precondition
ing at
chronologica
l separation
from step 1
and 2
Recharge
12h max
First start of ICE
Test n
(transcient)
Test n+1
(needed for
calculations)
36h soak max
1h max from
plug off
charge and
start of CD
CO
2
hot CS
CO
2
Transcient
CO
2
avg CD
Spak
time+
battery
charge
OIL.No31
Low power vehicle
What is Low power vehicle?
How to validate?
To be raised DTP level

## Slide 25
Proposal
Step5: Calculation
 | Operation switch | Pollutants | Fuel Consumption | Electric Energy | Range |  |  |  |  | RCB(DC) | Chaege Duration | others | 
 |  |  |  |  | AER | EAER | Rcda | Rcdc | AERcity |  |  |  | 
EV | n/a | n/a | n/a | applicable | applicable | n/a |  |  |  |  | Applicable |  | 
OVC HEV | Without | applicable | applicable | Applicable | Applicable |  |  |  |  |  |  |  | 
 | With |  |  |  |  |  |  |  |  |  |  |  | 
 | With |  |  |  |  |  |  |  |  |  |  |  | 
NOVC HEV | Without | applicable | applicable | n/a |  |  |  |  |  |  |  |  | 
 | With |  |  |  |  |  |  |  |  |  |  |  | 
 | With |  |  |  |  |  |  |  |  |  |  |  | 
Pollutants :
CO2/Fuel Consumption :
Range :
Detailed calculation formula is developed
based on validation test results.

## Slide 26
Proposal
Appendix: Utility Factor
 | Operation switch | Utility Factor
EV | Without | n/a
OVC HEV | With (incl. pure EV) | OIL. No.1 SAE method is acceptable. But to get the traffic data of all country is too difficult. Political issue what should be discussed in DTP meeting.
 | With (no pure EV) | 
 | Without | 
NOVC HEV | With (incl. pure EV) | n/a
 | With (no pure EV) | 
 | Without | 
OVC range (km)
Utility Factor
25
0.5
1.0
JPN
US
(EU)
US: SAE J1711 with US data JPN: SAE J1711 with JPN data EU: CS weight is 25km (fixed)
OIL No.1: WLTP UF SAE 1711 with Opt.1) based on reagional data Opt.2) based on worldwide data
To be discussed later stage

## Slide 27: Annex: Open issue list 1

## Slide 28: Open issue list2

## Slide 29: Open issue list3

## Slide 30: Open issue list4

## Slide 31: Open issue list5