## Slide 1: WLTP Validation 2
Assessment Criteria
WLTP-DTP-10-06

## Slide 2
DTP subgroup Lab-process ICE

## Slide 3: Inertia Setting
Objective: Clarification of feasibility needed. Handling of stepless inertia setting has to seen in conjunction with certification and family construction
Background：
  Feasibility of stepless setting of inertia on dyno test bench to be tested
How to：
  Evaluate lowest and highest test mass following the parameter stetting advice of subgroup LabProcICE
  Setting of exact value for inertia (kg)
Measurement parameter：
  none
Test equipment：
  dyno test bench

## Slide 4: WLTC Cycle
Objective: Evaluation of gear shifting and clutch pressing time points for optimized activation of start/stop and engine stalling procedures.
Background：
  WLTC is more dynamic than NEDC.
  Clutch pressing points are relevant for activation of start/stop.
  Gear shifting points influence engine stop strategies.
How to：
  Measurement of gear shifting and clutch pressing time points in WLTC
  Monitoring of start/stop
Measurement parameter：
  Time, engine speed, clutch pressing switch, gear shifting
Test equipment：Testbench, data monitoring system

## Slide 5: WLTC Cycle
Objective: Evaluation of OBD monitoring during WLTC.
Background：
  WLTC is more dynamic than NEDC.
  OBD monitoring needs certain conditions for demo testing.
  Real world behaviour is covered by IUMPR.
How to：
  Evaluation of OBD monitoring strategies in WLTC
  Judgement of structural restrictions
  Are future Euro6 threshold covered?
Measurement parameter:
OBD monitoring
Test equipment：Testbench, ECU monitoring system

## Slide 6: Preconditioning Cycle
Objective: Precon as identical cycle as baseline test WLTC facilitates handling of subsequent testing. After the first emission test a precon could be exempted if soak conditions are met.
Background：
  Preconditioning cycle is needed to bring the vehicle in a consistent state.
  Consistency is required for RCB, adaption to reference fuels, etc.
  Battery charging before precon, no charging after precon
How to：
  Measurement preconditioning cycle (L,M, h, xH) with cold start. After precon soak 6(forced cooling down with coolant temperature control), > 12 – 36 h without temp condition.
  Optional testing with fully charged battery and with depleted battery
Measurement parameter：
  Temperature of vehicle at representative locations, RCB, Emissions, temperature of bench, optional temperature of tyres, feasibility of process.
Test equipment：Testbench, emission measurement, temperature monitoring system, RCB monitoring system

## Slide 7: Preconditioning Cycle for Dilution Tunnel
Objective: Dilution tunnel should be in a consistent state before measurement of low particle concentration
Background：
  Preconditioning cycle is needed to bring the dilution tunnel in a consistent state.
  Consistency is required for exact measurement of particulate matter and particle number.
How to：
  Drive vehicle at a constant speed of variable time length (e.g. 10 min at 120 km/h).
  Measurement of particulate matter and particle number before and after test
Measurement parameter：
  Concentration and mass of particulate, time, vehicle speed.
Test equipment：Testbench, emission measurement system

## Slide 8: Soak Temperature Tolerances
Objective: Feasibility of 2 K tolerance to be confirmed.
Background：
  3 phases of temperature
  monitoring (soak, start of test,
  test cell during cycle)
  Setpoint is 25°C, Target
  tolerance of temperature is +- 2 K
How to：
  Measurement of local temperatures in the soak area
Measurement parameter：
  Modal air temperature in various locations, 1 Hz frequency, averaging over 5 min, ambient temperature for comparison
Test equipment：
  Testbench, emission measurement, temperature monitoring system, RCB monitoring system

## Slide 9: Tolerances of dyno load setting
Objective: Tighter tolerances improve reproducibility. Could require enhanced dyno technique in the labs. Feasibility to be confirmed.
Background：
  The road load of vehicles has to be simulated on the dyno for testing in the lab.
  Road load forces are simulated on the dyno following a function in second order.
  Vehicle drags could behave not exactly parabolic over velocity e.g. with automatic transmissions. Therefore certain tolerance for dyno load setting is necessary.
  Evaluation if averaging of multiple coast down times is required.
How to：
  Multiple measurement of coast down times with various vehicle types
Measurement parameter：
  Time, velocity during coast down
Test equipment：Testbench automation system

## Slide 10: Vehicle temperatures during forced cooling down
Objective: 6 h forced cooling down improves lab efficiency. Feasibility of forced cooling down and equivalency to 12 -36 h soak time to be confirmed.
Background：
  Option of minimum soak time 6 h with forced cooling down and vehicle oil within 2 K of setpoint is setout in the gtr
  Location of temperature measurement of vehicle should be representative (engineering judgement)
  For example the temperature inside the compartment, water, oil…
How to：
  Measurement of representative vehicle temperatures during soak time with/without forced cooling down
Measurement parameter：
  Temperature, time,
Test equipment：
  Temperature monitoring system

## Slide 11: Test Cell Temperature Tolerances
Objective: Feasibility of tighter tolerance to be evaluated. Might request enhanced air condition infrastructure. Evaluate worst case conditions.
Background：
  3 phases of temperature monitoring
  (soak, start of test, test cell
  during cycle)
  Setpoint is 25°C, target tolerance
  of temperature is +- 2K
How to：
  Measurement of temperature between outlet of the fan and vehicle
Measurement parameter：
  Modal temperature, 1 Hz frequency, dynamic temperature behavior in phase II (before start of testing)
Test equipment：
  Temperature monitoring system

## Slide 12: Speed Trace Tolerances
Objective: Speed tolerances should be maintained for drivability reasons to allow human driver deviations of target schedule, but with no significant impact on emission results. Feasibility to be confirmed.
Background：
  Target schedule of test cycle has to be followed as closely as possible.
  Tolerances have to be evaluated with various vehicles.
  Target tolerance is -+ 2km/h within 1 sec.
  How to：
  Measurement of actual vehicle speed with min. 1 Hz, comparison with target schedule
Measurement parameter：
  Vehicle speed, time
Test equipment：
  Automation system

## Slide 13: Handling of GSI
Objective: Testing of GSI shifting points could be mandatory in future legislation. Feasibility of handling and problems with WLTC to be evaluated.
Background：
  Shifting points of GSI shall be tested within Validation Phase 2
  Handling and feasibility for driver to be checked
How to：
  Indicate GSI shifting points during test cycle (video?)
Measurement parameter：
  Indicated shifting points of GSI, executed shifting points, vehicle speed trace
Test equipment：
  dyno test bench, GSI monitoring system

## Slide 14: Tolerances of Humidity during Test Cycle
Objective: Tolerance to be confirmed with higher energy input through WLTC
50 % rel. humidity at 25°C could be critical for technical equipment.
Background：
  Tolerance of Humidity depends of technical specification of test cell and test cycle
  Higher thermal load can lead to exceeding of humidity tolerances
How to：
  Measurement of humidity within the test cell during cycle with 1 Hz in the vicinity of the fan
Measurement parameter：
  Humidity modal data, temperature of test cell during cycle
Test equipment：
  Humidity measurement system

## Slide 15: Monitoring of RCB of all batteries
Objective: Measurement of RCB will be mandatory for all vehicles. Feasibility and tolerances as critical issues have to be checked thoroughly.
Background：
  RCB has an influence on CO2 emissions
  RCB of all batteries to be considered for evaluation of CO2 Emissions
  Thermal load of clamps is limited (< 40 °C)
How to：
  Measurement of RCB in all phases of WLTC separately of all batteries (all low voltage and high voltage batteries). Measurement of temperature with closed bonnet.
Measurement parameter：
  Current, time, temperature in the vicinity of the clamps
Test equipment：
  RCB measurement system for all batteries, temperature monitoring system

## Slide 16: Exhaust pressure before Remote Mixing Tee or CVS
Background：
  GTR limits maximum back pressure at end of tailpipe to avoid distortion of engine mass flow
  Evaluation of pressure averaging requirements
How to：
  Measurement of pressure at the end of tailpipe with/without CVS connected, with a frequency of 1Hz.
Measurement parameter：
  Exhaust pressure
Test equipment：
  Pressure monitoring system

## Slide 17: Proportional Fan
Background：
  Feasibility of geometrical prescription for positioning of fan is to be tested
How to：
  Measurement of position and air flow
Measurement parameter：
  Fan speed, air flow
Test equipment：
  Scale, air flow measurement system

## Slide 18: Cycle Mode Construction
Background：
  2 Options to be tested (one with hot start and intermediate soak)- see Mode construction overview in OICA/JRC/UTAC Proposal (draft)
  Soak time is dependant on measurement equipment restrictions and other parameter
How to：
  Performance of hot start option with soak time variation (0,5,10,15,20 min)
Measurement parameter：
  Relevant temperatures, emissions and batteries balance, feasibility in regard to measurement equipment (gaseous, PM, PN)
Test equipment：Temperature monitoring system

## Slide 19: Required time for bag analysis
Background：
  Option of Mode Construction for WLTC for hot start testing includes soak time for bag analysis
  Testing of PHEV: CD test requires bag analysis after each completion
How to：
  Measurement of time needed for complete bag analysis and restart between two charge depleting cycles or hot start tests.
Measurement parameter：
  System time
Test equipment：
  Automation system

## Slide 20: Tolerances of Emission Measurement System
Objective: Higher repeatability could reduce test number and testing burden.
Background：
  Number of certification tests depends on level of emissions in relation to standard (1x < 70%, 2x <85%, 3x >85% ) in actual gtr.
  Higher repeatability through enhanced equipment is predicted
How to：
  Application of calibration frequency and tolerances of actual gtr
  Measurement of statistical spread of all criteria pollutants, CO2 and RCB in multiple tests (min. 3)
Measurement parameter：
  RCB, Emissions, additional parameters
Test equipment：
  Testbench, emission measurement equipment, RCB and temperature monitoring system

## Slide 21: Subtraction of Intake Air Concentration
Background：
  Consideration of background emissions at low concentrations of criteria pollutants
  Relevant for HEV, PHEV with intermittent ICE operation
How to：
  Measurement of background concentrations of CO, HC, NMHC, NOx, NO2, PM etc. and the intake air flow
Measurement parameter：
  Emissions - Evaluation of statistical data of bags and background
Test equipment：
  Emission testbench, vehicle selection preferably PHEV with blended operation mode, air flow monitoring system

## Slide 22: Dilution Factor
Background：
  Dilution Factor has to reach a certain level to avoid condensation of water in the CVS
How to：
  Measuring of modal CO2 data, optional measuring of modal humidity in exhaust and diluted exhaust flow
Measurement parameter：
  CO2 concentration, water concentration
Test equipment：
  Test bench, humidity sensor, FTIR et al.

## Slide 23: Dyno Operation Mode
Objective: Dyno operation mode is required for safe vehicle operation on dyno. Feasibility of lab process to be checked.
….. to be supplemented

## Slide 24
DTP subgroup PM/PN

## Slide 25: PM filter conditioning
Background:
  Minimum conditioning time required for filter after test
How to:
  Weigh filter post test after 1 h conditioning and continue periodic weighing (recommended 30min until 3hrs and longer frequency until 24hrs) until weighings indicate stable weight. Data required to determine minimum conditioning time (aim is to trace the evolution).
Measurement parameter:
  Filter weight
Test equipment:
  Filter weighing equipment

## Slide 26: Dilution tunnel pre-conditioning & PM/PN background levels
Background:
  Is 20 minutes pre-conditioning at 120kph sufficient?
  Define background correction levels
How to:
  Measure PM/PM tunnel backgrounds at minimum a single measurement before or after test and after any tunnel conditioning. More frequent measurements are optional.
Measurement parameter:
  Tunnel PM/PN backgrounds
Test equipment:
  Filter weighing equipment

## Slide 27: PN during regeneration
Background:
  Experience on PN during DPF regeneration
  Confirm PN measurement system is capable of excluding worst case volatile material during DPF regenerations
  Check CVS and filter face temperatures during regenerations
How to:
  Vehicles
    Will need regen indicator and inhibitor switch
  Measure PN before, during and after regeneration
  Different PN measurement systems
    Two systems per lab sampling in parallel
  Impact of VPR pcrf
    Test over range from 100-3000 (one system at high, one at low setting each test)
  Two tests at each pcrf setting
  Impact of CVS dilution on nucleation mode particles
    Test at max and min CVS dilution
  DPF fill procedure
    Either fast loading on engine dyno or on vehicle loading
    Follow R83 advice on fill state stabilisation for pre-regen tests
  VPR sulphate removal capability
    Test with highest sulphur lube oil permitted by OEM and fuel at maximum (10/15mg/kg) sulphur limit
Measurement parameters
  PN emissions, PCRF, CVS dilution factor, sulphur level of fuel
Test equipment:
  PN equipments

## Slide 28: Mode Construction for ki Determination
Background：
  Ki Determination has to be performed in baseline option of mode construction
How to：
  Measuring of relevant parameters during subsequent testing with and w/o regeneration
Measurement parameter：
  PM loading, regeneration time
Test equipment：
  Test bench, emission measurement system

## Slide 29: Mode Construction for ki Determination of multiple periodically regenerating systems
Background：
  Ki Determination has to be performed in baseline option of mode construction
How to：
  Measuring of relevant parameters during subsequent testing with and w/o regeneration of a multiple regenerating system
Measurement parameter：
  PM loading, regeneration time, NOx loading, regeneration
Test equipment：
  Test bench, emission measurement system

## Slide 30
DTP subgroup AP

## Slide 31
NO-measurement
All participating labs should measure both ways (bag and dilute modal).
All measurements:
  Absolute difference between dilute and modal measurement
Repeat tests:
  Variability of NO result compared to NOx-measurement
  Variability of NO result from bag measurement versus dilute modal
Qualitative assessment parameters
for validation phase 2

## Slide 32
N2O-measurement
Use of two (or more) different systems in parallel (e.g. QCL, GC-ECD, FTIR,…)
Cal Gas: 5 ppm of N2O in N2 (+/- 2%)
All measurements:
  repeatability of air bag measurement
  difference in result of the two systems
  stability of calibration (apply cal gas before and after test)
Repeat tests:
  Variability of N2O result
Qualitative assessment parameters
for validation phase 2

## Slide 33
NH3-measurement
NH3 only for Diesel with SCR
take care of extracted sample
measurement of two systems in parallel (e.g. QCL and FTIR…)
use of different sampling systems
  one with smallest possible Volume, shortest possible line length
  one with larger Volume and line length
  where available, use in situ system in parallel
All measurements:
  compare average concentration result
  Compare traces of the systems
    incidence of first peak
    rise time
    drag
Repeat tests:
  Variability of NH3 result
Qualitative assessment parameters
for validation phase 2

## Slide 34
DTP subgroup EV/HEV

## Slide 35: Consideration items on E-Lab. Gr.
Day 1
Day 2 (EV: Day 1)
Day 3 (EV: Day 2)
Battery condition [Ah}
Precondition
Pre-con cycle
Soak 2 Options
12~36hr or
6hr 25+/-2
Confirm tire pressure
Prepare RCB measurement
Discharge
CS cold
Charge sustaining (CS) mode test (cold)
Full charge
max. 12 hr
⊿E
within 1hr
Plug OFF
CD mode×n
Charge depleting (CD) mode test
CS hot
Soak 12~36 hr
⊿E
AER
EAER
RCDR
Full charge
Charging voltage
100 / 200V (PL12)
End of charge
criteria (PL1)
Order of CD/CS
(PL4)
Interruption
condition (PL5)
RCB break off
criteria (PL2/9)
Termination condition
for EV range (PL6/7)
Charge sustaining (CS) mode test (hot)
Prepare RCB measurement
CO2/FC calculation
(PL8/10)
Performance of
Watt-hour meter,
Am-meter (PL3)
Multi mode
gear box
(PL11)
◆Test flow (independent test for L/M/H/ExH)
*) EAER: Equivalent All Electric Range
*) RCDR: Charge Depleting Range
*) NEC: Net Energy Change = RCB * nominal voltage of RESS
*) RCB: RESS Charge Balance (=SOC)
*) RESS: Rechargeable energy storage system
*) AER: All Electric Range

## Slide 36: PL1. End of charge criteria
Objective :
  To confirm influence of fluctuation of RCB from charge completed to plug of.
Back ground：
  gtr draft
  IV.1.2.4.2.End of charge criteria
  The end of charge criteria corresponds to a charging time of 12 hours,
  except if a clear indication is given to the driver by the standard instrumentation that the electrical energy/power storage device is not yet fully charged.
  ACEA proposal: Starting within 1 hour from “plug-off”
  Japanese proposal: ”from charge completed”
How to：
  Monitoring RCB fluctuation after charge complete
  CD test：2（max/minimum charging）×4 phase（L/M/H/ExH）
  Impact of battery type ？ (Ni-MH /Lithium，，)
Measurement parameter：
  RCB（Voltage/electric current & CAN）
Test equipment ：
  RCB measurement system
Charge complete
Plug off
CD test start
1hr
fluctuation
CS test
CD test

## Slide 37: PL2/9. RCB break off criteria
Objective :
  To confirm test sequence and break off criteria as absolute value Ah, detection of CS condition.
Back ground：
  RCB Break off Criteria (CD→CS)
How to：
  Comparing 2 calculation result by each procedure
  CDtest：4phase（L/M/H/ExH）×3times
Measurement parameter：
  RCB，Fuel Consumption， total Energy demand at wheels to perform the cycle based on the theoretical profile of the WLTC
Test equipment：
  RCB measurement system
CS mode
CD mode
To be analyzed : a relative NEC:
1) (RCB x Nominal Voltage of the battery) / (RCB x Nominal Voltage of the battery + Energy of the Fuel)
2) (RCB x Nominal Voltage of the battery) / (total Energy demand at wheels to perform the cycle based on the theoretical profile of the WLTC)
or an absolute NEC : RCB x Nominal Voltage of the battery
*) RCB: RESS Charge Balance (=SOC)
*) RESS: Rechargeable energy storage system
*) NEC: Net Energy Change = RCB * nominal voltage of RESS

## Slide 38: PL4. Order of CD/CS test
Objective :
  To compare charging before test and charging after test and to compare emissions results, electric range and electric consumption. Influence or not on the results and on the battery charging.
Back ground：
  Confirm impact of the order of CD/CS test
  Soak -CS test –Charge or CD test –shifting CS mode-Charge
    For example the temperature impact around Battery
How to：
  CD and CS test：4phase（L/M/H/ExH）
Measurement parameter：
  RCB（Voltage/Electric current, CAN and temperature of Battery or any other electrical parts）
  Fuel consumption/CO2, Exhaust emissions
Test equipment：
  RCB measurement system

## Slide 39: PL6/7. Termination condition for EV range (EV)
Objective :
  Detection of test termination condition for range tests on EV.
Back ground：
  Japan：the deviation occurs not more than once within 4 second
  US：more than 2 second
  Europe：Target more than 50km/h：Below 50km/h，
Target Less than 50km/h：more than 5s 6 times during 1 hour
How to：
  Running until completely stop and calculate EV range by each procedure
  Compare each result
  EV range test：4Phase（L/M/H/ExH）
Measurement parameter：
  RCB（Voltage/electric current and CAN）and driving distance
Test equipment：
  RCB measurement system

## Slide 40: PL6/7. Termination condition for EV range (OVC HEV)
Objective :
  Detection of test termination condition for range tests on OVC HEV.
Back Ground：
  To compare OVC HEV and Range Extender, full test cycle and low power cycle.
How to：
  Confirmation test procedure for range extender
  Compare with OVC HEV
  CD and CS test：4phase（L/M/H/ExH）
Measurement parameter：
  RCB（Voltage/Electric current & CAN）, CO2 and driving distance
Test equipment：
  RCB measurement system

## Slide 41: PL 8 CO2 and FC calculation method
Objective :
  Test sequence independent UF compared to one UF for the complete CD test.
Back ground：
  US: possible to have one UF for each test sequence
How to ：
  CD test：4phase（L/M/H/ExH)
Measurement parameter：
  Emissions, CO2, FC, RCB etc.
Test equipment ：
  Test equipment proposed for validation phase 2

## Slide 42: PL 10 CO2 and FC calculation method
Objective :
  Investigate the possibility to split the CO2 value of the transient cycle, the n-cycle.
Back ground：
  The calculation method for CO2 and FC on the CD test is not decided
How to ：
  CD test：4phase（L/M/H/ExH)
Measurement parameter：
  Emissions, CO2, FC, RCB etc.
Test equipment ：
  Test equipment proposed for validation phase 2

## Slide 43: PL 11 Multi mode gearbox
Objective :
  Investigate if the ICE proposal (default mode approach) is applicable to OVC HEV for CO2, FC measurement.
Back ground：
  For OVC HEV, the concept of default mode developed in ICE group is not transposable and to keep the ECE concept (the most electric consuming mode to best match the driving curve in CD test and the most fuel consuming mode to best match the driving curve in CS test), irrespective of the presence of a default mode if any. This preliminary statement has to be confirmed during the validation phase 2 (to check the relevance of such an approach ).
How to ：
  CD and CS test：4phase（L/M/H/ExH)
Measurement parameter：
  Emissions, CO2, FC, RCB etc.
Test equipment ：
  Test equipment proposed for validation phase 2

## Slide 44: PL12. Charging voltage 100 / 200V
Objective :
  Influence of charging voltage on results.
Back ground：
  Charging voltage has impact for charging efficiency.
  There are several Voltage in all of the world.
  US:110-120V, Japan:100/200V, EU:220-240V(127V)
How to ：
  Measure Charging time，Fluctuation during Plug ON，impact for CS/CD test result, Electric Range.
  OVC HEV: CD test：each Voltage×4phase（L/M/H/ExH）
  EV: Electric range :Each Voltage × 4phase（L/M/H/ExH）
Measurement parameter：
  RCB（Voltage and CAN）
Test equipment ：
  RCB measurement system