## Slide 1: WLTP-DTP Subgroup Additional Pollutants Progress report
WLTP-DTP-AP, Mörsch/Astorga
Date: 06. Jun. 2012
WLTP-DTP-10-11

## Slide 2
WLTP-DTP-AP, Mörsch/Astorga
Meeting schedule
# | Date | Location | Participants | Main Topic
1 | 20.07.2010 | Web/TelCo | 14 | Definitions
2 | 27.09.2010 | Web/TelCo | 20 | List of pollutants
3 | 9./10.12.2010 | JRC/Ispra | 15 | List of Candidate methods
4 | 7./8.03.2011 | BMW/Munich | 21 | Drafting of GTR
5 | 10/11.05.2011 | JRC/Ispra | 16 | Drafting of GTR
6 | 09.12.2011 | Web/TelCo | 16 | VP2 parameter list
7 | 11.05.2012 | Web/TelCo | 16 | Open issues GTR
8 | 25.05.2012 | Web/TelCo | 15 | Open issues GTR
9 | 19.06.2012 | Horiba/Frankfurt |  | Validation of AP
10 | Tbd. | Tbd. |  | 
Notes: <number>

## Slide 3
Validation phase 2:
NO/NOx-measuremenst: all labs should provide feed back
N2O: only some labs will provide data
NH3 only for Diesel with SCR: a few labs will be able to deliver data
EtOH and Adehydes: later… (specific VF for those compounds?)
WLTP-DTP-AP, Mörsch/Astorga

## Slide 4
WLTP-DTP-AP, Mörsch/Astorga
All participating labs measure both ways (bag and dilute modal).
All measurements:
  Absolute difference between dilute and modal measurement
Repeat tests:
  Variability of NO result compared to NOx-measurement
  Variability of NO result from bag measurement versus dilute modal
Validation phase 2: NO/NOx-measurement
 All participating labs in VP2 should deliver results
P 43-45; Annex 5
P 49 Mix gases
Notes: Nitrogen oxide and nitrogen oxides (ND IR) pg 22 Annex 5
This will be consider also a summary of the assessment criteria that you will find in the CIRCA document
<number>

## Slide 5
Use of two (or more) different systems in parallel (e.g. QCL*, GC-ECD, FTIR,…)
Calibration Gas: 5 ppm of N2O in N2 (+/- 2%)
All measurements:
  repeatability of air bag measurement
  difference in result of the two systems
  stability of calibration (apply calibration gas before and after test)
Repeat tests:
  Variability of N2O result
Validation phase 2: N2O-measurement
 Some labs will deliver results
P 52-53; Annex 5
* Quantun cascade Laser detecto
Notes: NITROUS OXIDE =N2O
<number>

## Slide 6
WLTP-DTP-AP, Mörsch/Astorga
Validation phase 2:
 Only few labs will deliver results
NH3 only for Diesel with SCR
Take care of extracted sample
Measurement of two systems in parallel (e.g. QCL and FTIR…)
Use of different sampling systems
  one with smallest possible Volume, shortest possible line length
  one with larger Volume and line length
  where available, use in situ system in parallel
All measurements:
  compare average concentration result
  compare traces of the systems (incidence of first peak, rise time, drag)
Repeat tests:
  Variability of NH3 result
P 50-51; Annex 5

## Slide 7
WLTP-DTP-AP, Mörsch/Astorga
Validation of AP
NO/NOx  sufficient results expected from VP2
N2O  due to limited results from VP2 additional validation might be necessary
NH3  additional validation necessary
EtOH  additional validation necessary
Aldehydes  additional validation necessary
OK!

## Slide 8
WLTP-DTP-AP, Mörsch/Astorga
Proposed setup:
Test in one lab (tbd.)
Flex fuel vehicles runnig on E05, E25 and E75
Request to suppliers to make available online systems for EtOH
All systems measure in parallel along with existing impinger method
Test should be carried out together with validation of aldehydes (on-line systems for Aldehydes are under development but not yet available) for efficiency reasons
Validation of EtOH measurement
P 54-55; Annex 5

## Slide 9
WLTP-DTP-AP, Mörsch/Astorga
Proposed setup:
Online systems for Aldehydes are under development but not yet available
As soon as systems become available:
Test in one lab (tbd.)
Request to suppliers to make available online systems for aldehydes
All systems measure, in parallel, along with existing DNPH-method
Validation of Aldehydes
P 56; Annex 5

## Slide 10
WLTP-DTP-AP, Mörsch/Astorga
Possibilities and necessary setup for additional Validation test will be discussed in detail during next face to face meeting in Frankfurt (hosted by Horiba)
Date 19.06.2012 10:00 – 16:00
Further definition of an additional validation program

## Slide 11
THANKS FOR YOUR ATTENCION
C. Astorga
CIRCA documents WLTP-DTP-AP
Draft GTR proposal: Main contribution to Annex 5
Notes: <number>