## Slide 1: Proposal tire & vehicle selection for WLTP
DTP10 06-Jun-2012
JAPAN

## Slide 2: Discussion in DTP9
Class | RRC (kg/ton) | Case-1
1 | - 6.5 | 
2 | 6.6 - 7.7 | 
3 | 7.8 - 9.0 | 
4 | 9.1 - 10.5 | 
5 | 10.6 - 12.0 | 
6 | 12.1 - | 
Lighter
Heavier
Worst [class] is selected.
Consider later with CO2 information from ICCT, in case that 2 or more [RRs] are in the worst class.
If mass production tyre is classified to heavier class, re-test is required with the worst [class].
Specification change at Mass Production
This part is excluded from DTP discussion due to “Extension Issue”.
<<<Homework>>>
Above discussion is only TMH, which the worst case vehicle selection in NL/T&E/ICCT proposal.
Japan should indicate their position of tire selection for TML, which the best case vehicle selection.

## Slide 3: Current proposal / Japanese proposal
Vehicle Weight
CO2 Emission
Summary of current proposal by NL+T&E+ICCT
Tested by the BEST and WORST cases, including not only vehicle weight, but also aerodynamic parts and tires.
Interpolation by vehicle weight only for moderate vehicles.
Question at DTP9
CO2 from best and worst vehicle weight, aero. parts, and tires can be interpolated by vehicle weight only??? (ICCT has been requested to estimate CO2 impact other than vehicle weight.)
Japanese proposal
Interpolation by vehicle weight is allowed in case of weight difference only.
For other difference influenced to CO2 or Fuel Economy, additional tests are necessary.
with the best road load (aero. parts and tires) and lightest vehicle weight
with the worst road load (aero. parts and tires) and heaviest vehicle weight
Interpolated by vehicle weight

## Slide 4: Case study - tires
 | Ver. A | Ver. B | Ver. C | Ver. D
 | Lightest | Lighter | Heavier | Heaviest
#2 | X | X |  | 
#3 |  | X | X | 
#4 |  | X | X | X
Weight
RRC
Low RR
High RR
Vehicle Weight
CO2 Emission
Sample of specification
Ver. A
Ver. B
Ver. C
Ver. D
RRC#4
RRC#2
Theoretical slope by weight
Slope by current proposal
RRC#3
TMH
TML
Concern
Current proposal could produce CO2 gap since RRC of tire does not correlate with vehicle weight. (Dots of theoretical CO2 performance are not on the line of slope by the current proposal.)
Japan estimate approx. 2% CO2 impact within a RRC. Interpolation by the current proposal could make some error not negligible.
Theoretical CO2 performance

## Slide 5: Case study - tires & aero. parts
 | Ver. A | Ver. B | Ver. C | Ver. D
 | Lightest | Lighter | Heavier | Heaviest
#2 | X | X |  | 
#3 |  | X | X | 
#4 |  | X | X | X
Weight
RRC
Low RR
High RR
Adjustable controlled aerodynamic pars;
Radiator shutter
Folding front spoiler
Folding Rear spoiler
Vehicle Weight
CO2 Emission
Sample of specification
Ver. A
Ver. B
Ver. C
Ver. D
RRC#4
RRC#2*
Negative effect of aero. parts**
* with the best aero. Setting
** assumed actual impact is 50% of total aero. parts effect (adjusted by blue arrow)
Theoretical slope by weight
Slope by current proposal
TML
TMH
Concern (same as previous slide)
Current proposal could produce CO2 gap since RR of tire and aerodynamics does not correlate with vehicle weight. (Dots of theoretical CO2 performance are not on the line of slope by the current proposal.)
Theoretical CO2 performance

## Slide 6: Proposal
 | Ver. A | Ver. B | Ver. C | Ver. D
 | Lightest | Lighter | Heavier | Heaviest
#2 | X | X |  | 
#3 |  | X | X | 
#4 |  | X | X | X
Weight
RRC
Low RR
High RR
Vehicle Weight
CO2 Emission
Sample of specification
Ver. A
Ver. B
Ver. C
Ver. D
RRC#4
RRC#4
RRC#2
This must be tested as the worst case data.
TMH
TML
RRC#3
Element |  | Proposal
Weight |  | Interpolation is OK in case of weight difference only, or worse data can be used with no additional tests.
Tire |  | Tested by worst RRC.
Aerodynamics | Electric/Automatic controlled | Tested by the worst case unless authorities approve that the modified road load reflect representative condition of the electric controlled aero. systems.
 | Mechanical parts | Tested by the road load with applicable parts, or worse data can be used with no additional tests.