## Slide 1: WET GRIP ADHESION FOR C2 & C3 TYRES Proposal for minimum requirements
<number>
Transmitted by the expert from ETRTO
Informal document GRRF-73-18
(73rd GRRF, 18-20 September 2012 Agenda item 7(d))
Reference to document GRRF-73-08
Notes: <number>

## Slide 2: Introduction
The minimum performance level should fit to the State of Art on existing markets since there are no indications that C2 or C3 tyres on the market are unsafe regarding wet adhesion.
<number>

## Slide 3: 1. Limits in R117.02 for C1 tyres
<number>
Category of use |  | Wet grip index (G)
Normal tyre |  | ≥ 1.1
Snow tyres |  | ≥ 1.1
 | “Snow tyre for use in severe snow conditions” and with a speed symbol ("R" and above, including "H") indicating a maximum permissible speed greater than 160 km/h | ≥ 1.0
 | “Snow tyre for use in severe snow conditions” and with a speed symbol ("Q" or below excluding "H") indicating a maximum permissible speed not greater than 160 km/h | ≥ 0.9
Special use tyre |  | Not defined

## Slide 4: 2. Proposed limits in R117.02 for C2 tyres
<number>
Category of use |  | Wet grip index (G) | 
 |  | 0ther | Traction Tyres
Normal Tyres |  | ≥ 0.95 | > 0.85
Snow Tyres |  | ≥ 0.95 | > 0.85
 | Snow tyres for use in severe snow conditions | ≥ 0.85 | > 0.85
Special use Tyres |  | > 0.85 | > 0.85

## Slide 5: 2. Proposed limits in R117.02 for C3 tyres
<number>
Category of use |  | Wet grip index (G) | 
 |  | 0ther | Traction Tyres
Normal Tyres |  | > 0.65 | > 0.65
Snow Tyres |  | > 0.65 | > 0.65
 | Snow tyres for use in severe snow conditions | ≥ 0.65 | > 0.65
Special use Tyres |  | > 0.65 | > 0.65

## Slide 6: 3. Comparison to the State of the Art: C2 tyres
NORMAL TYRES
SNOW TYRES
<number>
0.95
0.85

## Slide 7: 3. Comparison to the State of the Art: C3 tyres
<number>
NORMAL TYRES
TRACTION TYRES
SNOW TYRES
0.65
0.65
0.65

## Slide 8: 4. General comments
The minimum requirement has been proposed to keep the minimum performance as per the European and Japanese State of Art.
The limit proposed for C2 normal tyres is the same as the one requested by Korea.
The impact of the planned requirements for Rolling Resistance and Noise on the future state of the art is unknown. Therefore at least the current level of wet grip performance shall be maintained.
<number>

## Slide 9
Thank you!
<number>