## Slide 1: Concept of the exclusion of the blind area
In Japan, it is predicted that, among accidents recorded during 8 years in the 1990s, five fatal accidents occurred at the time of the vehicle’s start due to a blind area.
In all these five accidents, the vehicle part causing damage to the victim was the left rear wheel (on the passenger’s side). Hence, we propose to specify the field of vision such that the driver, when starting the vehicle, can notice the object and stop the vehicle before it comes in contact with the rear wheel even if there is some blind area.
Based on the result of an experiment using the actual vehicle driven by a general driver, we determined the blind area, X, and the distance from when the object appearing from the blind area is noticed to when the vehicle is stopped, Ls, as follows:
X=0.292Ls-0.203
In order to prevent the object from being involved in an accident, Ls should be shorter than the distance from the rearmost edge of the blind area to the edge of the rear wheel, L, and the blind area, X, needs to be set with L > Ls.
Submitted by the expert from Japan
Informal document GRSG-104-46
(104th session, 15-19 April 2013
agenda item 5)

## Slide 2
Blind area generated by A pillar and a door mirror
Obstacle
(Height ;1m, φ;0.3m）
Speed when driver recognize the obstacle; V(m/s)
Experimental method
Distance from when the object appearing from the blind area to when the vehicle is stopped; Ls(m)
Width of blind area; X(m)
Distance from when the object appearing from the blind area to rear tire ; L(m)
Participant; 14 males, 16 females (20-60 year-old)
Conducted by JARI(Japan Automobile Research Institute)
Experimental condition 0, 0.2, 0.4, 0.6, 0.8m)
Vehicle used in this experiment
Experiment condition; Width of blind area 0, 0.2, 0.4, 0.6, 0.8m
Measurement;
V(ms); Speed when driver recognize the obstacle
Ls(m);Distance from when the object appearing from the blind area
to when the vehicle is stopped;
Notes: <number>

## Slide 3
Experimental results
Distance when driver recognize the object appearing from the blind area to when the vehicle is stopped, Ls(m)
Width of blind area; X(m)
Speed when driver recognize
the obstacle; V(m/s)
Speed when driver recognize
the obstacle; V(m/s)
Width of blind area; X(m)
Distance when driver recognize the object appearing from the blind area to when the vehicle is stopped, Ls(m)
X=0.292Ls-0.203
Acceptable
blind area width