## Slide 1
Gtr7 measuring method for effective
head restraint height
Update for GRSP, following
the IWG on gtr No.7 in London March 2012
Hans Ammerlaan - Netherlands
Update GRSP on measuring method - Geneva, May 2012
<number>
Informal document GRSP-51-23
(51st GRSP, 21–25 May 2012,
agenda item 3)
Notes: <number>
IWG on gtr No.7-Phase 2, 5-6 December 2011

## Slide 2
<number>
Contents
Terms of reference of the informal group gtr No.7 - Head Restraints - Phase 2,
part (a): how to define the effective height / concerns expressed in the rationale of gtr7
Anthropometry / position of back-of-head in the 1980’s
Physical tools for positioning of back-of-head
Tools for positioning of back-of-head of people nowadays
Measuring procedure for effective head restraint height (step by step)
Update GRSP on measuring method - Geneva, May 2012

## Slide 3
<number>
Terms of reference of the informal group gtr No.7
Head Restraints Phase 2
Text from doc. GTR7-01-08 (ECE/TRANS/WP.29/2009/130):
“ III. SUBJECTS FOR REVIEW AND TASKS TO BE UNDERTAKEN
6. With regard to head restraint height, the informal group should decide:
How to define the effective height;
The height requirements ”
Update GRSP on measuring method - Geneva, May 2012

## Slide 4
<number>
Concerns expressed in the rationale of gtr No.7
The measurement of the head restraint height taken as shown above does not address the effective height of the head restraint.
In the case of extremely contoured head restraints, the height of the surface that the head would contact is less than the measured height.
Update GRSP on measuring method - Geneva, May 2012

## Slide 5
<number>
Anthropometry / position of back-of-head in the 1980’s
UMTRI-86-39 study, merged H-points of the small female, mid-sized male and large male (known from the UMTRI-83-53-1).
It was found that the back-of-head of the large male, compared to the mid-sized male, is a “distance x” (being 31 mm) more rearward.
However this result is reached with:
a chosen seatback angle,
a large male dating from the 1980’s, so not representing the nowadays large male car occupant.
Update GRSP on measuring method - Geneva, May 2012

## Slide 6
<number>
Physical tools for positioning of back-of-head
Update GRSP on measuring method - Geneva, May 2012
Combined in one picture two physical tools:
(both for mid-sized male of the 1980’s)
the HRMD (from ICBC) mounted on the 3-D H-point machine,
the Torso & Neck Link (known from gtr No.7, fase 1).

## Slide 7
<number>
Tools for positioning of back-of-head of people nowadays I
The TNO study presented in Berlin (GTR7-04-03) made use of the posture from UMTRI-83-53-1 ( this study is used to create the HRMD) and combined this posture with the recent anthropometric database of CAESAR (Civilian American and European Surface Anthropometry Resource).
The back-of-head of the 2004 NL large male is found to be 39 mm more rearwards than a mid-sized occupant (HRMD).
Based on this the Torso & Neck Link (known from the gtr No.7 Phase 1) is supplemented with an upscaled version as follows:
Update GRSP on measuring method - Geneva, May 2012
 | Torso & Neck Link, based on HRMD | Torso & Neck Link, based on large male (CAESAR NL 2004)
Torso link | 504,5 | 593
Neck link | 203 | 215
Head-overhang | 71 | 76

## Slide 8
<number>
Tools for positioning of back-of-head of people nowadays II
The original Torso & Neck Link together with the upscaled Torso & Neck Link can be expressed in goniometric formulas.
With these formulas can be calculated the difference in back-of-head position between the mid-sized male (HRMD) and the nowadays large male (this difference is hereafter called “Distance x”).
The design torso angle is the only parameter in the formulas. So the outcome of the calculations can also be expressed in a table (e.g. just like is done in Regulation No.125 on Forward Field of Vision of Drivers (Table IV)).
Doing so, the measuring method for effective head restraint height does not need tools that are questionable.
The so developped measuring method comprises the following 5 steps.
Update GRSP on measuring method - Geneva, May 2012

## Slide 9
<number>
Test procedure for effective head restraint height I
the Torso & Neck Link concept expressed in goniometric formulas
With head restraint set in mid-sized position,
the measuring of Contact Point CP:
Available are:
the coordinates of the R-point,
the design torso angle, and
the dimensions of the mid-sized Torso & Neck Link.
Needed actions:
1) calculate Z-coordinate CP =
504.5 * COS(design torso angle – 2.6º) + 203
(instead of calculation, a table will be provided),
2) mark this point on the head restraint surface and
measure X-coordinate CP.
Update GRSP on measuring method - Geneva, May 2012

## Slide 10
<number>
Test procedure for effective head restraint height II
the Torso & Neck Link concept expressed in goniometric formulas
With head restraint set in its highest position, the measuring of Intersection Point IP:
Available are:
the X-coordinate CP
the table providing the “distance X” which
depends of the design torso angle
Needed actions:
3) calculate X-coordinate IP =
measured X-coordinate CP + “distance x”,
4) mark this point on the head restraint and measure Z-coordinate IP.
Update GRSP on measuring method - Geneva, May 2012

## Slide 11
<number>
Test procedure for effective head restraint height III
the Torso & Neck Link concept expressed in goniometric formulas
Calculation of the highest effective head restaint height:
Needed final action:
5) Calculate effective head restaint height =
Δ X * SIN(design torso angle) + Δ Z * COS(design torso angle)
Update GRSP on measuring method - Geneva, May 2012

## Slide 12
<number>
Thank you for your attention
Update GRSP on measuring method - Geneva, May 2012