## Slide 1
Actual needed height
of head restraints
Follow up of discussions during
IWG on gtr No.7 in London, March 2012
Hans Ammerlaan - Netherlands
Update GRSP on actual needed HR height - Geneva, May 2012
<number>
Informal document GRSP-51-24
(51st GRSP, 21–25 May 2012,
agenda item 3)
Notes: <number>
IWG on gtr No.7-Phase 2, 5-6 December 2011

## Slide 2
<number>
Contents
Terms of reference of the informal group on Head Restraints phase 2,
part (b): the actual height
History
Anthropometry:
- sitting height dummies versus erect sitting height of males in USA and NL
- measurement of erect sitting height
- erect sitting height, data from UK and Germany
Head restraint height based on automotive posture
Calculation of needed head restraint height
Needed head restraint height
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 3
<number>
Terms of reference of the informal group on
Head Restraints phase 2
Text from doc. GTR7-01-08 (ECE/TRANS/WP.29/2009/130):
“ III. SUBJECTS FOR REVIEW AND TASKS TO BE UNDERTAKEN
6. With regard to head restraint height, the informal group should decide:
How to define the effective height;
The height requirements ”
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 4
<number>
History
  the study UMTRI-83-53-1, Dec. 1983 delivered anthropometric specifications for a small female, a mid-sized male and a large male,
  these data were used for the constitution of an adult-dummy family,
  the mid-sized male in
  automotive posture
  is also used by ICBC
  to create the HRMD.
  (hereby a reproduction
  of Figure 5-1 showing
  some specifications)
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 5
<number>
Anthropometry / dummies versus males from USA and NL
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 6
<number>
Anthropometry / measurement of erect sitting height
Update GRSP on actual needed HR height - Geneva, May 2012
An objective method, used in Anthropometry worldwide, measures the erect seating height with the subject sitting up straight
(this method includes also the straightening of the spine that occurs at the moment the occupant sustains a rear impact).

## Slide 7
<number>
Anthropometry / data from UK
(earlier presented in HR-6-11)
Update GRSP on actual needed HR height - Geneva, May 2012
Anthropometric Data 1 - UK
Male
5th%ile 50th%ile 95th%ile
Stature 1641.0 1755.1 1869.2
Erect Sitting Height 860.4 920.2 980.0
Head Circumference 547.3 575.0 602.7
Face Length 105.9 118.8 131.7
1 ADULTDATA - The handbook of adult anthropometric and strength measurements. Department of Trade and Industry, London. ISBN 0 9522571 3 0. May 1998.

## Slide 8
<number>
Anthropometry / data from Germany I
(abstract from DIN 33402-2: 2005, tabelle 22)
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 9
<number>
Anthropometry / data from Germany II
(presented in March 2007 in EEVC SC)
Update GRSP on actual needed HR height - Geneva, May 2012
Free from internet
anthropometric data
from source:
“Brandenburgische Umwelt Berichte (BUB)
10S.23-53 (2001),
Körpermasse
Young adult males
Erect Sitting Height
5th%ile 885 mm
50th%ile 943 mm
95th%ile 1000 mm

## Slide 10
<number>
Head restraint height based on automotive posture
Update GRSP on actual needed HR height - Geneva, May 2012
In the world of anthropometry the erect sitting height is used.
On the other hand, in the automotive world the use of automotive posture is very common.
In the following we will make use of automotive posture.
Accompanying remarks:
- when using automotive posture, for the proper design of
head restraints one should take account of spine straightening,
- besides spine straightening one has to take account of ramping up too!

## Slide 11
<number>
X- and Z-coordinate of back-of-head of people nowadays
The TNO study presented in Berlin (GTR7-04-03) made use of the posture from UMTRI-83-53-1 (= the study used to create the HRMD) and combined this with the recent anthropometric database of CAESAR (Civilian American and European Surface Anthropometry Resource).
This study delivered a.o. the X- and Z-coordinate of the back-of-head of the 2004 NL large male (in automotive posture with a seat back angle of 25 degrees).
Compared with the HRMD installed on the 3-D H-machine this leads to the following:
These new found coordinates can be used to calculate the actual needed head restraint height
Update GRSP on actual needed HR height - Geneva, May 2012
 | HRMD installed on 3-D H-point machine | Large male (= Caesar 2004 NL)
Z-coordinate back-of head w.r.t. H-point | 669 | 763
X-coordinate back-of head w.r.t. H-point | 263 | 302

## Slide 12
<number>
Calculation of needed head restraint height I
Available are the X- and Z-coordinate of the back-of-head of the large male being 302 respectively 763 mm;
It is assumed that there will be no spine straightening and no ramping up of the body, so the head would travel horizontally rearward;
It is assumed that the distance (backset) from the head to the contact point on the head restraint is 30 mm;
So the X- and Z-coordinate of the point of the head restraint that is supposed to catch the head will be 332 respectively 763 mm;
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 13
<number>
Calculation of needed head restraint height II
The formula for calculating effective head restraint height =
Δ X * SIN(design torso angle) + Δ Z * COS(design torso angle);
Used values will be Δ X = 332 mm, Δ Z = 763 and
a design torso angle of 25 degree;
The outcome for the actual needed head restaint height
is 831 mm.
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 14
<number>
Needed head restraint height
Remarks:
On one hand it is assumed that there will be no spine straightening and no ramping up of the body, but from research concerning automotive seats (e.g. SAE paper 983158 Human Head-Neck Responses During Low-speed Rear Impact from Kroonenberg, A. van den, Philippens, M., Cappon, H., Wismans, J., Hell, W., Langwieder, K.) an upward movement of the head of 35 mm is reported.
On the other hand the population in the Netherlands and Scandinavia seems to be taller than e.g. in the UK.
However the EEVC WG20 report “UK Cost-Benefit Analysis: Enhanced Geometric Requirement for Vehicle Head Restraints”, reported that a head restraint height of 840 mm and a backset of 40 mm would deliver the greatest benefit after subtracting the associated cost!
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 15
<number>
NL conclusions on needed head restraint height
In the Informal Group of GRSP on Head Restraints (phase 1) The Netherlands has proposed a head restraint height that would at least reach to 850 mm based on the principle of erect sitting height;
In the Informal Group of GRSP on gtr No.7 Head Restraints (phase2) the item of head restraint height has been further explored and for the above mentioned height, values of 830 and 840 mm seem better to serve more Parties.
The Netherlands concludes now that the head restaint height should at least reach to the values mentioned under the second bullet.
Update GRSP on actual needed HR height - Geneva, May 2012

## Slide 16
<number>
Thank you for your attention
Update GRSP on actual needed HR height - Geneva, May 2012