## Slide 1: 51st GRSP Session Helmets
Pierre CASTAING
 | Informal document GRSP-51-32 (51st GRSP, 21 - 24 May 2012, agenda item 13)

## Slide 2: Helmet Visor and Sunscreen
In the current Regulation 22, in § 6.15.3.4., we should test the luminous transmittance as specified below :
Visors shall have a luminous transmittance τv ≥ 80%, relative to the standard illuminant D65.
A luminous transmittance 80% > τv ≥ 50%, measured by the method given in § 7.8.3.2.1.1., is also permissible if the visor is marked with the symbol shown in figure 2 and/or with the English words “DAYTIME USE ONLY”. The luminous transmittance shall be measured before the abrasion test.

## Slide 3: Helmet Visor and Sunscreen
1- ECE R22-05 transparent visor Tv ≥ 80%
2- ECE R22-05 tinted visor 80% > Tv ≥ 50%
3- Visor supplied as spare parts with helmet
(but without type approval)
1
2
3
4
5
4- ECE R22-05 visor
5- Sunscreen integrated in Helmet, without type approval
We find on the market some helmets equipped with integrated sunscreen (5). These sunscreens are not approved according to ECE R22-05, and modify the luminous transmittance.
Moreover, helmet visors (3) which not met luminous transmittance criteria of ECE R22-05
could be found, as spare parts, on the market.

## Slide 4: French proposal
We will propose for next meeting a document to amend current ECE R22.05 in order to take into account this innovation.
This document will be based on the following principles :
  Authorises in ECE R22-05 tinted visor with lower light transmission
  Creates the sunscreen definition in ECE R22-05

## Slide 5: Principles
OR
OR
One layer
Two layers

## Slide 6: EN 1938 Goggles for motorcycle and moped users