## Slide 1: 51st GRSP Session Draft new Regulation on child restraint systems
Pierre CASTAING
 | Informal document GRSP-51-34 (51st GRSP, 21 - 24 May 2012, agenda item 20)

## Slide 2: Terms of Reference for Phase 2 and Phase 3
The informal group shall consider in Phase 2, the development into the new draft Regulation for "enhanced Child Restraint Systems used on-board of motor vehicles" of the necessary amendments to integrate the category of non-integral CRS with ISOFIX attachments and to extend the I-size concept to these CRS for consideration by GRSP.
The completion date for Phase 2 shall be targeted for the fifty-first session of GRSP (May 2012).
Phase 2 will develop definitions, performance criteria and test methods for non–Integral CRS with ISOFIX attachments (Restraint done for the adult safety belt).
In Phase 2, the test pulse for frontal impact (Increased severity and CRS integrity check) will be reviewed in the light of recent accident data.
In Phase 2, the strict application of recognized and accepted injury criteria related to the new generation baby/child crash test Q-dummies, as supported through the European Enhanced Vehicle-safety Committee (EEVC) and other EU research programs, will be reviewed in the light of recent accident data.
Develop transitional provision to withdraw ISOFIX application from Regulation No. 44 after WP.29 adopts Phase 1 and Phase 2.
The completion date for Phase 3 shall be targeted for the fifty-third session of GRSP (May 2013).
Phase 3 will develop the necessary amendments to upgrade Regulation No. 44 for the Seatbelt mounted CRS and Regulation Nos. 14 and 16 in order to introduce for this category of CRS the outcome of Phase 1 and 2.
The informal group will considers among others things, the technical expertise of EEVC working group 18 (WG.18), EEVC WG12, ISO TC22/SC12, the new program for the assessment of child-restraint systems (NPACS), the child advanced safety project for European roads (CASPER) as well as the results of the discussions held in the informal group and at GRSP.
If necessary, the informal group shall develop complementary test methods and propose alternative judgment criteria.
Consider appropriate measures to limit misuse of child restraint systems, in particular for children less than 15 months of age.

## Slide 3: Extended Mandate
The IWG asks GRSP to extend the mandate until the end of 2014
  Draft regulation for phase 2 (May 2013)
  Development of transitional provision to withdraw ISOFIX application from ECE R44 (December 2013)
  Draft regulation for phase 3 (May 2014)

## Slide 4: Meetings
01 February 2012 at EC – Brussels
11 & 12 April 2012 at CCFA – Paris
  Special dummies meeting on the 12
06 June 2012 at OICA – Paris
30 August 2012 at ACEA - Brussels

## Slide 5: Work on progress
Defines common interface on current vehicle fleet
  UTAC study to define a reference belt routing using 5th female dummy

## Slide 6
Z
X
▀ R44 anchorages

## Slide 7
Z
Y
▀ R44 anchorages

## Slide 8: Work on progress
Accident analysis focusing on booster
  CASPER Program reporting on boosters cushions and boosters seats available data (field and tests)
« ISOFIX » Booster seats - Recent data from the field
  Extracts from the first roadside survey of child restraint system use and misuse in Belgium

## Slide 9: Accident data : Conclusions
The protection of the abdomen is one of the priorities to improve the situation of restrained children in cars when restrained the seatbelt (with and without CRS)
Abdominal injuries occur often on organs located relatively high in the abdomen (liver and spleen) = likely due to submarining or diagonal belt excessive loading
Misuse is expected to increase the risk of abdominal injury (direct loading to the abdomen, increased risk of submarining, etc)
Extra analysis:
  appropriate/inappropriate use (what is the limit to be considered); misuse
  side impact – Left vs right (corrolate with organ injuries)

## Slide 10: Summary of roadside survey
Injury risks on the abdominal segment booster cushions and booster seats is higher than in harness systems and close to the one of seatbelt use only. ISOFIX CRS shows a global reduction of rate of misuse including booster seats (no technical reason found for that) In our matrix 3 important factors generator of abdominal injury :
  Belt under the arm
  Belt over the horn of the CRS
  “Far relax” position Booster connected with ISOFIX rigid anchorages does not show better results than when not connected (only one test performed)
Lots of tests show us that the weakest part of the Q6 dummy is the abdomen and the abdominal sensors seem to be a good predicting tool to evaluate abdominal injury risk.
The main criterion is the correct routing of the seatbelt !
Tests prove that the “additional seatbelt positioner device” amplify the risk of submarining through a poor positioning of the belt on the abdomen.

## Slide 11: Work on progress
Child Dummy Subgroup
  Validation of the drawing packages for Q0, Q1, Q1,5, Q3 dummies

## Slide 12
1- First meeting on April, the 12 in Paris
2- Representatives of laboratories from Germany/France/Italy/Japan/Spain/UK/US
+Humanetics
3- Data available for Q0 / Q1 / Q1 ½ /Q3
4- Data for Q6 and Q10 should be available later (dummies not used in Phase 1)
Presentation of documents from NHTSA to homogenize the methodology used for all
the dummies;
Start a common work on Q0 dummy with establishment of Excel sheet
with comments;
Sharing of the work:
Q1 ½  Dorel (and CSI)
Q1  CSI (and Dorel)
Q3  PDB and EC (represented by M.Hynd)
 | Informal document GRSP-51-xx (51st GRSP, 21 - 24 May 2012, agenda item 20)

## Slide 13
Calibration tools
Nomenclature
Dummy drawings

## Slide 14
Complete review of the data and report to Humanetics in order to improve the set
For introduction of the dummies in the future regulation
Next steps :
  collect the data from the participants before next IWG CRS meeting
  Provide these data to Humanetics
  Final set of data provided by Humanetics to be formatted in accordance with the standard presented by UK (numbering, etc.)