## Slide 1: Rechargeable Energy Storage systems (REESS) requirements
Gerd Kellermann, Germany
Informal document GRSP-51-35
(51st GRSP, 21 - 24 May 2012,
agenda item 17)

## Slide 2: Sequence of actions
<number>
Amended: Reg 100 SA 01 (3/2010)
Reg 12, 94, 95 (11/2010)
Reg 10 (3/2011)
Group of interested experts on Rechargeable Energy Storage systems
Nov. 2010 Bonn Jan. 2011 Paris
Apr. 2011 Boras Jul. 2011 Mainz
Oct. 2011 Madrid Jan. 2012 Brussels
Dec. 2011 Geneva GRSP inf.doc.
May 2012 Geneva GRSP formal and inf. doc
Notes: <number>

## Slide 3: Goal
Establish regulations for commercialization of EV
EV as save as ICE vehicles
Ensure safety in aftersale market (retrofitting)
<number>

## Slide 4: having in mind
<number>
do not hinder the fast development in high voltage vehicles but contribute to the new technology by avoiding discredit by accident
do not restrict the scope to Li-Ion batteries
2 way approach: REESS type approved as component or vehicle based
align with UN 38.3 as far as possible to reduce time and effort for testing (e.g. vibration)
consider existing IEC and ISO standards

## Slide 5: Amend existing regulation
The current Reg. 100 contains safety requirements for high voltage vehicles, i.e.
Protection against electrical shock
  Direct contact
  Indirect contact
  Isolation resistance
Avoid overheat of REESS
Ensure functional safety
Determine emissions for open type (lead acid) traction batteries
<number>

## Slide 6: integration in R 100
<number>
Develop a new Part II with REESS requirements
  5. Part I: Requirements of a vehicle with regard to its electrical safety 6. Part II: Requirements of a Rechargeable Energy Storage System (REESS) with regard to its safety
No restriction to high voltage batteries, but excluding batteries for starting the engine, lighting,.
Amend an annex with test procedures

## Slide 7: Requirements in Part II
<number>
1 Vibration
2 Thermal shock and cycling
3 Mechanical shock
4 Mechanical integrity
5 Fire resistance (if electrolyte is flammable)
6 External short circuit protection
7 Overcharge protection
8 Over-discharge protections
9 Over-temperature protection

## Slide 8: What has to be tested
Tests related to mechanical impact or fire can be conducted eather with the vehicle or with the component
In general test with REESS subsystems instaed of the whole REESS could be done, if the manufacturer demonstrate its representative
<number>

## Slide 9: Test conditions
Acceptance criteria - elektrolyte leakage - rupture - fire - explosion - isolation resistence after the test
Test procedure with starting conditions like state of charge, temperature, …
<number>

## Slide 10: open issue
<number>
Transport of damaged batteries (WP.15)
Instructions for rescue operation after crash (recommendations on a local/regional level)
Chemical safety (HF)
More experience till EOL will show whether reduced quality or increased risk at EOL lead to further amendments

## Slide 11
<number>
Thank you for your attention