## Slide 1
Japanese Proposal
for the New Regulation
JASIC / Japan
Informal document GRSP-51-39
(51st GRSP, 21 – 25 May 2012,
agenda item 20)
Notes: <number>
I will present the “Japanese proposal for the new regulation”.

## Slide 2
Background & Purpose
NTSEL (type approval test department in Japan) uses the acceleration type sled test system. So, it is necessary to compare the results of the CRS side impact sled test between when tested by the deceleration type sled system and when tested by the acceleration type sled test system.
We conducted CRS side impact sled tests using the acceleration type sled test system:
1. to compare the test severity between deceleration sled
and acceleration sled
2. to confirm main test parameters which determine
dummy injury measures.
Notes: <number>
The back ground of this research is that the NTSEL, which is the type approval test department in Japan, has the acceleration type sled system, and does not have the deceleration type sled system.
So we need to confirm that we can do the CRS side impact sled test by acceleration type sled test system.
And we done 2 series of test.
to compare the test severity between deceleration sled and acceleration sled
the main test parameters which determine the dummy injury measures. .

## Slide 3
Parameters of New Side Impact Test
Intrusion
Relative velocity between door and sled
Door intrusion
There are 2 parameters for the dynamic
Side Impact Test Procedure.
Notes: This shows the parameters of side impact test.
The relative velocity between sled and door, and door intrusion are the parameters.
<number>

## Slide 4
Concept of CRS Side Impact Test Using the Acceleration Type Sled System
Notes: Next we shows the concept of our sled test system
<number>

## Slide 5
Photos before sled tests
Our jig for the CRS side impact test
using the acceleration type sled system
Notes: <number>
This shows the photos of sled test initial conditions.
Seat is set on sled on sled and therefore seat can be easily moved.

## Slide 6
Video
Notes: This shows the video of test.
<number>

## Slide 7
Test Concept
The concept is that the door moves with the sled, and the seat moves on the sled.
Relative velocity
Intrusion
Door velocity
Notes: This shows the velocity and intrusion time histories.
Time of 0ms is defined when the door is at the end of the seat, defined in regulation.
The door velocity is maximum before time is 0ms, and the door velocity keep almost constant till the seat velocity catches up with the door.
The seat velocity start increasing almost at time is 0ms.
Relative velocity between the door and seat is in corridor.
The intrusion is the same with relative displacement of door and seat.
And the intrusion is almost 250mm and satisfy the regulation.
<number>

## Slide 8
Influence of Door Ground Velocity
Notes: Next we present about the main parameter which determined the dummy injury measures.
<number>

## Slide 9
Testing the Influence of Door Ground Velocity
6.6m/s
6.0m/s
5.3m/s
We tested 3 door ground velocities.
Door intrusions were the same.
Relative velocities were different.
Notes: We tested the 3 different door ground velocities.
Door intrusion were same.
Relative velocity were different because of the door velocity was small.
<number>

## Slide 10
Door ground velocities influences
dummy injury measures
Testing the Influence of Door Ground Velocity
Head resultant accelerations
Notes: This shows the velocity and dummy head resultant acceleration time histories.
We tested the door ground velocity at about 6.8m/s, 5.8m/s and 5.3m/s.
The dummy head injury measures were large when the door ground velocity was large.
And the dummy head injury measures were small when the door ground velocity was small.
So door ground velocity has influence to dummy injury measures.
<number>

## Slide 11
Dummy velocity catches up with door velocity.
Reason Why Door Ground Velocity Influences Dummy Injury Measures
To catch up with door velocity, the dummy needs to get enough energy. So, under the same conditions except for the door ground velocity in our tests, the relative velocity between door and dummy influences dummy injury measures.
Relative velocity between door and dummy is important.
Notes: The one of the reasons that door ground has influence to injury measures was that the need energy for dummy velocity to catch up with door velocity is based on the relative velocity between dummy and door.
In this test method, dummy is stayed so the relative velocity between dummy and door is due to the door ground velocity.
So probably the important parameter is not door ground velocity but the relative velocity between door and dummy.
<number>

## Slide 12
Influence of Relative Velocity between Door and Seat
Notes: Next speak about Relative velocity between door and seat
<number>

## Slide 13
Test of Influence of Relative Velocity
The relative velocities between door and seat, and door intrusions of 2 tests are almost similar.
Test A
Test B
Notes: We done 2 tests series.
Both tests, the relative velocity between door and seat is same.
But the door ground velocity is different.
Test A, the door ground velocity is constant and seat move and catch up with door.
Test B, the door ground velocity is changed in corridor and seat is stayed.
<number>

## Slide 14
Relative Velocity
Intrusion
Relative velocity and intrusion are almost same
Test of Influence of Relative Velocity
Notes: This shows velocity and intrusion time histories.
Relative velocity of Test A and B were almost same.
<number>

## Slide 15
Same relative velocity but different injury measures
⇒ The relative velocity has little
influence on injury measures.
Dummy head acceleration
Test of Influence of Relative Velocity
Notes: This shows dummy head injury measures.
Injury measures of test A are high and those of test B are low.
So injury measures in 2 tests were different though the relative velocity is almost same and in corridor.
This shows that the relative velocity had little influence to injury measures.
<number>

## Slide 16
Velocity
Time
Problem of the Test Procedure
Relative Velocity
Corridor
Door Velocity
Seat Velocity
The current draft regulation that defines solely relative velocity allows various test conditions to be set.
Notes: So we think that the test parameter of the regulation is not sufficient.
And the reason why relative velocity has little influence to injury measures is that if parameter is only relative velocity, there are many conditions for doing the test.
<number>

## Slide 17
Velocity
Time
Problem of the Test Procedure
Relative Velocity
Corridor
Door Velocity
Seat Velocity
The door speed is constant and the seat is moved rapidly
(Test A condition)
Impact time of
dummy and Door
Relative velocity
between door
and dummy
Notes: This shows the velocity time histories of door, seat and relative about the test that the door velocity is constant, for example test A.
<number>

## Slide 18
Velocity
Time
Relative Velocity
Corridor
Door Velocity
Seat Velocity
Problem of the Test Procedure
The door speed decreases and the seat stops
(Test B condition)
Impact time of
dummy and Door
Relative velocity
between door
and dummy
Notes: This shows the velocity time histories of door, seat and relative when seat stays, for example test B.
The relative velocity between door and dummy was smaller than that of the case door velocity is constant,
<number>

## Slide 19
Velocity
Time
Problem of the Test Procedure
Relative Velocity
Corridor
Door Velocity
Seat Velocity
The door speed decreases and the seat moves
(Various conditions between Test A and B)
Impact time of
dummy and Door
Relative velocity
between door
and dummy
Notes: And the conditions between test A and B are various, the door velocity decrease and seat velocity increase case, relative velocity between door and seat is in corridor.
So the relative velocity between door and dummy are various between test A and B.
<number>

## Slide 20
We get same results using the deceleration sled,
if the door is moving when the door hit the CRS.
Same Results in Deceleration Type Sled
Dummy
SLED
Door
CRS
Notes: Same thing can be done in deceleration type sled if the door is moved.
<number>

## Slide 21
Velocity
Time
Relative Velocity
Corridor
Door Velocity
Seat Velocity
The door stops and the seat speed decreases in corridor
(Same condition as Test A)
Problem of the Test Procedure
in Deceleration Type Sled
Impact time of
dummy and Door
Relative velocity
between door
and dummy
Notes: This is the velocity time histories of door, seat and relative between door and seat at condition that door stay.
This is the same condition of test A.
<number>

## Slide 22
Velocity
Time
Problem of the Test Procedure
in Deceleration Type Sled
Relative Velocity
Corridor
Door Velocity
Seat Velocity
The door speed increases and the seat speed is constant
(Same condition as Test B)
Impact time of
dummy and Door
Relative velocity
between door
and dummy
Notes: This shows the velocity time histories at the condition that seat velocity is constant and door velocity catch up the seat.
<number>

## Slide 23
Velocity
Time
Relative Velocity
Corridor
Door Velocity
Seat Velocity
The door speed increases and the seat speed decreases
(Various conditions)
Problem of the Test Procedure
in Deceleration Type Sled
Relative velocity
between door
and dummy
Impact time of
dummy and Door
Notes: And there are various conditions between the door staying and the constant of seat.
<number>

## Slide 24
Same Severity Condition
Relative Velocity
Corridor
Door Velocity
Seat Velocity
The relative velocity between the door and the dummy is the same, both tested by moving the door at a constant speed on the acceleration type sled, and tested by keeping the door fixed on the deceleration type sled.
Velocity
Time
Impact time of
dummy and Door
Velocity
Time
Relative velocity
Between door
and dummy
Acceleration type sled
Deceleration type sled
Notes: This shows the worst case of acceleration type sled and deceleration type sled.
Severity of 2 tests are almost similar.
And we need another test parameters to define the test conditions.
<number>

## Slide 25
Conclusion
It is possibility that the relative velocity between door and dummy influences dummy injury measures.
Under the condition which satisfy the CRS side impact test procedure of the new regulation, dummy injury measures varied.
The current draft regulation that defines solely relative velocity allows various test conditions to be set.
Additional conditions are needed for the CRS side impact test procedure of the new regulation to make the conditions the same in various tests.
Notes: Conclusion
It is possibility that the relative velocity between door and dummy has influence to dummy injury measures.
Under the condition which satisfy CRS side impact test procedure of new regulation, different dummy injury measures were got.
Various test conditions are made under the now test procedure that only relative velocity is defined
Additional conditions are need for CRS side impact test procedure of new regulation to make same condition in various tests.
<number>

## Slide 26
Japanese Proposal
Add door ground velocity to define one test condition
In a test which the door is moving at T = 0ms, (i) the door ground velocity shall be between [6.375m/s] and [7.25m/s] at least the time when the door intrusion is maximum, and (ii) dummy is stayed at T = 0ms.
In a test which the door is stayed at T = 0ms, (i) the door shall be fixed, and (ii) the dummy’s [chest] ground velocity shall be between [6.375m/s] and [7.25m/s] at T = 0ms.
Notes: This is Japanese proposal.
Add door ground velocity to define one test condition
Test that door is moving at T = 0ms, door ground velocity is kept between [6.375m/s] and [7.25m/s] at least before the time when the door intrusion is maximum and dummy is stayed at T = 0ms.
Test that door is stayed at T = 0ms, the door ground velocity is kept 0 m/s during the test and dummy [chest] velocity is between [6.375m/s] and [7.25m/s] at T = 0ms.
<number>

## Slide 27
Japanese Proposal
Velocity
Time
Relative Velocity
Corridor
Door Velocity
Seat Velocity
Additional corridor
Acceleration type sled
Notes: This shows the proposal of acceleration type sled.
<number>

## Slide 28
Japanese Proposal
Relative Velocity
Corridor
Door Velocity
Seat Velocity
Add door velocity
Deceleration type sled
Velocity
Time
Add dummy velocity at T = 0ms
Notes: This shows the proposal of deceleration type sled.
<number>