## Slide 1: A Proposal Related to the Establishment of a New Regulation for Category L
JASIC
Informal document GRSP-52-09
(52nd GRSP, 11–14 December 2012,
agenda item 18)
Notes: <number>

## Slide 2
Ⅰ. Proporsal
*R100 (electrical/battery safety standards for electric vehicles) is a standard based on the 4-wheel configuration.
*For uniform regulations covering categories M/N/L, adoption by individual countries and harmonization across the
categories at revision is essential.
This may possibly cause delays especially between categories with substantially different structures or design concepts.
->A separate regulation should be established for category L whose structures and safety concept are
different from others. (See the other regulations for these categories below.)
R46
R???
R100
L6/7
R41
R51
Noise
R40
R83
Emission regulations
R9
M/N
L
L2/4/5
L3
L1/2
Engine type
R63
L1
L3/4/5
R4/5/7/19/31/65/77/91/98/99/112/113/123
R116
R30
R13H
With passenger compartment
More freedom for passengers
Vehicle weight of 1 t or more
Crushable zone and seat restraint
to protect passengers
Crash requirements
Lamps
Tyres
Braking
Rear-view mirrors
Electric shock/battery safety
Passenger compartment
Handle mount
Driving on flat tyres
Body stability
Passenger compartment
Anti-theft devices
Vehicle/engine structure
Vehicle structure
Driving backward
R50/56/74/76/82/113
Functional complexity
R62
R75
R78
R81
L1~5
衝突要件なし
Both hands required for operation
(Less freedom for passengers)
No compartment
Light weight up to approx. 200 kg
Separation and protectors to
protect passengers
Passenger protection concept
Vehicle structure/size
Driving mode (usage)
Social demand
L1/2/6
L1/2/5
L1~5
L1
L1~7
L1~7
R47
L1/2
Notes: <number>

## Slide 3
Passenger’s posture onboard
Passenger Compartment
Body Shell
Sit-in
Saddled
More freedom
3395*1475*1610 1070 kg
1830*695*1065 mm 106 kg
No Body Shell &
Passenger Compartment
R???
R100
Passenger protection concept
Vehicle structure/size
Electric shock/battery safety
Vehicle structure/size
Portable Battery
→Direct Contact Requirement
→Add Battery Drop Requirement
Small size/light weight
Balancing required and less freedom
Drop
Ⅱ. justification
Passenger freedom
→ Protection Degree
For Direct Contact
Notes: <number>

## Slide 4
Helmet
Gloves
Boots
Long
Sleeves
Right Wearing!
Seat Belt
Air Bag
Protectors
Passenger Compartment
Body Shell
Crushable Zone
Crushable Zone
Sit-in
Saddled
No Body Shell &
Passenger Compartment
Post-Crash Requirement
R???
R100
Passenger protection concept
Vehicle structure/size
Electric shock/battery safety
Passenger protection concept
Restraint
Separate
No need to require the time to go out of the vehicle
→Mechanical Integrity
→Fire Resistance
Component test only for category L
→Mechanical Integrity
→Mechanical Impact
→
Notes: <number>

## Slide 5
END
With regard to the proposed addition of category L to R100,
it is appropriate to establish a new regulation for category L separately from categories M/N because the former is different from the latter in terms of structure and safety concept.
Notes: <number>