## Slide 1: Flex PLI GTR Status
1-2 December 2011
Bernard Been
Informal Group GTR9 PH2
GTR9-1-08r1
Notes: <number>

## Slide 2: Content
Number of GTR legs manufactured
Flex Status
Leg availability
GTR9-1-08r1

## Slide 3: Number of GTR Legs Made
3 JARI prototypes
3 Humanetics for internal testing, demo and CAE
22 customer legs have been sold
12 legs are on order
All customer legs have onboard DAS
Some with optional addition channels up to 24
GTR9-1-08r1

## Slide 4: Flex Status
All production legs have Vinyl ester bones (more durable) Some prototypes have been updated to Vinyl ester
All legs were build passing agreed GTR static component corridors
All production legs pass GTR Pendulum corridors
  T3 and T4 are usually high and MCL is generally low
Production legs consistently fail some Inverse GTR corridors
  some tibia moment channels are too low
  failure very repeatable
4 different batches of Vinyl ester bone have been used
From test experience Humanetics currently manufactures bones to be as close to GTR inverse corridors as possible
GTR9-1-08r1

## Slide 5: Example 2011 Production Pendulum Results
Pendulum |  |  | SN DH5646 |  |  |  |  | SN DG0726 |  |  |  | SN DG6304 |  |  |  | SN DH6791 |  | 
Date |  |  | 3/21/2011 | 3/21/2011 | 4/1/2011 | 4/7/2011 |  | 4/29/2011 | 5/2/2011 | 5/16/2011 |  | 6/16/2011 | 6/16/2011 | 6/17/2011 |  | 5/5/2011 | 5/6/2011 | 5/6/2011
Test site | Low | High | Plymouth | Plymouth | Nagoya | Nagoya |  | Plymouth | Plymouth | BAST |  | Plymouth | Plymouth | Plymouth |  | Plymouth | Plymouth | Plymouth
Peak Moment @ T1 | 235 | 272 | 243.29 | 245.57 | 246.97 | 252.70 |  | 251.00 | 246.83 | 248.30 |  | 244.25 | 244.33 | 243.67 |  | 247.76 | 247.71 | 248.41
Peak Moment @ T2 | 185 | 211 | 198.12 | 199.87 | 199.64 | 205.10 |  | 207.98 | 204.93 | 199.50 |  | 199.49 | 199.54 | 198.98 |  | 204.72 | 204.12 | 204.63
Peak Moment @ T3 | 135 | 160 | 152.92 | 154.93 | 151.24 | 156.50 |  | 159.07 | 155.94 | 150.30 |  | 151.61 | 151.77 | 151.08 |  | 156.46 | 155.79 | 153.01
Peak Moment @ T4 | 94 | 108 | 102.79 | 103.89 | 102.89 | 107.00 |  | 109.33 | 106.83 | 101.50 |  | 102.39 | 102.45 | 101.50 |  | 106.91 | 106.50 | 106.52
Peak ACL Elongation | 9 | 11 | 10.02 | 9.99 | 10.03 | 10.20 |  | 9.23 | 9.07 | 9.90 |  | 9.23 | 9.24 | 9.25 |  | 9.55 | 9.90 | 9.68
Peak MCL Elongation | 23 | 26 | 22.87 | 23.08 | 23.17 | 23.60 |  | 23.14 | 22.96 | 22.90 |  | 22.67 | 22.70 | 22.72 |  | 23.14 | 23.08 | 23.18
Peak LCL Elongation | 2 | 4.5 | 3.24 | 3.18 | 3.19 | 4.30 |  | 3.66 | 3.54 | 3.10 |  | 2.86 | 2.86 | 2.86 |  | 4.10 | 3.93 | 3.97
Peak PCL Elongation | 4 | 5.4 | 4.09 | 4.18 | 4.27 | 2.00 |  | 4.94 | 5.06 | 4.20 |  | 4.93 | 4.95 | 4.96 |  | 4.76 | 4.45 | 4.53
Femur stiffness |  |  | mid |  |  |  |  | High |  |  |  | MID |  |  |  | Low |  | 
Femur thickness |  |  | 10.44mm |  |  |  |  | 10.38mm |  |  |  | ? |  |  |  | ~10.3 |  | 
Femur Batch |  |  | B2 |  |  |  |  | B2 |  |  |  | B2 |  |  |  | B2 |  | 
Tibia stiffness |  |  | mid-high |  |  |  |  | High |  |  |  | MID |  |  |  | Medium |  | 
Tibia thickness |  |  | 10.36mm |  |  |  |  | 10.67mm |  |  |  | ? |  |  |  | 10.4 |  | 
Tibia Batch |  |  | B2 |  |  |  |  | B3 |  |  |  | B2 |  |  |  | B3 |  | 
Tibia Assembly |  |  | Pass |  |  |  |  | Pass |  |  |  | Pass |  |  |  | Pass |  | 
Femur Assembly |  |  | Pass |  |  |  |  | Pass |  |  |  | Pass |  |  |  | Pass |  | 
Knee Assembly |  |  | Pass |  |  |  |  | Pass |  |  |  | Pass |  |  |  | Pass |  | 
 |  |  |  | 1/2 turn to springs |  | With SLICE |  |  |  |  |  |  |  |  |  |  |  | 
GTR9-1-08r1

## Slide 6: Example 2011 Production Inverse Results
Inverse |  |  | SN DH5646 |  |  | SN DG0726 |  |  | SN DG6304 |  |  | DH6791 |  | DI6014
Date |  |  | 4/19/2011 | 4/20/2011 |  | 4/29/2011 | 5/16/2011 |  | 6/17/2011 | 8/4/2011 |  | 4/20/2011 |  | 6/2/2011
Test site |  |  | Plymouth | Plymouth |  | Plymouth | BAST |  | Plymouth | BAST |  | Plymouth |  | Plymouth
Pre Impact velocity | 10.9 | 11.3 | 11.05 | 11.34 |  | 11.34 | 11.09 |  | 11.24 | 11.15 |  | 11.24 |  | 11.24
Peak Moment @ T1 | 237 | 277 | 0.00 | 257.14 |  | 237.73 | 250.30 |  | 241.32 | 246.8 |  | 231.48 |  | 241.01
Peak Moment @ T2 | 223 | 269 | 228.26 | 232.05 |  | 221.94 | 229.50 |  | 222.27 | 224.1 |  | 216.31 |  | 217.43
Peak Moment @ T3 | 176 | 204 | 173.37 | 180.00 |  | 169.13 | 177.70 |  | 170.39 | 170.5 |  | 171.09 |  | 167.68
Peak Moment @ T4 | 98 | 120 | 98.19 | 101.26 |  | 93.42 | 97.40 |  | 97.06 | 97.3 |  | 99.40 |  | 97.11
Peak ACL Elongation | 8.5 | 10.5 | 8.28 | 8.75 |  | 9.27 | 8.70 |  | 9.26 | 9.7 |  | 8.22 |  | 9.55
Peak MCL Elongation | 18 | 23 | 19.77 | 19.73 |  | 19.59 | 19.10 |  | 19.33 | 20.3 |  | 16.24 |  | 19.42
Peak PCL Elongation | 4.5 | 6 | 0.01 | 5.83 |  | 5.34 | 5.10 |  | 5.62 | 5.4 |  | 4.38 |  | 6.27
Femur stiffness |  |  | mid |  |  | High |  |  | MID |  |  | Low |  | High
Femur thickness |  |  | 10.44mm |  |  | 10.38mm |  |  | ? |  |  | ~10.3 |  | ?
Femur Batch |  |  | B2 |  |  | B2 |  |  | B2 |  |  | B2 |  | B3
Tibia stiffness |  |  | mid-high |  |  | High |  |  | MID |  |  | Medium |  | High
Tibia thickness |  |  | 10.36mm |  |  | 10.67mm |  |  | ? |  |  | 10.4 |  | ?
Tibia Batch |  |  | B2 |  |  | B3 |  |  | B2 |  |  | B3 |  | B2
Tibia Assembly |  |  | Pass |  |  | Pass |  |  | Pass |  |  | Pass |  | Pass
Femur Assembly |  |  | Pass |  |  | Pass |  |  | Pass |  |  | Pass |  | Pass
Knee Assembly |  |  | Pass |  |  | Pass |  |  | Pass |  |  | Pass |  | Pass
GTR9-1-08r1

## Slide 7: Leg Availability for Testing
Humanetics proposes at least 6 legs should be tested for corridor definition at 6 labs minimum after they have been checked and certified
Availability of legs for testing would depend on customer co-operation
Humanetics would make their internal leg available for testing
GTR9-1-08r1

## Slide 8
Thank you for your attention!
GTR9-1-08r1