## Slide 1: Update on Pedestrian Leg Testing
National Highway Traffic Safety Administration
49th GRSP Session May 2011
Nha Nguyen
<number>
Informal document GRSP-49-23
(49th GRSP, 16-20 May 2011,
agenda items 4(a))
GTR9-1-12

## Slide 2: Pedestrian Leg Testing
Projectile leg simulates a moving vehicle hitting a stationary pedestrian
<number>

## Slide 3: Pedestrian Legforms
TRL
Flex-GT
Flex-GTR
<number>

## Slide 4: Background
The Flex-GTR had not been tested against aggressive vehicles in the US fleet and there was concern about its durability
There was also concern about topping out the Flex-GTR’s measurement limits (Mallory, 2010)
Fracture
Bend
Shear
<number>

## Slide 5: Goals of the Testing
This series of impacts was done to test the Flex-GTR against aggressive US vehicles to see if it would survive
Confirm whether the Flex-GTR legform can distinguish marginally performing vehicles from poor performing vehicles
<number>

## Slide 6: Test Sequence
Due to durability concerns, the TRL legform was tested on each vehicle first to rank the vehicles in order of increasing aggressiveness
The Flex-GT was then tested on each vehicle to rank them for the Flex-GTR tests
This allows us to get in as many tests as possible before possibly damaging the legform
<number>

## Slide 7
Volkswagen Passat
Mazda Miata
Honda Civic
<number>

## Slide 8
Honda Pilot
Chevrolet Silverado
Chevrolet Equinox
<number>

## Slide 9: Test Results
<number>

## Slide 10
TRL Test Results
*Performed under GTR conditions with legform 25 mm above ground reference level
<number>

## Slide 11
Flex-GT Test Results
*Performed under GTR conditions with legform 25 mm above ground reference level
<number>

## Slide 12
Flex-GTR Test Results
*Performed under GTR conditions with legform 75 mm above ground reference level
<number>

## Slide 13: Comparison of Results TRL vs GTR
<number>

## Slide 14
Comparison of Results – TRL vs Flex-GTR
<number>

## Slide 15
Comparison of Results – TRL vs Flex-GTR
<number>

## Slide 16: Summary of Findings
The Flex-GTR measures lower values than the TRL legform
The current Flex-GTR seems to be able to distinguish differences in relatively aggressive vehicle bumper designs better than the previous version
<number>

## Slide 17
Sensitivity
Testing with a previous version of the Flex-GTR legform showed an inability of the legform to distinguish among vehicles that performed poorly
  Measurements reached a limit (Mallory, 2010)
Improvement in the current series of tests may be due to changes in Flex-GTR legform
  Cable stop gap increase
    Femur: 8 mm  9.1 mm
    Tibia: 9 mm  10.3 mm
Three additional tests performed on the centers of the three passenger cars
Fracture
Bend
Shear
<number>

## Slide 18
Volkswagen Passat
Mazda Miata
Honda Civic
<number>

## Slide 19
Comparison of Old and New Flex-GTR Data – Center Impacts
<number>

## Slide 20: Summary of Findings
The Flex-GTR measures lower values than the TRL legform
The current Flex-GTR seems to be able to distinguish differences in relatively aggressive vehicle bumper designs better than the previous version
  Topping out is not a concern with the current Flex-GTR
Flex-GTR repeatability was not directly evaluated, but
  Silverado Flex-GTR tests 1001 and 1002 showed similar numbers at the same impact location, which is promising
<number>

## Slide 21: Flex-GTR Repeatability – Chevy Silverado
Injury Measurement |  | Injury Reference Value (FlexTEG) | Chevrolet Silverado | 
Impact Location |  |  | Center | 
 |  |  | GTR (1001) | GTR (1002)
Femur Moment (Nm) | Femur 3 (Upper) | --* | 73.67 | 77.28
 | Femur 2 (Middle) |  | 139.48 | 138.52
 | Femur 1 (Lower) |  | 252.05 | 245.58
Tibia Moment (Nm) | Tibia 1 (Upper) | 340 Nm (380 Nm) | 332.73 | 332.61
 | Tibia 2 (Mid Upper) |  | 311.07 | 319.53
 | Tibia 3 (Mid Lower) |  | 233.53 | 237.41
 | Tibia 4 (Lower) |  | 110.52 | 107.91
MCL Elongagtion (mm) |  | 22 mm | -- | 22.28
ACL Elongation (mm) |  | 13 mm | 8 | 7.87
PCL Elongation (mm) |  | 13 mm | 5.41 | 5.61
LCL Elongation (mm) |  | --* | -4.16 | -3.76
Tibia Acceleration (g) |  | --* | -59.21 | -59.39
Velocity (m/s) |  | --* | 11.055 | 11.137
<number>

## Slide 22: Summary of Findings
The Flex-GTR measures lower values than the TRL legform
The current Flex-GTR seems to be able to distinguish differences in relatively aggressive vehicle bumper designs better than the previous version
    Topping out is not a concern with the current Flex-GTR
Flex-GTR repeatability was not directly evaluated, but
  Silverado Flex-GTR tests 1001 and 1002 showed similar numbers at the same impact location, which is promising
The Flex-GTR was observed to be durable
  Survived US vehicles
  A majority of the issues that were observed were minor and repairable
<number>

## Slide 23
Observations and Durability Assessment (Flex-GT)
Pinching of wires between blue tab and metal knee condyle
Wear and tear of plastic sheath around knee tension cables
Pushed Surface of the Legform
<number>

## Slide 24
Observations and Durability Assessment (Flex-GT)
Tibia and Femur knee blocks are rotated/not flush with each other
Pushed Surface of the Legform
<number>

## Slide 25
Observations and Durability Assessment (Flex-GTR)
Misalignment of the knee after Passat and Miata impacts
Tear in the neoprene skin and scratches on the femur knee block
<number>

## Slide 26: Issues with Flex-GTR
Needed to modify the legform in order for its flight to be within GTR tolerances for forward pitch (specific to the VRTC launch system)
  Removed black protective end caps
  Konosu-san (JARI) informed us that they cut out notches at the top and bottom of the launch plate to accommodate for the end caps
Femur strain gauge #2 (middle gauge)
  Broken gauge/wire
  Still being investigated
<number>

## Slide 27: Summary of Findings
Durability:
  The Flex-GTR seems to be able to distinguish differences in relatively aggressive vehicle bumper designs better than the previous version
  Flex-GTR repeatability was not directly evaluated, but
    Silverado Flex-GTR tests 1001 and 1002 showed similar numbers at the same impact location, which is promising
  The Flex-GTR was observed to be durable
    Survived US vehicles
    A majority of the issues that were observed were minor and repairable
<number>

## Slide 28: Summary of Findings
<number>
Injury criteria:
  The Flex-GTR measures lower values than the TRL legform
  Injury results were not consistent with previous testing:
    Previous study has shown that it’s rare to injure the ACL or PCL without injuring MCL. However, in the VW and Honda Civic tests, we observed ACL elongation that exceeded the injury criteria before the MCL exceeding injury criterion.
  The findings raise concerns on whether the Flex GTR is properly modeling the impact or that the injury criteria are appropriate

## Slide 29: Conclusion
<number>
Flex-GTR legform is found to be durable
Additional research and testing needed to address the injury criteria concerns
Currently, more world fleet data is needed
Different evaluation criteria may result in different counter-measures (design and cost benefit)

## Slide 30
Thank you
<number>