## Slide 1
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>
Wet Grip for C3 tyres
Minimum Type Approval Level
Informal document GRRF-75-02
(75th GRRF, 17-19 September 2013,
agenda item 7(b))
Submitted by ETRTO
(Reissued on 11/09/2013 for technical reasons)
Notes: <number>

## Slide 2: Proposal (ref. GRRF-73-18e) Minimum Type Approval Value (Safety Net)
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>

## Slide 3: Justification
Due to new efforts of CO2 reduction linked to heavy goods vehicles and buses, for instance within the European Union (EU), it may be expected that tyre manufacturers will begin improving the rolling resistance of C2 and C3 tyres as we have seen for C1 tyres. It is also commonly known that a reduction of the rolling resistance may also lead to a reduction of the tyre’s wet grip properties.
As can also be read in the recitals (17) and (19) of the General Safety Regulation (EC) 661/2009 in force in the EU, and referring directly to Regulation No. 117, it is deemed appropriate to set out requirements concerning wet grip requirements ensuring that tyre safety levels are maintained (safety net).
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>

## Slide 4: Justification (con’t)
Back in 2004, the same rational was followed, proposed and approved by the Contracting Parties of GRRF for C1 tyres.
It is recognized that C2 and C3 tyres available on the market today are indeed sufficiently safe in terms of wet grip and the current minimum performance levels should be taken as a baseline for the minimum type-approval values.
For C3 tyres, harmonization on world-wide level is desirable, recognizing the alignment already in place between Brazil for C1, C2 and C3 tyres and Korea for C1 and C2 tyres.
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>

## Slide 5: GRRF outcome
GRRF agreed on the proposal from F, EC and ETRTO as amended in Annex VII to the report of the last February meeting and requested ETRTO to provide technical data supporting the choice of the proposed limit values for C3 tyres before the next GRRF session in September 2013.
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>

## Slide 6: Action
For that purpose, ETRTO initiated the following:
To collect market data from public databases reporting the value of the wet grip index indicated on the tyre label of most of the tyre sizes sold in Europe.
To update the State of Art 2010 as presented in the document GRB-73-18.
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>

## Slide 7: Market Data (Lizeo) Wet Grip value per Brand
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>
Global market
Nb of tyre sizes: 1453 / 2933
Volume: 10 205 033 / 11 796 103
Technology
Brand
Nb of sizes
Wet Grip Index
A > 1,25
B 1,10-1,25
C 0,95-1,10
D 0,80-0,95
E 0,65-0,80
F < 0,65

## Slide 8: Other data
Other public databases have been analyzed:
TOLEnergy with 1808 different tyre sizes
EDIWHEEL with 1681 different tyre sizes
The ETRTO / JATMA State of Art of 2010 has been updated.
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>

## Slide 9: Comparison between market data LIZEO, EDIWHEEL and TOLEnergy and ETRTO/JATMA SoAs
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>
 | TOLEnergy |  | LIZEO |  | EDIWHEEL |  | ETRTO/JATMA State of Art | 
 |  |  |  |  |  |  | Year 2010 | Year 2013
Wet Grip Index | % | Nb of sizes | % | Nb of sizes | % | Nb of sizes | % | %
> 1,25 | 3.3% | 60 | 2.8% | 40 | 2.9% | 48 | 0.3% | 2.8%
1,10-1,25 | 32.0% | 576 | 30.0% | 440 | 32.0% | 539 | 21.3% | 37.0%
0,95-1,10 | 59.0% | 1066 | 64.0% | 935 | 59.0% | 995 | 63.2% | 53.0%
0,80-0,95 | 5.5% | 99 | 3.9% | 57 | 5.4% | 90 | 14.9% | 6.7%
0,65-0,80 | 0.4% | 7 | 0.3% | 4 | 0.5% | 9 | 0.4% | 0.4%
< 0,65 | 0.0% | 0 | 0.0% | 0 | 0.0% | 0 | 0.0% | 0.0%
Number of sizes in the database | 1808 |  | 1453 |  | 1681 |  |  | 

## Slide 10: Analysis
Both sources, ETRTO / JATMA State of Arts (SoA) and Public databases are comparable.
The population of tyres having a WGI in the range 0,65 to 0,80 is between 0.3 and 0.5 %
There are no tyres with WGI below 0,65.
A deeper analysis of tyres with WGI in the range between 0,65 to 0,80 indicates that some of those tyres have been developed for specific performances like, for instance, grip in ice condition and not necessarily for rolling resistance, wet grip or rolling noise.
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>

## Slide 11: Conclusions
The above technical data are supporting the choice of the proposed minimum type approval value of 0,65 for Normal, Traction and Snow tyres of class C3. This represent an adequate safegard to maintain the current performance on wet grip.
Raising the limit would remove from the market safe tyres that have been developed for specific performances (like special use, ice …) and would need to redevelop a significant number of tyres which, consequently, increase the tyre manufacturer cost without proven benefits on safety.
In setting minimum values, a “margin of error” due to the challenges posed by the Wet Grip test method variability has to be considered.
It has to be noted that Brazil and Korea adopted already minimum performance level as proposed by the tyre industry, while still ensuring a sufficient level of safety, as no issues in the field are observed.
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>

## Slide 12
Thank you!
T h e E u r o p e a n T y r e a n d R i m T e c h n i c a l O r g a n i s a t i o n
<number>