## Slide 1
Traffic Accidents caused by Lane Departure in Japan
Data of Traffic Accidents around Japan
Transmitted by the expert from Japan
Informal document GRRF-75-33
(75th GRRF session (17-19 September 2013, agenda item 9(b))

## Slide 2: Discussion points in 74th GRRF
Q1. What is the result of the Impact Assessment of
LKAS?
Q2. Does making a new regulation become
restriction to the new technologies?
Q3. Which is better, amendment of R79 or
making a new regulation?
Q4. Should LKAS become “mandatory” or “if
fitted”?
Q5. What is the schedule? (Is setup of the
informal meeting necessary?)

## Slide 3: Discussion points in 74th GRRF
In Japan, concerning commercial vehicles, the
number of lane departure accident caused by
disturbance of consciousness or drowsy driving
which cannot be covered by LDWS was 7608,
and also the number of fatal accident was 443 for
10 years from 2001 to 2011.
Q1. What is the result of the Impact Assessment
of LKAS?

## Slide 4: Discussion points in 74th GRRF
In Europe, concerning category 1,2,3 vehicles, it is
estimated that the number of lane departure
accident caused by disturbance of consciousness
or drowsy driving was maximum 19313 incidents,
and also the number of fatal accident was
maximum 1131 for one year in 2006.
Not all the above accidents can be prevented by
LDWS. However it is considered that if the vehicles
equipped with LKAS, most of them might be
prevented.
Q1. What is the result of the Impact Assessment
of LKAS?

## Slide 5
The number of Lane Departure Accidents of commercial vehicles (in Japan)
- Lane Departure Accidents on commercial vehicles - (2009 - 2011)
Percentage of Disturbance of Consciousness and Drowsy Driving

## Slide 6
- The number of Lane Departure Accidents in case of Disturbance of Consciousness and Drowsy Driving - (2001 - 2011)
The number of the lane departure accidents (the disturbance of consciousness and the drowsy driving situation) is calculated by the percentage of lane departure accidents on commercial vehicles.
Estimated number of Lane Departure Accidents of Category 1-3 (in Japan)

## Slide 7
- The number of Lane Departure Accidents in case of Disturbance of Consciousness and Drowsy Driving based on the impact assessment of LDWS using the ratio of Japanese commercial vehicle accident -
Estimated number of Lane Departure Accidents
(in EU)
Data from
STATS19(GB)
GIDAS(D)
(provided by TRL)
Notes: <number>

## Slide 8
Estimation of Effectiveness of LDWS
on the Japanese highway
This estimation investigates the relationship between the effectiveness of LDWS and the road dimension in the Japanese highway

## Slide 9
Dimension of Highway in Japan
B(Right side)
A(Left side)
Road dimension on the outside of the lane (Regulation of highway road dimension in Japan)
Estimation of Effectiveness of LDWS on the Japanese highway
Estimation calculates the timing of the driver’s avoiding action.
- When the driver can control the steering after the warning system activation -
Time
Activation of warning system
Driver’s avoiding action
Reaction time
Driver’s avoiding action

## Slide 10
Estimation of Effectiveness of LDWS on the Japanese highway
6.5.2. The LDWS shall provide the lane departure warning indication mentioned in paragraph 5.4.1. at the latest when the outside of the tyre of the vehicle’s front wheel closest to the lane markings crosses a line 0.3 m beyond the outside edge of the visible lane marking to which the vehicle is being drifted.
Requirements of LDWS
6.5.1. Maintaining the prescribed speed, gently drift the vehicle, either to the left or the right, at a rate of departure of between 0.1 and 0.8 m/s so that the vehicle crosses the lane marking. Repeat the test at a different rate of departure within the range 0.1 and 0.8 m/s.
Rate of departure of LDWS
Maximum rate of departure is 0.8 m/s in test procedure of LDWS
LDWS shall activate the warning system until the departing of 0.3m from the outside of the lane.
Driver’s response time is 0.8[s] for the purpose of collision avoidance.
Driver’s response time in AEBS
0.3m
Driver’s avoiding action
0.8[s] × 0.8[m/s]
=0.64[m]

## Slide 11
This estimation investigates the relationship between the effect of LDWS and the road condition in Japan
Conclusion:
When we take into account of the Japanese highway dimension, in some cases LDWS is not enough to avoid the vehicle hitting the side wall.
Estimation of Effectiveness of LDWS on the Japanese highway
Calculating formula:
Margin= (Road dimension – Warning timing[0.3m]) – (Response time[0.8s] × Rate of
departure[0.8m/s])
*Minus means that the driver control the steering after the vehicle collide the side wall.

## Slide 12
In Japan, it is estimated that 44 fatalities can be reduced per one year in addition to the effectiveness of LDWS.
In EU, by using Japanese accident data of disturbance of consciousness and drowsy driving , it is estimated that maximum 1131 fatalities can be reduced per one year in addition to the effectiveness of LDWS.
In addition, when we take into account of the Japanese highway dimension, effectiveness of avoiding side wall hitting can be expected in the condition of no disturbance of consciousness and not drowsy driving .
Summary of LKAS Effectiveness Estimation

## Slide 13: Discussion points in 74th GRRF
Q2. Does making a new regulation become
restriction to the new technologies?

## Slide 14: Discussion points in 74th GRRF
Q3. Which is better, amendment of R79 or
making a new regulation?
For Japan, we don’t stick to establishing a new
regulation.

## Slide 15: Discussion points in 74th GRRF
Q4. Should LKAS become “mandatory” or
“if fitted”?
Japan does not see any necessity to make the
LKAS regulation as mandatory.
Since the purpose of the LKAS regulation would
be to add the provisions as the minimum
requirement to prevent the drivers’ confusion and
decreasing safety because of various kind of
LKAS available the market, “if fitted” is
acceptable.

## Slide 16: Discussion points in 74th GRRF
Q5. What is the schedule? (Is setup of the
informal meeting necessary?)
At the present, Japan doesn’t stick to setting up of
the Informal meeting.
In GRRF, the time is very limited for sufficient
discussion.
We would like to propose the ad-hoc meeting
between now and the next February, and based on
the result of the ad-hoc meeting, we would like to
consider the Informal meeting if necessary.
We would like to propose to hold the ad-hoc
meeting in November 2013 in Paris, Geneva or
Sweden.