## Slide 1: Introduction on CEL Annex issue
How the split of R13H was done:
the split of R13H creates a specific issue on CEL
OICA is seeking for guidance from GRRF
5. General requirements
EMC
PTI
Call for CEL …
Annex 8: CEL
Annex 9: ESC & BAS
5. General requirements
EMC
PTI
Call for CEL …
Annex 8: CEL
5. General requirements
EMC
PTI
ESC requirements from Annex 9…
[Call for CEL]
[Annex CEL]
5. General requirements
EMC
PTI
BAS requirements from Annex 9…
[Call for CEL]
[Annex CEL]
R13H
R13H - split
ESC
BAS
Informal document GRRF-75-39

## Slide 2: The issue
Existing R13H CEL fully covers braking system, ESC and BAS.
The CEL Annex cannot simply be duplicated in the new ESC and BAS regulations, while remaining in R13H, since it may create:
  duplication and additional workload to repeat CEL approval for ESC and BAS in both R13H and independent regulations
  conflicting interpretations of CEL requirements by different CPs / between each regulation
A smart solution has to be found to avoid these risks.
OICA is seeking for guidance from GRRF, on whether and how referring to CEL requirements in the independent new ESC and BAS regulations

## Slide 3: CEL Annex - Background
The purpose of the complex electronic control system requirements is to verify the basic braking system is not adversely affected by the complex electronic control systems, which override the basic braking system.
It is required to respect the basic performance prescribed by R13H under non-fault and fault conditions of the complex electronic control systems.
And fundamentally, this verification has to be completed by the braking regulation.
It is the same situation for steering systems.
Brake
actuator
ABS
…
Computer(s)
Sensors
ESC
B
A
S
A
C
C
Brake
Brake pedal
= Primary control of braking
Complex electronic
control
systems
=
Complex controls of braking
B
asic braking
system
Override

## Slide 4: CEL Annex - Background
ESC and BAS are currently covered by R13H CEL Annex: description of the function of “the system”; layout and schematics; safety concept; verification and tests…
When splitting R13H, OICA intentions are to:
  Maintain the level of safety delivered today
  Avoid duplication and any additional workload to cover separate CEL approval’s for R13-H, ESC and BAS
  Avoid conflicting interpretations of CEL by CPs / between each regulation
  Avoid design restrictive requirements
OICA is seeking for guidance from GRRF, on whether and how referring to CEL requirements in the independent new ESC and BAS regulations
Brake
actuator
ABS
…
Computer(s)
Sensors
ESC
B
A
S
A
C
C
Brake
Brake pedal
= Primary control of braking
Complex electronic
control
systems
=
Complex controls of braking
B
asic braking
system
Override

## Slide 5: CEL Annex What are the options?
CEL Annex included in the Regulation Associated with the Basic Function:
Regulation 13
Regulation 13H
Regulation 79
Independent Regulation 1
Independent Regulation 2
Requirement linking the new Regulation to the parent Regulation for the base function
Requirement linking the new Regulation to the parent Regulation for the base function
Requirement in the new Regulation linking the CEL requirements to the parent Regulation for the basic function

## Slide 6: CEL Annex - Different options
Option 1: CEL present in each regulation
R13H, ESC and BAS regulations include and call CEL Annex, AND
  Option 1A
  ESC and BAS regulations propose two alternatives:
  1. Fulfilling CEL Annex, or
  2. the applicant demonstrates the Systems are already covered by R13H-CEL approval
Option 1B
Braking system, ESC and BAS regulations propose two alternatives:
  1. Fulfilling CEL Annex, or
  2. Functions or sub-systems being subject to CEL requirements may be demonstrated by CEL annex of another regulation.
Option 2: CEL present in R13H only
Only R13H includes and calls CEL Annex, AND
R13H CEL Annex covers all complex electronic control systems including ESC and BAS