## Slide 1
Proposal to Modify Homologation Brake Test Procedure to Improve Safety on Proving Ground 18/09/2013
Mr . Klaus Vosteen ATP Executive Director
Mr . Fran Martínez IDIADA Proving Ground Supervisor
Informal document GRRF-75-42
(75th GRRF, 17-19 February 2013,
agenda item 13(d))
Submitted by the experts from ATP and Idiada
Notes: <number>

## Slide 2
Index
Introduction
  ATP & IDIADA
  EPGSA
Homologation Brake Test Tracks
Standard Safety Regulations on High Speed Circuit
Accident Background
Accident Reconstruction
Recently Corrective Actions at IDIADA & ATP
Proposals to improve safety
Proposed modifications on Test Procedures

## Slide 3
Introduction
ATP Automotive Testing Papenburg
Applus IDIADA
Notes: <number>

## Slide 4
Introduction
EPGSA (www.EPGSA.eu)
  The European Proving Ground Safety Assoiciation EPGSA is a forum for the discussion of safety related items regarding vehicle testing.
  EPGSA was founded in 2002.
  It is not the intention of the organization to develop standards, but to collectively share possible solutions to safety related issues.
  It is a non-profit organization.
  The membership is limited to vehicle testing organizations with proving grounds.
Members:
  Arctic Falls (Sweden), ATP (Germany), Bosch (Germany), Bridgestone (Italy), Bruntingthorpe (UK), UTAC -CERAM (France), Continental (Germany), DEKRA (Germany), Ford (Belgium), GoodyearDunlop (France), Icemakers (Sweden), IDIADA (Spain), Jaguar/Land Rover (UK), Opel (Germany), Millbrook (UK), MIRA (UK), Nardo (Italy), Renault (France), Volvo (Sweden),
Notes: <number>

## Slide 5
Homologation Brake Test
ECE R13 (Heavy Vehicles)
ECE R13H (Passenger cars)
ECE R90 (Replacement brake linings)
Notes: <number>

## Slide 6
Homologation Brake Test Tracks
Straight Line Braking Surfaces
Notes: <number>

## Slide 7
Homologation Brake Test Tracks
High Speed Circuit (HSC):
Test usually performed on track
  Braking Test
  Engine Performance Test
  Coast Down
  Dynamic Test
  Durability Test
  …
Notes: <number>

## Slide 8
Preventive Measures:
Applus IDIADA
Standard Safety Regulations on High Speed Circuit
ATP Automotive Testing Papenburg
Notes: <number>

## Slide 9
Preventive Measures:
Standard Safety Regulations on High Speed Circuit
Identify the test vehicle with the appropriate identifying plate, for high speed braking and for changing lanes, on the rear side of your vehicle.
Identify the test vehicle with a flashing light placed on the roof, permanently switched on when performing Braking Test or Lane Changes
Switch on the hazard (emergency) lights in the moment you are performing the braking manoeuvre and switch off when you finish.
Keep a safety distance between vehicles when performing special tests:
  10 seconds between vehicles in ATP
  500 meters between vehicles in IDIADA
Only in ATP, no stopping for more than 30 seconds
Notes: <number>

## Slide 10
Accident Background IDIADA
Date: April 2006
Vehicle 1:
Type of test: Brake Test
Test Speed: from 120km/h to 0km/h
Vehicle 2:
Type of test: Durability
Test Speed: Acceleration Test
Causes of the accident:
The driver of the first car stopped at the second lane
The driver of the second car was distracted.
Consequences of the accident:
Hard crash between both cars.
Fatal injuries.

## Slide 11
Accident Background ATP
Date: July 2012
Vehicle 1:
Type of test: Durability Test
Test Speed: various
170 km/h at the moment of the accident
Vehicle 2:
Type of test: Durability Test
Test Speed: various
0 km/h at the moment of the accident
Causes of the accident:
The driver of the first car was probably distracted.
The driver of the second car was stopping without permission
Consequences of the accident:
Hard crash between both cars
Fatal injuries

## Slide 12
Accident Background IDIADA
Date: February 2013
Vehicle 1:
Type of test: Brake Test
Test Speed: from 100km/h to 0km/h
Vehicle 2:
Type of test: Confidential
Test Speed: constant speed 90km/h
Causes of the accident:
The driver of the first car probably don’t respect safety distance.
The driver of the second car was distracted.
Consequences of the accident:
Hard crash between both cars.
Slight human injuries.

## Slide 13
Accident Background IDIADA
Date: July 2013
Vehicle 1:
Type of test: Brake Test
Test Speed: from 100km/h to 0km/h
Vehicle 2:
Type of test: Confidential
Test Speed: constant speed 90km/h
Causes of the accident:
The driver of the first car probably don’t respect safety distance.
The driver of the second car was distracted.
Consequences of the accident:
Hard crash between both cars.
Serious human injuries (3 People involved)

## Slide 14
Accident Reconstruction
Notes: <number>

## Slide 15
Accident Reconstruction

## Slide 16
Accident Reconstruction

## Slide 17
Accident Background
Description of the problem
Performance tests at high decelerations (eg 1g) from high speeds to ZERO
Stopped vehicles at the High Speed Track with vehicles driving at high speed.
Fade tests that have to be performed at rigid periods of time (eg every 45 seconds), and if one stop fails or is aborted, the whole test including all the preparation and bedding of the samples is not valid and need to be repeated.
It makes the driver do not fulfil the safety regulations mainly the safety distance.
Notes: <number>

## Slide 18
Recently Corretive Actions at Idiada
Increase the quantity of Safety Cars in Proving Ground in order to reinforce the safety on test tracks
Improve the driver training
Timetables restrictions for Braking Test on high speed track
Extend the Braking Track.
Notes: <number>

## Slide 19
Recently Corrective Actions at ATP
Installation of a new Track Operation Mode
No brake testing with more than 5m/s² in standard track operation allowed.
No Stopping in standard track operation allowed.
Brake tests only in exclusive or special track operation.
All tests are to be coordinated by the Test- and Safety Coordinator
A Risk Assessment is mandatory

## Slide 20
Recently Corrective Actions at ATP
New Guard Rails installed
Asphalt Safety Lane on high speed oval
Collision Warning System mandatory for each vehicle on oval.
Installation of Gantry Signs

## Slide 21
Proposals to improve safety
Proposal for slight modifications on Brake Test Procedures
on High Speed Track:
Final test Speed ≥ 20 Km/h.
More flexibility on Fading Tests
Notes: Other actions would be:
<number>

## Slide 22
Proposed modifications on Test Procedures
Final test Speed ≥ 20 Km/h as for ECE R117 :

## Slide 23
Proposed modifications on Test Procedures
Final test Speed ≥ 20 Km/h as for ECE R117 :

## Slide 24
Proposed modifications on Test Procedures
Final test Speed ≥ 20 Km/h as for ECE R117 :

## Slide 25
Proposed modifications on Test Procedures
Final test Speed ≥ 20 Km/h as for ECE R117 :

## Slide 26
Proposed modifications on Test Procedures
Final test Speed ≥ 20 Km/h as for ECE R117 :

## Slide 27
Proposed modifications on Test Procedures
Final test Speed ≥ 20 Km/h as for ECE R117 :

## Slide 28
Proposed modifications on Test Procedures
More flexibility on Fading Tests :
We would like to propose a certain tolerance in the frequency and even more, a scape possibility, if during the 15 snubs, there is a need of extend some of the periods due to safety aspects, at discretion of the technical service, this might be compensated by one additional snub to ensure that the brakes have been sufficiently heated.

## Slide 29
For further information:
Mr . Klaus Vosteen T +494961975312
Klaus_Vosteen@ATP-Papenburg.de
Mr . Fran Martínez T +34 977 16 60 04
fmartinez@idiada.com
Thank you very much for your kind attention