## Slide 1
UN | Japan
Comparison of Rear Collision Standards
(UN Regulations and Japanese Safety Regulations)
UN Regulation No. 34
Safety Regulation No. 15
Velocity of collision: 35 – 38 km/h
Velocity of collision: 50+/- 2 km/h
(1) Applicability: Optional (at the request of the manufacturer)
(2) Vehicle categories: M, N, O
(3) Velocity of collision: 35 – 38 km/h
(1) Applicability: Mandatory
(2) Vehicle categories:
* M1 with GVW of 2.8 t or less
* N1 with GVW of 2.8 t or less
(3) Velocity of collision: 50 +/- 2 km/h
1,100 kg
1,100 kg
Proposal for the 03 series of amendments to Regulation No.34
(Fire prevention) (submitted by Japan)
Informal document GRSG-104-47
(104th GRSG, 15-19 April 2013
Agenda item 3)

## Slide 2
Survey Conditions
* Years of data: 2001-2006
Subject vehicles:
Ordinary & light passenger cars
Accident type:
Vehicle-to-vehicle rear-end collision
Subject accidents:
Accidents causing injury or death
Years of first registration:
Before & after rear-end collision
regulation tightening
* Number of vehicles: 1,196,686
Fire Incidence Rate of Rear-End Collisions (Japan)
After the tightening of the rear-end collision regulation (collision speed 35 km/h  50 km/h), the ﬁre incidence rate of rear-end collisions has reduced to about 1/3, indicating that the regulatory tightening is effective.
0.48
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1.0
Fire incidence rate of rear-end collisions
(No. of vehicles with fire incidence per 10,000 vehicles with accidents causing injury or death)
Before
tightening Collision speed 35 km/h
After
tightening Collision speed 50 km/h
0.14
Notes: <number>
<number>