## Slide 1: Transposition of GTR No.13 “Hydrogen and fuel cell vehicles” into UN Regulation
- Explanatory material -
20/September/2013 The European Commission and OICA
<number>
Informal document GRSP-54-01
(54th GRSP, 17 - 20 December 2013,
agenda item 20)
Notes: <number>

## Slide 2: Background
Global technical regulation No.13 on “Hydrogen and fuel cell vehicles” has been established on 27 June 2013 (ECE/TRANS/180/Add.13)
The European Commission made a statement at the 160th WP29:
  The European Commission, together with OICA, will lead transposition of the GTR into UN Regulation
  Once the UN Regulation is established, EU will adopt as an alternative to existing EU regulation
The editorial team (COM, OICA volunteers) developed the base draft of UN Regulation, with the considerations as shown in this material
<number>
Notes: <number>

## Slide 3: Principle
Transposition of GTR into UN Regulation  No additional technical requirement (in principle, correction & clarification may be required)
  Any addition of technical requirements should be discussed for phase 2 of GTR at the informal WG
  Non-safety related requirements should be developed by relevant bodies.
Minimum changes in existing Regulations
  If existing Regulations allows approval of vehicles satisfying GTR requirements, no amendment is required on such Regulations.
<number>
Notes: <number>

## Slide 4: Correlation between GTR and ECE
GTR requirements | Relevant ECE
5.1./6.2. Compressed hydrogen storage system | New ECE
5.2.1./6.1.3-6. In-use fuel system integrity | New ECE
5.2.2./6.1.1-2. Post-crash fuel system integrity | New ECE (see below)
5.3.1./6.3.1-4. Electrical safety requirements – in-use | R100 (slide #5)
5.3.2./6.3.5. Electrical safety requirements – post-crash | R12/R94/R95 (slide #6)
7.2./7.4. LHSS design qualification requirements | New ECE
7.3./7.5. LHSS fuel system integrity | New ECE
Existing crash test procedures are applied to post-crash fuel system integrity requirements  Use similar approach as REESS tests in R100-02
LHSS requirements are optional for CPs in GTR  LHSS requirements are included as separate Parts. If it will become an obstacle to establish a new ECE, LHSS requirements may be separated
<number>
Notes: <number>

## Slide 5: Electrical safety – in-use
Difference between R100-01 & HFCV-GTR
  Isolation resistance monitoring system
    HFCV-GTR(5.3.1.2.4.1.) – installation is mandatory
    R100-01 (5.2.3.8) – installation is optional
<number>
(with respect to in-use electric safety requirements)
GTR compliance will allow the approval under R100
No amendment to R100 is necessary
Conclusion
Notes: <number>

## Slide 6: Electrical safety – post-crash
Difference between R94-02 & HFCV-GTR (relevant requirements exist also in R12 and R95)
  Available compliance options
    GTR will not allow “low energy” option
<number>
No urgent amendment is necessary (Same for R12, R94 and R95)
Conclusion
No issue, if physical protection option is generally allowed
GTR compliance will allow the approval under ECE
Use of huge open-type battery for HFCV is not realistic
  Isolation resistance for combined DC- & AC-buses
    Combination with physical protection (GTR 5.3.2.2.2.2. (b)) does not exist in ECE
  Electrolyte leakage
    GTR does not have 5L limit for open-type batteries.
Notes: <number>

## Slide 7: Structure of Draft UN Regulation
<number>
Part I
Part II
Part III
Part IV
Part V
Part VI
Compressed Hydrogen Storage System
Assembly of components
Components
Vehicle
Liduefied Hydrogen Storage System
Notes: <number>

## Slide 8: Material Compatibility & Hydrogen embrittlement - Transitional provision -
<number>
GTR No.13 Part I
1. Material compatibility and hydrogen embrittlement
156. The SGS subgroup recognized the importance of requirements for material compatibility and hydrogen embrittlement and started the work in these items. Compliance with material qualification requirements ensures that manufacturers consistently use materials that are appropriately qualified for hydrogen storage service and that meet the design specifications of the manufacturers. However, due to time constraint and other policy and technical issues, agreement was not reached during Phase 1. Therefore, the SGS working group recommended that Contracting Parties continue using their national provisions on material compatibility and hydrogen embrittlement and recommended that requirements for these topics be deferred to Phase 2 of the gtr activity.
To accommodate this statement under the 58 Agreement, a transitional provision is proposed
EIF, Hydrogen ECE
2013
2014
Phase 2 discussion of HFCV-GTR
Est. of GTR on material compatibility
98 Agreement
58 Agreement
Continue national requirements
Existing requirements on material compatibility
Est. GTR No.13
Transposition
Notes: <number>

## Slide 9: Guide for draft document
<number>
Document is based on Part II of ECE/TRANS/180/Add.13 with following changes
  Delete provisions only related to electrical safety
  Add administrative provisions for type approval
  Re-arrange layout of provisions as typical UN Regulations (test procedures in Annex)
  Adjust paragraph numbers and cross references
  Correct errors in GTR text (Amendments to GTR for correction will be separately proposed)
In informal document, the changes from GTR contents are described in Red color (except for deletion of electrical part)
Comments are given where careful consideration may be necessary
Item numbers for Annex I, part 1 (information document) will be taken account for the future EU WVTA framework regulation
Notes: <number>