## Slide 1: Short Report Status of GTR No. 7/BioRID TEG
Bernd Lorenz (BASt)
For 54th GRSP 17th/20th December 2013
Geneva
Informal document GRSP-54-28
(54th GRSP, 17 - 20 December 2013,
agenda item 2)

## Slide 2
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
On the workshop in March 2013 a procedure for measuring effective head restraint height and backset based on the R-point without the use of the HRMD was explored and agreed (see next slides).
Aim of the July workshop was to define a procedure how to position the BioRID without the use of the HRMD.
The aim of the second day was to draft some new text mainly related to Annex 9 of the draft GTR.
As offered in the last official GTR 7 meeting held in April 2013 at OICA in Paris, OICA presented a proposal for a procedure for BioRID seating which served as a basis for the workshop.
Notes: <number>
<number>

## Slide 3
CP: contact point
IP: intersection point
Distance x: function of design torso angle
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Concept of measuring effective HR height
Notes: <number>
<number>

## Slide 4
Test procedure for effective head restraint height I
The Torso & Neck Link concept expressed in goniometric formulas
Source: GTR7-08-03e.pdf (Hans Ammerlaan, RDW)
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Notes: <number>
<number>

## Slide 5
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Source: GTR7-08-03e.pdf (Hans Ammerlaan, RDW)
Test procedure for effective head restraint height I
The Torso & Neck Link concept expressed in goniometric formulas
Notes: <number>
<number>

## Slide 6
Fotos: B. Lorenz
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Impressions I
Notes: <number>
<number>

## Slide 7
Fotos: B. Lorenz
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Impressions II
Notes: <number>
<number>

## Slide 8
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Difference between the static measurements and the dynamic test is the position of the seat.
A new „reference point“ is needed as basis for a similar procedure as agreed for the static one
-> Introduction of the „R50 point“
Notes: <number>
<number>

## Slide 9
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Introduction of the „R50 point“
Introduction of a new “designated H-point” for mid-size male seating position “R50”.
This data is provided by the manufacturer, allowing the seat to be adjusted to this point.
Note: static measurement is made in a different seat set-up than for the dynamic test.
“R50“tolerance is checked by the H-point machine. If it lies within the 50 mm box it is this is the designated design point.
Notes: <number>
<number>

## Slide 10
Annex 1 Head - Position Table
HEAD POSITION TABLE Location of the back-of-head of two designated males in automotive posture with respect to the R-point at several design torso angles, and their in-between “distance x” |  |  |  | 
Design torso angle | X-coordinate of back-of-head calculated for the mid-sized male | Z-coordinate of back-of-head calculated for the mid-sized male | X-coordinate of back-of-head calculated for large male 1 | “Distance x”: distance between X-coordinates of back-of-head of both males
 | 504.5*sin(design torso angle - 2.6)+71 | 504.5*cos(design torso angle - 2.6)+203 | 593*sin(design torso angle - 2.6)+76 | 88.5* sin(design torso angle- 2.6)+5
5 | 92 | 707 | 101 | 9
6 | 101 | 707 | 111 | 10
7 | 110 | 706 | 121 | 12
8 | 118 | 705 | 132 | 13
9 | 127 | 704 | 142 | 15
10 | 136 | 703 | 152 | 16
11 | 145 | 702 | 163 | 18
12 | 153 | 701 | 173 | 19
13 | 162 | 699 | 183 | 21
14 | 171 | 698 | 193 | 22
15 | 179 | 696 | 203 | 24
16 | 188 | 694 | 213 | 26
17 | 196 | 692 | 223 | 27
18 | 205 | 689 | 233 | 29
19 | 213 | 687 | 243 | 30
20 | 222 | 684 | 253 | 31
21 | 230 | 682 | 263 | 33
22 | 239 | 679 | 273 | 34
23 | 247 | 676 | 283 | 36
24 | 255 | 673 | 292 | 37
25 | 263 | 669 | 302 | 39
26 | 271 | 666 | 312 | 40
27 | 279 | 662 | 321 | 42
28 | 287 | 659 | 330 | 43
29 | 295 | 655 | 340 | 44
30 | 303 | 651 | 349 | 46
Notes: <number>
<number>

## Slide 11
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Introduction of the „R50 point“
The BioRID H-point is located 20 mm forward of the “R50 point”
Based on the “R50 point” Annex 1 table shall be applied which provides the target back of the head.
Based on the experience from the BioRID user group and current practice in NCAP subtract 15 mm from figure given for the backset taken from the Annex 1 table.
Note: The group was well aware that most experience with the BioRID in dynamic testing is based on 25 degrees design angle as used at IIHS and Euro NCAP.
However, JNCAP uses the BioRID for a range of design torso angles. Based on the available expert knowledge the group recommends to limit the use of the BioRID to torso angles between 20-30 degrees.
Notes: <number>
<number>

## Slide 12
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Issues discovered during the workshop
At 20 degree torso angle it seems not possible/difficult to meet the back of head and head level requirement at the same time. However, the introduction of a reasonable angle tolerance of the head might solve the problem.
The different definition of the pelvis angle in the draft gtr (torso angle plus 1.5 ± 2.5º ) and Euro NCAP (26.5º ± 2.5º), which gives the same value for 25º angle, was discussed.
-> JASIC will review JNCAP data to look at the issue of the BioRID pelvic angle and the head leveling
Notes: <number>
<number>

## Slide 13
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
As a result of the workshop the group recommends the following BioRID set up priority procedure:
1 – Verify H-point to R50, using SAE 3 H-point machine.
2 – Position BioRID checking in order of:
  BioRID H-point location forward +20mm
  Pelvis angle
  Back of head coordinate subtract -15mm.
  Level Head, if possible.
Notes: <number>
<number>

## Slide 14
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach
Further actions:
JASIC shall review JNCAP data to look at the issue of the BioRID pelvic angle and the head levelling which it was noted was a resultant of using BioRID at angles below 25 to 20 degrees and that this was an issue that would need to be addressed regardless of the BioRID set up procedure used.
OICA agreed to review specific wording in the text to provide improvements as noted in the dual pane document.
JASIC to provide information on using the torso design angle, using JNCAP information
During the workshop(s) the seat design angle was used for the static as well as for the dynamic procedure. It was the feeling of the group that a confirmation by the GTR group is needed that this was the correct way forward.
Notes: <number>
<number>

## Slide 15
Conclusion
Workshop was enjoyable, constructive and successful. All participants have been very supportive!
Concept based on the „R50 point“ worked for the positioning of the BioRID
New text for GTR Annex 9 proposed
-> HRMD no longer needed for static assessment and BioRID positioning!
GTR No. 7 Workshop on 16th of July 2013 @BASt, Bergisch Gladbach

## Slide 16
Issues to be solved / under discussion
Injury Criteria / Seat performance Criteria: proposals made by NHTSA, Japan, Chalmers/Folksam at the September Gothenburg meeting; cadaver testing and data analysis at VRTC ongoing (delayed due to governmental shut-down)
Certification procedure: current procedure does not discriminate between the dummies used during the R&R series (refurbished dummies)
Proposals for new/updated certification test made by Humanetics at the Gothenburg meeting (9th/10th September 2013) *)
*) Available for download on the UNECE GTR no. 7 website:
https://www2.unece.org/wiki/display/trans/GTR7+14th+Meeting

## Slide 17
Draft drawing package available on UNECE website http://www.unece.org/trans/main/wp29/wp29wgs/wp29grsp/gtr7phase2_3_drawing_package.html
Draft PADI available on UNECE website (TEGID-23)
Check list included in PADI to check for correct build level
Harmonization of Drawings (Humanetics)
All dummy specifications need to be included into UN Mutual Resolution No. 1 (M.R.1)
M.R.1: „Concerning the description and performance of test tools and devices necessary for the assessment of compliance of wheeled vehicles, equipment and parts according to the technical prescriptions specified in UN Regulations and UN Global Technical Regulations”
New way of defining test tools for regulation!
Link to M.R.1: http://www.unece.org/trans/main/wp29/wp29wgs/wp29gen/wp29resolutions.html

## Slide 18
New Certification Test – Mini Sled with Seat Back and with Head Restraint
Multi-segment full back support
• Base of spine can translate X and rotate Y
• Double teflon between dummy & sled to reduce friction
• Fairly stiff head restraint surface
• Same pendulum and energy transfer device
Source: GTR7-14-08, Humanetics

## Slide 19
New Test – Bumper Compression on Spine
Probably
An absolutely necessary test for maintaining dummy
Can be an inspection test to be done as part of maintenance rather than a certification test As long as mini-sled with back support proves to detect dummy differences adequately
Currently doing R&R testing to verify procedure works properly
Further work
Confirm R&R (within 1 lab and between labs)
Finish building parts for all vertabra locations
Collect test data Dummies 0054, 0068, 0077, 0100 from
Various bumper stiffnesses going into mini-sled with back support work
Establish corridors on R&R dummies (and/or similar bumpers)
Source: GTR7-14-08, Humanetics

## Slide 20
New Test – Jacket only Impact
Detailed study done on o4 R&R jackets
Excluding original R&R jackets that gave differences
Lab to lab variation testing R&R jackets
Checking practicality of production to corridors
Some possible sources of test variation
Conclusions reached and recommendations made for parameters, corridors and test improvements
Source: GTR7-14-08, Humanetics

## Slide 21
New Test – Pelvis Bottom
Detailed study done on
4 R&R pelvises, back and bottom
Excluding original R&R pelvises that gave differences
Lab to lab variation testing R&R pelvises
Checking practicality of production to corridors
oome possible sources of test variation
Conclusions reached and recommendations made for test to use, parameters, corridors and test improvements
Only bottom of pelvis test needed
Source: GTR7-14-08, Humanetics

## Slide 22
New Test – Pelvis Shape Check
Inspection test to make sure pelvis has not shrunk too much
Plate with 5 locations for each side
Measure pelvis offset with a steel ruler
  Rough check to catch gross deformations
  If we can eventually set limits, a go/no go gage could be used
Just starting to work with this
Need to test multiple old pelvises
Verify R&R is sufficient
Set corridors
Source: GTR7-14-08, Humanetics

## Slide 23
Thank you for your attention!
Bernd Lorenz
Bundesanstalt für Straßenwesen (BASt)
Brüderstraße 53
D-51427 Bergisch Gladbach
lorenz@bast.de