UN/SCETDG/46/INF.27

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 21 November 2014 Forty-sixth session Geneva, 1 – 9 December 2014 Item 2 (c) of the provisional agenda Recommendations made by the Sub-Committee on its forty-third, forty-fourth and forty-fifth sessions and pending issues: electric storage systems

Comments on ST/SG/AC.10/C.3/2014/101 – Consideration of what constitutes “Equipment”

Transmitted by PRBA – The Rechargeable Battery Association and RECHARGE, the European Association for Advanced Rechargeable Batteries

Introduction

1.	In ST/SG/AC.10/C.3/2014/101, IATA proposes to require a certain type of equipment known as “power packs” be classified as lithium ion batteries rather than lithium ion batteries contained in equipment. PRBA and RECHARGE believe power packs are lithium ion batteries contained in equipment and should not be classified as lithium ion batteries.

2.	Power packs are designed to recharge batteries inside various types of equipment such as mobile phones, tablets and notebooks. They do not provide a direct source of power for the equipment.

3.	Power packs are often comprised of batteries, plus charge-in/charge-out regulator circuit, connectors, fuel gauge, etc. In some cases the batteries contained in power packs also are used in other host articles such as cellular phones.  (See EXHIBIT 4 on page 5.)  Power packs also are generally shipped as consumer retail items that include a retail box with manual and accessories.  Pictures of these various articles associated with power packs are shown in EXHIBIT 5 on page 6.

4.	To be classified as lithium ion batteries, power packs would need to be tested in accordance with the UN Manual of Tests and Criteria. Power packs are generally not subjected to the UN testing scheme. Instead, the cell or battery inside the power pack is submitted separately for testing and then incorporated into the power pack after testing is completed. A picture of a stand-alone battery that has been subjected to UN testing and designed to power a power pack is shown in EXHIBITS 3 and 4 on pages 4 and 5.

5.	For the reasons noted above, PRBA and RECHARGE believe power packs should be classified and packaged in accordance with requirements associated with lithium ion batteries contained in equipment.

# Text boxes

Portable Charger

Fuel gauge button and indicators

Flexible power-out connector

EXHIBIT 1 - EXTERIOR

EXHIBIT 2 - INTERIOR

Device operation circuitry

Flexible power-out connector

Power-in connector

Battery Pack protection circuit and connector

Battery Pack

EXHIBIT 3 - INTERIOR WITH BATTERY REMOVED

Battery pack pocket

Battery Pack

(flip side from previous picture)

Battery: ~5.8 x 46 x 50 mm

Portable charger:

~10 x 56 x 109 mm

EXHIBIT 4 - COMPARISON WITH MOBILE PHONE REMOVED

Portable Charger

Mobile phone

Battery pack

Battery pack

Battery pack pocket

EXHIBIT 5 - Retail kit

Very similar to mobile phone or other device with rechargeable battery

(US quarter for scale)

Retail box

________________________

User guide

Portable Charger

Packaging

Power

supply