|  | United Nations | ST/SG/AC.10/C.4/2014/13 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 14 August 2014 Original: English and French |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Globally Harmonized
System of Classification and Labelling of Chemicals

Twenty-eight session

Geneva, 10 – 12 December 2014

Item 2 (a) of the provisional agenda

Classification criteria and related hazard communication:

Recommendations made by the Sub-Committee on its

twenty-fifth, twenty-sixth and twenty-seventh sessions

Draft amendments to the fifth revised edition of the Globally Harmonized System of Classification and Labelling of Chemicals (ST/SG/AC.10/30/Rev.5) adopted by the 
Sub-Committee at its twenty-fifth, twenty-sixth 
and twenty-seventh sessions

Note by the secretariat

Chapter 2.1

2.1.2.1 (f)	Replace “articles which contain only extremely insensitive substances or articles” by “articles which predominantly contain extremely insensitive substances or articles”

(Reference document: ST/SG/AC.10/C.4/52, Annex I)

Figure 2.1.3	Amend the figure by inserting a new box in the “No” line between the boxes that read “Would the hazard hinder fire-fighting in the immediate vicinity?” and “Are the hazardous effects outside the package”, as follows:

Figure 2.1.3: Procedure for assignment to a division in the class of explosives (Class 1 for transport)

1	See Chapter 3.3 of the UN Model Regulations on the Transport of Dangerous Goods, Model Regulations for details.”

(Reference document: ST/SG/AC.10/C.4/54, Annex)

2.1.4.2.2	Amend the first sentence to read as follows: “The acceptance procedure for the hazard class Explosives need not be applied if:”

(Reference document: ST/SG/AC.10/C.4/52, Annex I)

2.1.4.2.2 (c)	Amend to read as follows:

“(c) 	For an organic substance, or a homogenous mixture of organic substances, containing a chemical group (or groups) associated with explosive properties:

- 	the exothermic decomposition energy is less than 500 J/g, or

- 	the onset of exothermic decomposition is 500 ºC or above

as indicated by Table 2.1.3.

Table 2.1.3 DECISION TO APPLY THE ACCEPTANCE PROCEDURE FOR THE HAZARD CLASS EXPLOSIVES FOR AN ORGANIC SUBSTANCE OR A HOMOGENOUS MIXTURE OF ORGANIC SUBSTANCES

| Decomposition energy (J/g) | Decomposition onset temperature (°C) | Apply acceptance procedure? (Yes/No) |
| --- | --- | --- |
| < 500 | < 500 | No |
| < 500 | ≥ 500 | No |
| ≥ 500 | < 500 | Yes |
| ≥ 500 | ≥ 500 | No |

The exothermic decomposition energy may be determined using a suitable calorimetric technique (see section 20.3.3.3 of the UN Recommendations on the Transport of Dangerous Goods, Manual of Tests and Criteria); or”.

(Reference document: ST/SG/AC.10/C.4/52, Annex I)

Chapter 2.2

Amend the chapter title to read: “Flammable gases”

2.2.1	Renumber current paragraph 2.2.1.2 as 2.2.1.3. Insert a new paragraph 2.2.1.2 to read as follows:

“2.2.1.2	“A pyrophoric gas is a flammable gas that is liable to ignite spontaneously in air at a temperature of 54 ºC or below.”

(Reference document: ST/SG/AC.10/C.4/54, Annex)

2.2.2	Renumber current paragraph 2.2.2.2 as new 2.2.2.3 (current table 2.2.2 becomes table 2.2.3). Insert a new paragraph 2.2.2.2 to read as follows:

“2.2.2.2	A flammable gas is additionally classified as pyrophoric if it meets the criteria in the following table:

Table 2.2.2: Criteria for pyrophoric gases

| Category | Criteria |
| --- | --- |
| Pyrophoric gas | Flammable gases that ignite spontaneously in air at a temperature of 54 ºC or below. |

NOTE 1: Spontaneous ignition for pyrophoric gases is not always immediate, and there may be a delay.

NOTE 2: In the absence of data on its pyrophoricity, a flammable gas mixture should be classified as a pyrophoric gas if it contains more than 1% (by volume) of pyrophoric component(s).”.

(Reference document: ST/SG/AC.10/C.4/54, Annex)

2.2.3 	Renumber current paragraph before the table as 2.2.3.1. Amend current table 2.2.3 to read as follows:

“Table 2.2.4: Label elements for flammable gases

|  | Flammable gas | Additional sub-categories |
| --- | --- | --- |
|  |  | Pyrophoric gas | Chemically unstable gas |
|  | Category 1 | Category 2 | Pyrophoric gas | Category A | Category B |
| Symbol | Flame | No symbol | Flame | No additional symbol | No additional symbol |
| Signal word | Danger | Warning | Danger | No additional signal word | No additional signal word |
| Hazard statement | Extremely flammable gas | Flammable gas | May ignite spontaneously if exposed to air | May react explosively even in the absence of air | May react explosively even in the absence of air at elevated pressure and/or temperature |

Insert a new paragraph 2.2.3.2 to read as follows:

“2.2.3.2	If a flammable gas or gas mixture is additionally classified in one or more sub-categories, then all relevant classification(s) should be communicated on the safety data sheet as specified in Annex 4, and the relevant hazard communication elements included on the label.”

(Reference document: ST/SG/AC.10/C.4/54, Annex)

2.2.4.1	In decision logic 2.2 (a), insert two additional boxes with the text “Go to decision logics 2.2 (b) and 2.2 (c)” immediately to the right of the existing Category 1 and Category 2 boxes, as follows:

(Reference document: ST/SG/AC.10/C.4/54, Annex)

2.2.4.2	Insert a new paragraph 2.2.4.2 to read as follows:

“2.2.4.2	Decision logic for pyrophoric gases

To classify a flammable gas as a pyrophoric gas, data on its ability to ignite in air are required. The classification is according to decision logic 2.2 (b).

Decision logic 2.2 (b)

1  In the absence of data on its pyrophoricity, a flammable gas mixture should be classified as a pyrophoric gas if it contains more than 1% (by volume) of pyrophoric component(s).”

Current paragraph 2.2.4.2 becomes new paragraph 2.2.4.3 and current decision logic 2.2 (b) becomes decision logic 2.2 (c).

(Reference document: ST/SG/AC.10/C.4/54, Annex)

2.2.4.3	Current paragraphs 2.2.4.3 and 2.2.4.3.1 become new 2.2.4.4 and 2.2.4.4.1. Current paragraph 2.2.4.3.2 (“Chemical instability…classification purposes”) becomes new paragraph 2.2.4.4.4.

2.2.4.4.2 and 2.2.4.4.3	Insert two new paragraphs 2.2.4.4.2 and 2.2.4.4.3, to read as follows:

“2.2.4.4.2		Pyrophoricity should be determined at 54°C in accordance with either IEC 60079-20-1 ed1.0 (2010-01) “Explosive atmospheres – Part 20-1: Material characteristics for gas and vapour classification – Test methods and data” or DIN 51794 “Determining the ignition temperature of petroleum products”.

2.2.4.4.3	The classification procedure for pyrophoric gases need not be applied when experience in production or handling shows that the substance does not ignite spontaneously on coming into contact with air at a temperature of 54 ºC or below. Flammable gas mixtures, which have not been tested for pyrophoricity and contain more than one percent pyrophoric components, should be classified as a pyrophoric gas.  Expert judgement on the properties and physical hazards of pyrophoric gases and their mixtures should be used in assessing the need for classification of flammable gas mixtures containing one percent or less pyrophoric components.  In this case, testing need only be considered if expert judgement indicates a need for additional data to support the classification process.”.

(Reference document: ST/SG/AC.10/C.4/54, Annex)

Chapter 3.7

Table 3.7.1	In the heading, first column, replace “ingredients classified as” by “ingredient classified as”.

(Reference document: ST/SG/AC.10/C.4/54, Annex)

Chapter 3.8

3.8.3.4.6	Insert a new paragraph 3.8.3.4.6 as follows:

“3.8.3.4.6	In cases where the additivity approach is used for Category 3 ingredients, the “relevant ingredients” of a mixture are those which are present in concentrations ≥1% (w/w for solids, liquids, dusts, mists, and vapours and v/v for gases), unless there is a reason to suspect that an ingredient present at a concentration <1% is still relevant when classifying the mixture for respiratory tract irritation or narcotic effects.”

(Reference document: ST/SG/AC.10/C.4/54, Annex)

Chapter 3.10

3.10.3.3.1 to 3.10.3.3.2.3  	Amend to read as follows:

“3.10.3.3.1	The “relevant ingredients” of a mixture are those which are present in concentrations ≥ 1%.

3.10.3.3.2	Category 1

3.10.3.3.2.1	A mixture is classified as Category 1 when the sum of the concentrations of Category 1 ingredients is ≥ 10%, and the mixture has a kinematic viscosity ≤ 20.5 mm2/s, measured at 40°C.

3.10.3.3.2.2	In the case of a mixture which separates into two or more distinct layers, the entire mixture is classified as Category 1 if in any distinct layer the sum of the concentrations of Category 1 ingredients is ≥ 10%, and it has a kinematic viscosity ≤ 20.5 mm2/s, measured at 40°C.

3.10.3.3.3	Category 2

3.10.3.3.3.1	A mixture is classified as Category 2 when the sum of the concentrations of Category 2 ingredients is ≥ 10% and the mixture has a kinematic viscosity ≤ 14 mm2/s, measured at 40 °C.

3.10.3.3.3.2	In classifying mixtures in this category, the use of expert judgment that considers surface tension, water solubility, boiling point, volatility is critical and especially when Category 2 substances are mixed with water.

3.10.3.3.3.3	In the case of classifying a mixture which separates into two or more distinct layers, the entire mixture is classified as Category 2 if in any distinct layer the sum of the concentrations of Category 2 ingredients is ≥ 10%, and it has a kinematic viscosity ≤ 14 mm2/s, measured at 40°C.”.

(Reference document: ST/SG/AC.10/C.4/54, Annex)

Chapter 4.1

4.1.3.5.5.3 to 4.1.3.5.5.4 	insert the text “multiplied by their corresponding M factors” in the following paragraphs, as follows:

4.1.3.5.5.3.1:  	Second sentence after “ingredients”

4.1.3.5.5.3.2:  	Second sentence after “Acute 1”

4.1.3.5.5.3.3:  	Second sentence after “Acute 1”

4.1.3.5.5.4.1:  	Second sentence after “ingredients”

4.1.3.5.5.4.2:  	Second sentence after “Chronic 1”

4.1.3.5.5.4.3:  	Second sentence after “Chronic 1”

(Reference document: ST/SG/AC.10/C.4/54, Annex)

Annex 1

In Table A1.2:

Amend the title to read: “Flammable gases (see Chapter 2.2 for classification criteria)”.

In the hazard class column, amend the text in the column to read “Flammable gases”.

Insert a new row for pyrophoric gases, before the row for “A (chemically unstable gases)” as follows:

| Classification | Labelling | Hazard statement codes |
| --- | --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement |  |
|  |  | GHS | UN Model Regulationsa |  |  |  |
| Flammable gases | Pyrophoric gas |  |  | Danger | May ignite spontaneously if exposed to air | H232 |

(Reference document: ST/SG/AC.10/C.4/54, Annex)

Annex 3

Section 1, Table A3.1.1:

Insert a new row to read as follows:

| Code | Physical hazard statements | Hazard class (GHS chapter) | Hazard category |
| --- | --- | --- | --- |
| (1) | (2) | (3) | (4) |
| H232 | May ignite spontaneously if exposed to air | Flammable gases (chapter 2.2) | Pyrophoric gas |

For H230 and H231 amend the name of the hazard class in column (3) to read: “Flammable gases (Chapter 2.2)”

Section 2, Table A3.2.2:

For P222:

Insert a new row for the hazard class “Flammable gases (chapter 2.2)” (column 3) and hazard category “Pyrophoric gas” (column 4), with the same condition for use currently applicable to pyrophoric liquids and pyrophoric solids (column 5).

For P280:

Insert a new row for the hazard class “Flammable gases (chapter 2.2)” (column 3) and hazard category “Pyrophoric gas” (column 4).

Section 3, paragraph A3.3.5:

In the three tables for “Flammable gases (including chemically unstable gases) (chapter 2.2)”, amend the first line in the headings to read: “FLAMMABLE GASES”.

Add a new matrix applicable to pyrophoric gases as follows:

| FLAMMABLE GASES (Chapter 2.2) (Pyrophoric gases) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| Pyrophoric gas | Danger | H232 | May ignite spontaneously if exposed to air |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P222 Do not allow contact with air. – if emphasis of the hazard statement is deemed necessary. P280 Wear protective gloves/protective clothing/eye protection/face protection. Manufacturer/supplier or the competent authority to specify the appropriate type of equipment. |  |  |  |

Note: This table lists only precautionary statements that are assigned due to the pyrophoricity of the gas.  For the other precautionary statements, that are assigned based on the flammability, see the respective tables for flammable gases.”.

(Reference document: ST/SG/AC.10/C.4/54, Annex)

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2013-2014 approved by the Committee at its sixth session (see ST/SG/AC.10/40, para. 14, and ST/SG/AC.10/C.4/48, Annex IV).

# Text boxes

At 20 °C and a standard pressure of 101.3 kPa, does it:

(a)	ignite when in a mixture of 13% or less by volume in air?; or

(b)	have a flammable range with air of at least 12 percentage points regardless of the lower flammable limit?

Category 1

Danger

# Yes

No

Category 2

No symbol

Warning

Go to decision logics 2.2 (b) and 2.2 (c)

Go to decision logics 2.2 (b) and 2.2 (c)

Flammable gas or gas mixture

Does the flammable gas or gas mixture ignite spontaneously in air at a temperature of 54 ºC or below? 1

Yes

Pyrophoric gas

Danger