|  | United Nations | ECE/TRANS/WP.29/2014/23 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 18 December 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

162nd session

Geneva, 11-14 March 2014

Item 4.9.11 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 8 to the 01 series of amendments to Regulation No. 74 (Installation of lighting and light-signalling devices (mopeds))

Submitted by the Working Party on Lighting and Light-Signalling*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its seventieth session (ECE/TRANS/WP.29/GRE/70, para. 18). It is based on ECE/TRANS/WP.29/GRE/2013/56, as reproduced in Annex II to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Insert a new paragraph 2.5.14., to read:

"2.5.14. 	"Hazard warning signal" means the simultaneous operation of all of a vehicle's direction-indicator lamps to show that the vehicle temporarily constitutes a special danger to other road users;"

Paragraph 5.13., amend to read (footnote3 remains unchanged):

"5.13. 	Colours of the lights3

The colours of the lights referred to in this Regulation shall be as follows:

Driving beam headlamp: 			white

Passing beam headlamp: 			white

Front retro-reflector non triangular: 	white

Side retro-reflector, non-triangular:		amber at the front

amber or red at the rear

Pedal retro-reflector: 			amber

Rear retro-reflector, non-triangular:	red

Direction-indicator lamp: 			amber

Stop lamp: 					red

Rear position lamp:				red

Rear-registration plate lamp: 		white

Vehicle-hazard warning signal:		amber"

Insert a new paragraph 5.15.5., to read:

"5.15.5. 	Vehicle-hazard warning signal (paragraph 6.12.)"

Insert new paragraphs 6.12. to 6.12.4., to read:

"6.12.	Vehicle-hazard warning signal

6.12.1.	The signal shall be given by simultaneous operation of the direction-indicator lamps in accordance with the requirements of paragraph 6.8. above.

6.12.2.	Electrical connections

The signal shall be given by means of a separate control enabling all the direction-indicators to be supplied with current simultaneously.

6.12.3.	"Circuit-closed" tell-tale

Mandatory flashing red signal lamp or, in the case of separate tell-tales, the simultaneous operation of the tell-tale prescribed in paragraph 6.8.11.

6.12.4.	Other requirements

Light flashing 90 ± 30 times per minute.

Operation of the lamp-signal control shall be followed within not more than one second by the appearance of the light and within not more than one-and-a-half seconds by the first extinction of the light."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.