## Slide 1
GRB, 59th session
27-29 January, 2014
Informal document GRB-59-08
(59th GRB, 27-29 January 2014,
agenda item 6)
Method of Deceleration Measuring and Data Processing
for Tyre Rolling Resistance Determination.
Testing and Evaluation of the variant method using the dω/dt form.
The report of the ad-hoc working group organized in accordance with the recommendation of the 58th GRB session (ECE/TRANS/WP.29/GRB/56, para. 15)
(France)
(Russian Federation)
<number>
Notes: <number>

## Slide 2
The fragment of the report of the Working Party on Noise on its 58th session (ECE/TRANS/WP.29/GRB/56)
Regulation No. 117 (Tyre rolling noise and wet grip adhesion) (agenda item 6)
15.The expert from the Russian Federation made a presentation (GRB-58-12) to introduce a revised proposal (ECE/TRANS/WP.29/GRB/2013/10) that would introduce a "Deceleration Calculator" software for the deceleration test method in the test procedure for measuring rolling resistance. The expert from France informed GRB that the proposed calculator had been verified for a first cycle of tests by the Technical Union for the Automobile, Motorcycle and Cycle Industries (UTAC). However, he added that the method should be still thoroughly analyzed. The expert from the Russian Federation recalled that full cooperation was offered by the Russian experts as well as data sharing and asked GRB to take into consideration the positive experience developed by the industrial sector of his country in this field. The expert from France proposed to host a meeting of experts (date to be defined) in UTAC to further the exchange of views and finalize the proposal. Finally, GRB endorsed the ad hoc meeting with the experts of ETRTO and the Russian Federation which was proposed by the expert from France to test the proposed "Deceleration Calculator". It was also noted that once that the calculator was accepted by GRB as a valid alternative to the current one, it could be hosted on the WP.29 website, as an example, with an anonymous reference.
<number>

## Slide 3: The ad-hoc working group participants:
France (UTAC):
Serge Ficheux,
Thierry Ageron,
Celine Berthou,
Marc-Antoine Scorianz.
The Russian Federation (NAMI):
Vladimir Petrushov,
Evgeny Redkin.
ETRTO:
Jean-Claude Noirhomme,
Georges Dimitri.
<number>

## Slide 4: The work of the ad-hoc group included the following:
1. Evaluation of the theoretical justification of the method used in the variant method using the dω/dt form , its algorithm of data processing and particularly method of solving equation system, as well as statistical assessment of the method;
2. Experimental assessment of the method on one example of rolling resistance determination of the class C1 tyre on specialized test machine MTS and on test machine not specially designated for these measurements;
3. Consideration experimental data, obtained on tyres by NAMI prior to this measuring campaign on class C2 and C3 tyres in 2013 by this method.
<number>

## Slide 5
In the alternative calculation method a function “distance-time“ α=f(t) is used. Deceleration is the second derivative of that function. There is no need to measure/calculate speed. This increases accuracy of the method.
(3) Absolutely accurate transformation:
(A)
(B)
α,
j
<number>
So it is enough to record in discrete form function αi=f(t) then approximate it by formula (A) and take a result in form of (B).
This is simple. This is accurate. σ<0.03% , R2 >0.999.
(2) Approximation:
(1) Obtaining experimental data
DETERMINATION OF DECELERATION BY USING DIFFERENTIAL ∂ω/∂t FORM
t
Notes: <number>

## Slide 6: Installation of NAMI-357 data logger on MTS test machine in UTAC (“S” – drum sensor).
Sуr
S
<number>
Notes: <number>

## Slide 7: Tyre sensor “S” of NAMI-357 data logger.
S
<number>

## Slide 8: HAWITEC test machine in UTAC on which NAMI-357 data logger was used
<number>

## Slide 9: “Deceleration Calculator” windows
<number>
* Loaded test data file:
Notes: <number>

## Slide 10
<number>
Table 1. Deceleration j at 80 km/h and different speed range. Test machine UTAC1, Tyre 205/55R16, p=0,21 MPa, Lm=482,6daN, RT=0,3045 m, IT =0,97kgm2, Measuring device NAMI-357. Data processing by the “Deceleration Calculator”.
Table 2. NAMI-357 – UTAC-MTS j data comparison at 80 km/h
Test № | j, s-2 |  | ∆, %
 | NAMI | UTAC | 
1 | 0.0470 | 0.0462 | -1,70
2 | 0.0470 | 0.0462 | -1,70
3 | 0.0469 | 0.0461 | -1,71
Average | 0.0469 (±0.00%) | 0.0462 (±0.00%) | -1,70
Speed range | 82-78 km/h | 82-79 km/h | -
Note: the comparison of parasitic losses as cause of ∆ value was not executed.

## Slide 11
<number>
Note: in NAMI calculation moments of inertia determined by UTAC system were used. Average values are given with limit of their confidence intervals at the confidence level of 95 %, expressed in percent of the average.
Table 3. NAMI-357 – UTAC-MTS Cr data comparison- results obtained on the same machine (UTAC-MTS)

## Slide 12
<number>
UTAC

## Slide 13: UTAC-MTS ISO 28580 Roiling Resistance Deceleration Repeatability
Radial Force |  |  |  |  | N | 4824 |  |  | 
Inflation Pressure |  |  |  |  | N | 210 |  |  | 
Test Number | Test Date |  |  |  | Test | Cond1 | Cond2 | Average | Average
 |  |  |  |  |  | 80 km/h | 0 km/h |  | 
 |  |  |  |  |  | Frr | Frr | Frr | Cr
 |  |  |  |  |  | N | N | N | N/kN
1 | Nov-20-2013 |  |  |  | a | 36.231 |  |  | 7.510
2 | Nov-20-2013 |  |  |  | b | 36.245 |  |  | 7.513
3 | Nov-20-2013 |  |  |  | c | 36.268 |  |  | 7.517
Average |  |  |  |  | N | 36.248 |  |  | 7.513
Standard Deviation |  |  |  |  | N | 0.019 |  |  | 0.004
 |  |  |  |  |  |  |  |  | 0.05%
S.D. Spec |  | 0.050 |  | N |  | Meets Spec |  |  | 
<number>

## Slide 14
<number>
Table 8-b. Parasitic losses of the machine HAWITEC - drum R=0.8500 m, Id = 573kgm2 (deceleration j at 80 km/h and different speed range)
Table 8-a. Deceleration j at 80 kph and different speed range (Test machine UTAC-HAWITEC fitted with NAMI system)
Note: δ - deviation relatively basic range: for drum without tyre from Test № 1;for skim test from Test № 4.

## Slide 15
<number>
Table 9. NAMI-357 – fitted on UTAC-HAWITEC Cr data comparison with UTAC results on UTAC-MTS machine and system.
Note 1: δ - deviation relatively basic range;
∆ - discrepancy between NAMI HAWITEC and UTAC MTS data.
Note 2: these results are obtained in the supposition that total inertia of test Machine HAWITEC equals to 573 kg-m2

## Slide 16: NAMI-354 test machine with device NAMI-357
<number>

## Slide 17
<number>
Table 10. Deceleration j at 80 km/h and different speed ranges
(the test machine NAMI-354)
Notes: <number>

## Slide 18: The equipment NAMI-357 on the test machine IPZ-4 at the Nizhnekamsk Tyre Plant
<number>

## Slide 19
<number>
Table 12. Deceleration j at 80km/h and different speed range.
Tyre class C3. (The test machine IPZ-4)

## Slide 20: Conclusions
Testing of the “Deceleration Calculator” executed using two tyre test machines of UTAC had shown:
Good adaptability of the mentioned computer program as well as logger NAMI-357 to the tyre test machines.
The comparison of test data had shown satisfactory fit of deceleration data obtained by the both systems UTAC and NAMI on MTS machine. Taking into account the difference between the methods of parasitic losses and rolling radius determination obtained discrepancy of deceleration approximately of 1.7% may be estimated as high.
The obtained data presented by NAMI had shown that the algorithm of the “Deceleration Calculator” practically provides independence of measured deceleration from test speed range in span from 4 to 20 km/h.
<number>

## Slide 21: Conclusions (continued)
UTAC was successful to program the solution of the equation system presented by NAMI, with one of the module of the currently used software “SAS”. The statistic assessment of this solution in comparison with the results obtained by the “Deceleration Calculator” had shown good closeness of agreement.
Even though only one C1 reference tyre had been tested during this study, for the present time it may be presumed that the test results on C2 and C3 tyres presented by NAMI may be repeated using such test machines as MTS, but this would need to be considered in future on the base of mutual testing. It has to be noted that data characterizing C2 and C3 class tyres had been obtained by NAMI Nizhnekamsktyre plant on their machines with satisfactory accuracy using not specialized test machines. Common experiments using a test machine not specialized for rolling resistance, but for load and speed measurements, shown a low reproducibility, which needs to be investigated further, including finalizing spindle mechanical system diagnostics.
<number>

## Slide 22: Conclusions (end)
On the basis on the obtained test results the ad-hoc working group proposes the introduction of those amendments for clarifications and to adopt the proposal by the Russian Federation for Annex 6 – Appendix 4 to UN Regulation No. 117 for measurements and data processing for deceleration value obtaining in differential form dω/dt as presented in the document amending document ECE/TRANS/WP.29/GRB/2013/10.
<number>

## Slide 23: Thank you for your attention!
<number>