## Slide 1
59th GRB
(28-30 January 2014)
JASIC
Japan proposal for
Flat Front Light N1 Vehicle
<number>
Flat Front Light N1 Vehicle: | GVM ≤ 2.5 ton PMR (power to mass ratio) of GVM ≤ 35kW/t Engine capacity ≤ 660cc d value<1,100mm
Japan’s proposal is already included into the informal document “GRB-59-04” submitted by the GRB Expert Group on R51.
Informal document GRB-59-09
(59th GRB, 28-30 January 2014,
agenda item 3 (b))
Notes: <number>

## Slide 2
“Light Motor Vehicle” consists of “Light N1 Vehicle” and “Light M1 Vehicle”.
“Light N1 Vehicle” consists of “Flat Front type” and “Front Engine type”.
This proposal from Japan is only for “Flat Front type” of Light N1 Vehicle.
Front Engine type
Light N1 Vehicles
FOR BASIC UNDERSTANDINGS
Light M1 Vehicles
<number>
PMR of GVM > 35kW/t
Flat Front type
PMR of GVM ≤ 35kW/t
&
d value<1,100mm
Light Motor Vehicles
(GVM≤2.5ton, Engine capacity ≤ 660cc, etc)
Notes: <number>

## Slide 3
FOR BASIC UNDERSTANDINGS (additional)
<number>
6.2.2.1
Veh.Cat | Vehicles used for the carriage of goods | Phase1 | Phase2 | Phase3*/
M1 | PMR ≤ 120kW/t | 72 | 70 | 68
 | ・・・ | ・・・ | ・・・ | ・・・
・・・ | ・・・ | ・・・ | ・・・ | ・・・
Veh.Cat | Vehicles used for the carriage of goods | Phase1 | Phase2 | Phase3*/
N1 | GVW ≤ 2.5t | 72 | 71 | 69
 | GVW > 2.5t | 74 | 73 | 71
・・・ | ・・・ | ・・・ | ・・・ | ・・・
Light M1 Vehicles
Front Engine type
(=PMR of GVM > 35kW/t)
Flat Front type
(=PMR of GVM ≤ 35kW/t &
d value<1100mm)
Japan’s proposal
Light Motor Vehicles
(GVM≤2.5ton, Engine capacity ≤ 660cc, etc)
Light N1 Vehicles
Japan’s proposal is already included into the informal document “GRB-59-04” submitted by the GRB Expert Group on R51.
Notes: <number>

## Slide 4
<number>
CONTENTS
Japanese Regulations for Light N1 Vehicles
Bed size (loading space)
Usage of the Flat Front Light N1 Vehicles
Sales of Light N1 Vehicles in Japan
Noise Levels of Flat Front Light N1 Vehicles under R51-03 Test Method
Characteristics of Flat Front Light N1 Vehicles
Reasons Why the Noise Level of Flat Front Light N1 Vehicles is High
Data of Flat Front Light N1 Vehicle
Example of the vehicle similar to Flat Front Light N1 Vehicle sold in Europe
The situation of conformity to the UN/EU Regulations of Flat Front N1 Vehicle
Maximum speed of Flat Front Light N1 Vehicle
Exhaust emission of Flat Front Light N1 Vehicle (compare with EURO5)
The past sales of Light Motor Vehicles in Europe
The case of sales to Europe by using the chassis of Japanese Light Motor Vehicle in the past

## Slide 5
Length ≤ 3.40m, Width ≤ 1.48m, Height ≤ 2.00m
(1) Exterior dimensions
1. Japanese Regulations for Light N1 Vehicles
Light N1 Vehicle is defined as follows.
Max
1.48m
Max
3.40m
Max
2.00m
<number>
[Enforcement Regulations for Road Vehicles Act]
Article 2 Attached Table 1

## Slide 6
Engine capacity ≤ 660cc
(2) Engine capacity
(3) Maximum loading capacity (payload)
Maximum loading capacity ≤ 350kg
(4) Maximum seating capacity
Maximum seating capacity ≤ 4persons
1. Japanese Regulations for Light N1 Vehicle
(5) bed size (loading space)
bed size ≥ 0.6m2
[Light Motor Vehicle Inspection Activity Regulations]
3-3-67
[Examination Standards for New Type Vehicle]
Annex 2-26-3
[Classification of Use of Motor Vehicles, etc.]
4-1-3
[Enforcement Regulations for Road Vehicles Act]
Article 2 Attached Table 1
<number>

## Slide 7
2. Bed size (loading space)
Bed size example of Flat Front Light N1 vehicle
L1920mm x W1410mm ; 2.7m2
1.475m
1.41m
Japanese regulation requires that bed size of Light N1 Vehicles is 0.6m2 or more.
There is no regulations stipulating the maximum bed size, while in practice it is as close as possible to the exterior dimensions of the vehicle.
<number>

## Slide 8
3. Usage of the Flat Front Light N1 Vehicles
48% of Flat Front Light N1 Vehicles are used in agricultural area only.
64% of Flat Front Light N1 Vehicles are driven near such area (farm or factory), far from urban area.
In farm
(48%)
In factory
(16%)
Delivery
for business
(16%)
Others
Shopping
Leisure
(20%)
Investigated by JAMA at 2011
n=617
64%
Driven near farm and factory area, far from urban area
<number>

## Slide 9
3. Usage of the Flat Front Light N1 Vehicles
Investigated by JAMA at 2011
0
20
40
60
80
100%
Flat Front
Light N1
Vehicle
no use
several times
/year
1 time or more
/month
1 time or more
/week
Counts of usage on highway
n=791
n=289
0
20
40
60
80
100%
Flat Front
Light N1
Vehicle
over 50km
30 - 50km
10 - 30km
under 10km
The mileage in one run
N1Truck
except Light Motor Vehicle
n=789
n=289
Most users of Flat Front Light N1 Vehicles use the vehicle within their neighborhood only, not for long-distance travel.
Most users of Flat Front Light N1 Vehicles do not use the vehicle on highway, because it is hardly possible to run at about 100km/h.
<number>
N1Truck
except Light Motor Vehicle

## Slide 10
4. Sales of Light N1 Vehicles in Japan
The number of sales of Flat Front Light N1 Vehicles is only about 15% of the total sales of Light Motor Vehicles.
N1
M1
1,585,400
(80.1%)
PMR≤35
304,400
(15.4%)
1,979,400
The number of
Light Motor Vehicle
sales in 2012
PMR(GVM)>35
89,600 (4.5%)
<number>

## Slide 11
<number>
Light N1 (Flat Front)
Light N1 (Front Engine Type)
M1-derived N1 (Front Engine Type)
Trucks with GVM > 2.5 t (Flat Front)
R51-03 dB(A)
3000
2500
2000
1500
1000
500
0
Vehicle mass at R51-03 test (kg)
5. Noise Levels of Flat Front Light N1 Vehicles in the New Test (R51-03)
78
76
74
72
70
68
66
64
The noise levels of Flat Front Light N1Vehicles are higher than those of Front Engine Type by about 2 – 3 dB and are almost the same as trucks with GVM > 2.5 t.
2 – 3 dB
Notes: <number>

## Slide 12
Flat Front type
Front Engine type
N1 truck (GVM > 2.5 t)
Light N1 Vehicle
(GVM≤2.5t)
Different type
Same type
Flat Front Vehicle
(Engine under the seat)
Flat Front Light N1 vehicles are configured differently from Front Engine type vehicles (so-called M1-derived N1 vehicles) and have the same configuration as N1 vehicles (trucks) with GVM > 2.5 t.
6. Characteristics of Flat Front Light N1 Vehicles
engine
engine
engine
<number>
Notes: <number>

## Slide 13
<number>
Front Engine type
(M1-derived N1)
Flat Front type
(commercial N1)
d value
In Flat Front type vehicles, differently from Front Engine type vehicles, the engine and front tyre are located below the occupant to ensure large cargo space. Therefore, d value, which expresses the positional relation between occupant and front tyre can be used to classify these two vehicles.
6. Characteristics of Flat Front Light N1 Vehicles
d value: Horizontal distance between the front axle and the driver’s seat R-point
Notes: <number>

## Slide 14
<number>
-Comparison of d Values Between Flat Front type and Front Engine type Vehicles-
In Front Engine type vehicles, since it is necessary to install the steering wheel, pedals, etc. between front wheel and driver’s seat, their d values need to be at least 1,100 mm even in small vehicles.
In Flat Front type vehicles, to ensure large cargo space, it is necessary to locate the driver’s seat as forward as possible, i.e., above the engine and front wheel. Thus, their d values are no more than 1,100 mm.
d value (mm)
Overall length (m)
200
400
600
800
1000
1200
1400
1600
3.0
3.5
4.0
4.5
5.0
5.5
d value = 1,100
Light Motor vehicles
Smart 2
iQ
Flat Front type
Front Engine type
Flat Front type and Front Engine type vehicles can be separated at d value 1,100 mm.
6. Characteristics of Flat Front Light N1 Vehicles
Notes: <number>

## Slide 15
<number>
-Status of Categorization Based on the d Value and PMR (GVM)-
PMR (GVM)
15
20
25
30
35
40
45
50
55
0
200
400
600
800
1000
1200
1400
d value (mm)
d value = 1,100
PMR = 35
Bongo
(PMR < 35)
Front Engine Light N1
European small M1 &
M1-derived N1
Town Ace
Flat Front Light N1
Using the d value < 1,100 mm and PMR (GVM)  35, most Flat Front light N1 vehicles can be separated from other N1 vehicles.
6. Characteristics of Flat Front Light N1 Vehicles
660cc < Engine Capacity
Notes: <number>

## Slide 16
Since engines of Flat Front Light N1 vehicles are exposed, the engine radiated sound and air intake sound are emitted directly outside the vehicle. As a result, the vehicle external noise level and the engine sound contribution of Flat Front Light N1 Vehicles are higher than those of Front Engine type vehicles.
7. Reasons Why the Noise Level of Flat Front Light N1 Vehicles is High
Front Engine
type
Flat Front
Light N1 vehicle
Engine
Air intake sound
Exhaust sound
Tire
Contribution of each sound source of the vehicle external noise in average vehicles (amount of energy)
<number>
Sound emission in R51-03 test
Overall level 72 - 73 dB
Overall level about 70 dB
Notes: <number>

## Slide 17
Gear ratio comparison in 5-speed transmission cars(Light M1 vs. Flat Front Light N1)
Flat Front Light N1 Vehicle is required driving force at low speed, considering the usage environments such as load capacity (high load), high gradient, muddy ground, etc.
These situations demand higher gear ratio than M1 vehicle, as a result, Flat Front Light N1 Vehicles run with extra high engine speed making louder engine noise.
Flat Front Light N1 Vehicle
Light M1 Vehicle
<number>
over all gear ratio
5
10
15
20
25
4th
2nd
3rd
1st
5th
2nd
4th
3rd
1st
5th
(i) th gear ratio of M1 is same as (i+1) th of Flat Front Light N1 Vehicle.
7. Reasons Why the Noise Level of Flat Front Light N1 Vehicles is High

## Slide 18
8. Data of Flat Front Light N1 Vehicle
Items |  | Regulation for Light Motor Vehicle |  | Piaggio Porter* | 
 |  |  | Flat Front Light N1 Vehicle |  | 
 |  |  |  | PI engine | CI engine
Vehicle length | mm | ≤ 3400 | 3395 | 3390 | 3390
Vehicle width | mm | ≤ 1480 | 1475 | 1395 | 1395
Vehicle height | mm | ≤ 2000 | 1735 - 1905 | 1730 | 1730
Bed size | m2 | ≥ 0.6 | 2.53 - 2.7 | 2.5 | 2.5
Bed size length | mm |  | 1700 - 1940 | 1760 | 1760
Bed size width | mm |  | 1240 - 1415 | 1270 | 1270
Bed size height | mm |  | 235 - 1235 | ? | ?
Wheel base | mm |  | 1900 - 2450 | 1810 | 1810
Axle track | mm |  | 1290 - 1310 | 1210 | 1210
Number of seats | - | ≤ 4 | 2 - 4 | 2 | 2
Payload | kg | ≤ 350 | 350 | 550 - 700 | 550 - 700
GVM | kg |  | 1140 - 1510 | 1500 | 1500
Engine capacity | cc | ≤ 660 | 656 - 658 | 1300 | 1200
Max power | kw |  | 33 - 37 | 52 | 47
Max torque | Nm |  | 59 - 63 | 105 | 140
Max speed | Km/h |  | 104 - 107 | 130 | 130
Number of sales | '2012 |  | 304,400 | 4,400 | 
Price | € |  | 4,300 - | 10,800 - | 
Flat Front Light N1 Vehicle does not meet the preference of European market, given that the vehicle’s performance such as payload, maximum speed, etc, are limited.
* Piaggio Porter does not meet the Light Motor Vehicle regulation in Japan.
<number>

## Slide 19
9. Example of the vehicle similar to Flat Front Light N1 Vehicle sold in Europe
Piaggio Porter
From internet homepage
<number>

## Slide 20
Regulation | Conformity | Reasons
Emission levels R15 | No | The maximum speed of the test procedure is 120 km/h. But, Flat Front Light N1 Vehicle cannot trace this speed. So, running with wide open throttle is required.
Air-conditioning system EEC2006/40/EC | No | New air-conditioning system is necessary.
10. The situation of conformity to the UN/EU Regulations of Flat Front N1 Vehicle
Pole side impact performance | No | The informal document was submitted in the last GRSP (2013.12). The document will be discussed in next GRSP (2014.5). The requirements are as follows. [13X]00series test vehicle speed is below; 32 +/- 1km/h (vehicle width >1500mm) 26 -0/+6 km/h (vehicle width ≤1500mm) [13X]01series test vehicle speed is 32 +/- 1km/h In case that 01series becomes mandatory, Light N1 Vehicle cannot comply with 01 series due to narrow space between frame and seats.
Flat Front Light N1 Vehicle can not be sold in Europe since it is not adaptable to many regulations.
Future Regulation
The following countermeasures are necessary, if Flat Front Light N1 Vehicle shall comply with European requirements..
・Install drastically changed cooling system etc. for running at higher maximum speed.
・Develop a completely new air conditioner system.
・No countermeasures to comply pole side impact regulation with 01 series due to narrow space between frame and seats.
<number>

## Slide 21
Names of Flat Front Light N1 Vehicles | Engine power "S" rpm | Over all gear ratio | Diameter of tire (mm) | Maximum speed (km/h)
SUZUKI CARRY | 37kw/5700rpm | 5.625 (5th:1.000, final:5.625) | 550mm (145R12) | 105
DAIHATSU HI-JET | 37kW/5700rpm | 5.586 (5th:0.838, final:6.666) | 550mm (145R12) | 106
HONDA ACTY | 33kW/5500rpm | 5.364 (5th:0.861, final:6.230) | 550mm (145R12) | 104
MITSUBISHI MINICAB | 35kW/6000rpm | 5.842 (5th:0.852, final:6.857) | 550mm (145R12) | 107
11. Maximum speed of Flat Front Light N1 Vehicles
Maximum speed calculated with "S" rpm and over all gear ratio
"S" : Rated rotational engine speed at maximum power
Flat Front Light N1 Vehicles have very high gear ratio aiming at usage in farm area. As a result, the maximum speed of the vehicle is about 105km/h.
The lower maximum speed makes great influence to the exhaust emission test result and utility on highway.
<number>
Notes: <number>

## Slide 22
12. Exhaust emission of Light N1 Vehicles (compared with EURO5)
mode test |  |  |  |  |  | 
(g/km) |  | CO | THC | NMHC | NOx | PM
EURO5b (NEDC) | N1 ≤ 1305kg | 1.000 | 0.100 | 0.068 | 0.060 | 0.0045
 | N1 1306 - 1760kg | 1.810 | 0.130 | 0.090 | 0.075 | 0.0045
Japan (JC08) |  | 4.02 | - | 0.05 | 0.05 | 0.005
Idling test |  | 
 | CO(%) | HC (ppm)
EURO5 | 0.3 | －
Japan | 2.0 | 500
Note: Since the test mode is not the same, a simple comparison is not possible.
mode test |  |  |  |  | 
(g/km) | CO | THC | NMHC | NOx | PM
Flat Front Light N1 Vehicle (JC08) | 1.05 - 1.15 | － | 0.025 - 0.05 | 0.025 - 0.05 | －
Idling test |  | 
 | CO (%) | HC (ppm)
Light N1 Vehicle | 0.2 - 0.3 | 200 - 300
Range of measured values of Flat Front Light N1 Vehicle
<number>
Limit Value (PI engine)
0 200 400 600 800 1000 1200
0 200 400 600 800 1000 1200
Time (second)
Time (second)
Europe (NEDC)
Japan (JC08)
Vehicle speed (km/h)
Vehicle speed (km/h)
120km/h
100
100
Light N1 Vehicle is adjusted to emission regulations for four-wheel vehicles in Japan, however, it it is very difficult to conform Light N1 Vehicles to EURO5 (exhaust emission), because Light N1 Vehicles cannot run at 120km/h. Therefore wide open throttle which causes severe condition in the exhaust emission test is required during running the test cycle .

## Slide 23
13. The past sales of Light Motor Vehicle in Europe
<number>
Light Motor Vehicle is not sold and the type approval has not been granted in Europe so far, because of utility, sales-ability, etc.
The vehicle with maximum speed of about 105km/h does not fit to Europe traffic flow, so Light N1 Vehicle will not be sold in Europe.

## Slide 24
Daihatsu Cuore 989cc M1
(Name at Japan : Mira)
Sales year: 2007 - 2012
End of sales
14. The case of sales to Europe by using the chassis of Japanese Light Motor Vehicle in the past
Suzuki Super Carry 970cc N1
Sales year: 1986 - 1993
End of sales
It was necessary to improve the vehicle performance in order to sell in Europe, so engine capacity was modified from 660cc to 1000cc.
<number>

## Slide 25
<number>
Summary
With regard to the sub-category and limit values for Flat Front Light N1 vehicles, we propose the following:
6.2.2.1
6.2.2.2.6 For vehicle types of category N1 having a maximum technically permissible laden mass of less than or equal to 2.5 tons, a PMR of GVW of less than or equal to 35 kW/t and a horizontal distance “d” between the front axle and the driver’s seat R-point of less than 1100 mm, the limits of the vehicle types of category N1 having a maximum technically permissible laden mass above 2.5 tons apply.
・・・ | ・・・ | ・・・ | ・・・ | ・・・
Veh.Cat | Vehicles used for the carriage of goods | Phase1 | Phase2 | Phase3*/
N1 | GVW≤2.5t | 72 | 71 | 69
 | GVW>2.5t | 74 | 73 | 71
・・・ | ・・・ | ・・・ | ・・・ | ・・・
6.2.2.1 (same as the above)
6.2.2.1.5 For vehicle types of category N1 having a maximum technically permissible laden mass of less than or equal to 2.5 tons, the engine capacity not exceeding 660 cc and the power-to-mass ratio (PMR) calculated by using the maximum technically permissible laden mass not exceeding 35kW/t and a horizontal distance "d" between the front axle and the driver's seat R point of less than 1100 mm, the limits of the vehicle types of category N1 having a maximum technically permissible laden mass above 2.5 tons apply
(excerpt from GRB-58-17-Rev.1)
(excerpt from GRB-59-04 )
Japan’s proposal is already included into the informal document “GRB-59-04” submitted by the GRB Expert Group on R51.
Notes: <number>

## Slide 26
END
<number>