## Slide 1: Quiet road surfaces
Eurocities - working group noise
Chair: Henk Wolfert
Transmitted by the expert from the Netherlands
Informal document GRB-60-04-Add.1
(60th GRB, 1-3 September 2014,
agenda item 10)

## Slide 2: Source distribution
 | Rolling noise (%) | Propulsion noise (%)
Car @ 25 km/h | 50 | 50
Car @ 70 km/h | 90 | 10
Truck @ 25 km/h | 20 | 80
Truck @ 70 km/h | 50 | 50
In urban areas cars dominate vehicle fleet
In urban driving rolling dominates overall noise production
> 80% of total environmental noise produced is rolling noise

## Slide 3: Road surface type explains most of observed pass-by level difference

## Slide 4: Rolling noise = road Χ tyre
Tyre tread profile X road surface texture excite tyre structure
Vibrating tyre structure radiates noise
Rolling noise propagates over road surface (but also propulsion noise)
Road surface type is decisive for ambient noise level

## Slide 5: Road surface effect (rel. to DAC 0/16): cars between 40 and 70 km/h

## Slide 6: Aspects of Quiet Road Surface Application in cities
Magnitude of reduction
  Depends of traffic speed
  Depends on traffic composition
Wear and durability
  Free flowing or stop & go traffic
  Straight driving or turning
  Winter maintenance
Costs vs. Benefits

## Slide 7: Durability in N, SE and SF
Trials in Finland and Norway not successful
  service life <3 yr.
  >4 dB level increase in 1 yr.

## Slide 8: Durability in mainland Europe
Trials partly successful
  Very open wear quickly, especially at crossings
  Partly open wear moderate (after 8 yrs still 50% functioning)
  ≈ 4dB loss after 7 yrs.

## Slide 9: Evaluation of reduction effect
Takes into account :
  Aging of reference surface
  More frequent re-surfacing
  Average over several cycles

## Slide 10: Cost & benefits
Costs of noise reducing road surfaces often higher than conventional road surfaces
  Cost of construction is higher
  Lifetime is less
  More maintenance necessary
Cost/benefit ratio still better than other noise reducing measures like façade insulation and noise barriers

## Slide 11: Smooth road surfaces amplifies low noise tyre effect

## Slide 12: Conclusion
Low noise road surfaces valuable measure to reduce traffic noise
In general positive C/B ratio
Application shall be engineered with knowledge of limitations
Win-Win with other noise reducing strategies; especially low noise tyres

## Slide 13: Application for highways
Will be presented next GRB
By Wiebe Albers, chair of CEDR noise working group