## Slide 1
INTERNATIONAL ORGANIZATION OF MOTOR VEHICLE MANUFACTURERS
Assessment on the
Minimum Sound Level of the Horn
60th GRB Working Party on Noise
September 2014
Informal document GRB-60-16
(60th GRB, 1-3 September 2014,
agenda item 2)
Transmitted by the expert from OICA

## Slide 2
Review of Regulatory Situation in Countries that do not apply ECE R28

## Slide 3
SAE Assessment on typical Horn Level of US Vehicles
More than 60% of the tested vehicles have sound values for the horn below 93 dB(A).
85
89
93
97
101
105
109
113
115
ECE R28 Requirement
US Vehicles

## Slide 4
Recalculation of Korean Horn Requirement
Distance Correction:
The sound levels attenuates by -3 to -6dB per doubling of the distance. This means that measuring in 7 m distance the sound level is approximately -5.8 dB more quiet compared to a measurement in 2 m distance.
Filter Correction:
Applying an A-Filter instead a C- Filter will result in slightly higher sound level of approximately + 1.6 dB.
Result:
LKorea(ECE R28 conform) = 90 dB -5.8 dB + 1.6 dB = 85.8 dB
Korea
Level: 90 dB(C)
Distance: 2.0 m
ECE R28
Level: 93 dB(A)
Distance: 7.0 m

## Slide 5
Conclusions from the Review of other Regulations
There is no country that requires higher sound levels compared to ECE R28.
Most countries require only that a horn is installed.
Some countries require that the horn is audible in a certain distance „under normal conditions of traffic“, but no country provides a test method for this requirement.
An assessment of SAE for the US market indicates that the typical horn level of US vehicles is between 88dB and 95dB, with 60% of the vehicles under 93 dB horn level.
It is concluded that a minimum sound level of 87 dB(A) for the vehicles a specified in paragraph xxx of ECE R28 provides a sufficient level of safety.